FORM FOR SUBMITTING SUPPLIER’S QUOTATION

(This Form must be submitted only using the Supplier’s Official Letterhead/Stationery)

We, the undersigned, hereby offer to supply the items listed below in conformity with the technical specifications and requirements of UNDP as per RFQ Reference No. RFQ/056/18.

| Item # | Item Description | Unit of Measure | Q-ty | Price in [CURRENCY] (exclusive of VAT) |
| --- | --- | --- | --- | --- |
|  | Provide details of required items LOT 1 |  |  | Unit Price | Total Price |
| 1 | New office unit on the basis of 40-foot sea container. 1) Floor Base construction: • welded steel profile of cold rolled steel 3 mm thick • the bearing transverse floor beams are made of Ω - (omega) profiles, s = 2.5 mm • The distance from the bottom of the container is 100 mm (for installation of a heater and drain pipes) Insulation: • basalt wool 100 mm thick (density 16-24 kg / m³) • A flammability group A - not combustible; • smoke formation Q1 - faint smoke Floor: Wood chipboard, thickness 20mm, waterproof (V100); Wood chipboard complies to E1 emission indicator (wording according to DIBt 100 Directive dated June 1994); 1,5mm thick PVC flooring soldered at the joints; inflammability degree В1 – fire-resistant; smoke generation Q1 – low blanketing; 2) Ceiling Frame construction: • welded steel profile of cold rolled steel 3 mm thick • transverse load-bearing wooden beams 100 x 40 mm • The frame is attached to the container walls 130 mm from the roof of the container Insulation: • between the roof of the container and the ceiling • basalt wool with a thickness of 130 mm (density 16-24 kg / m³) • group of flammability: A - not combustible; • smoke formation Q1 - faint smoke Ceiling panel (fixed to the frame): • laminated chipboard (V 20), thickness 10 mm, • finish - white • Wood chipboard corresponds to the emission indicator E1 3) Outer walls Wall thickness - 175 mm Outer skin – Container wall Frame – Joists and planks 50х165 mm, frame with longitudinals after each 200 mm Insulation: 165mm thick continuous basalt fiber (density 16-24 kg/m3) inflammability degree: A – noninflammable; smoke generation Q1 – low blanketing Interior furnishing: laminated wood chipboard (V 20), thickness 10 mm, interior decoration – light oak finish Wood chipboard complies to E1 emission indicator 4) Poling Poling thickness - 70 mm Carcass - Joists and planks 50х100 mm, frame with longitudinals after each 200 mm Insulation: 50 mm thick continuous basalt fiber (density 16-24 kg/m3) inflammability degree: A – noninflammable; smoke generation Q1 – low blanketing Two sided trimming: laminated wood chipboard (V 20), thickness 10 mm, interior decoration – light oak finish Wood chipboard complies to E1 emission indicator Disposition – between the living room and tambour, between the kitchen and tambour 5) Doors External door: • left or right, wooden, opens outwards • double-sided cladding: galvanized steel sheet - inside; Cut out a piece of the outer wall to install the door - the outer side; • insulation of basalt wool with a thickness of 130 mm (density 16-24 kg / m3) • Steel door frame with perimeter seal • Mortise lock • external dimensions: 1850 x 1000 mm • Number of doors - 1 pc. Internal doors: from the living room to the tambour, from the kitchen to the tambour Left or right sided, wooden, opening to the tambour Two sided covering with laminated paper board Steel/wooden door frame with perimeter weather strip Outer dimension: 1850 x 700 мм Quantity of doors - 2 pcs. 6) Windows Window type 1: • PVC with double-glazed windows from 3 windows, open inwards • shutters one or two-leaved, on hinges, from a piece of the external wall, cut out for the device of windows solid, lockable on the inside • the color of the shutters according to the color of the outside of the container • swing-and-tilt mechanism • dimensions: 1100 x 900 mm • Accommodation - kitchen - 1 piece; living room - 2 pcs. • Quantity of windows - 3 pcs. The window in the living room at the end wall is designed as a reserve exit. " emergency exit " and installs a device for quick and easy opening of the window. Window type 2: • PVC with double-glazed windows of 3 windows • single-leafed shutters, on hinges, from a piece of the outer wall, cut out for the device of windows, lockable on the inside • the color of the shutters according to the color of the outside of the container • swing-and-tilt mechanism • dimensions: 300 x 500 mm • placement - a vestibule in the wall opposite the front door and kitchen in the wall opposite the window type 1 • Quantity of windows - 2 pcs. 7) Ventilation Natural ventilation through a pipe with a diameter of 100 mm, the length according to the thickness of the wall, with a grid and outer cover. Disposition - in a living room in the middle of a wall with windows between windows in 50 mm from the ceiling; In the tambour at the entrance door in 50 mm from the ceiling; In the kitchen between the door and the type 1 window in 50 mm from the ceiling. Quantity-3 pcs. 8) Furniture Living room: • 3 bunk beds with a frame made of painted metal profile with overlaid panels of laminated chipboard and chipboard sheets under mattresses, with drawers under the chipboard sheets: accommodation - 1 bed size 1800x800 mm, at the end wall, 2 beds 2000х800 mm in size against the wall opposite the windows; • Cabinets for documents, devices between beds 500x600x2000mm (up to the ceiling) from laminated chipboard. Above and below the cabinets are offices with doors, one shelf inside, a height of 500 mm. The average open part of cabinets 1000 mm high is equipped with two shelves. Number of cabinets - 2 pcs. • Folding tables under the windows of laminated chipboard length 1000, width 500 mm - 2 pcs .; • stools - 4 legs and connection of legs from the painted metal profile, seat from laminated chipboard, 4 pcs .; • metal hanger for clothes on the partition; • the color of all furniture is white Tambour: Metal hanger for outer garments on the poling with the living room, with length of 1000 mm. Quantity-1 pcs. Under the hanger a shelf for shoes with width of 1000 mm, depth 300 mm, and height 400 mm is installed. At a height of 200 mm from the floor an extra shelf is installed. Across the width the shelf is divided into 3 compartments of 320 mm. These dividers at the same time reinforce the top and an extra shelf. Shelf is made of laminated woodchip board. The back side of the shelf is covered by laminated paper board. Rack stack from laminated woodchip board on the poling with the kitchen, size of: width 1200 mm, height 2000 mm, depth 400 mm, 3 shelves are installed after 480 mm, shelves are divided by the width in to 3 compartments of 380 mm. Color of all the furniture in tambour is white Kitchen: Kitchen cupboard 500x600x2000mm (ceiling-high) from laminated woodchip board. The top and bottom of the cabinets are made of compartments with doors, with one shelf inside of height 500 mm. Middle open part of the cabinets of height 1000 mm is equipped with two shelves. The cabinets are installed in 2 corners of the kitchen in front of the wall with the type 1 window. Quantity of cabinets - 2 pcs. Kitchen cupboard from laminated woodchip board of height 900 mm, width 700 mm, length 600 mm. The upper part of the cupboard - working surface for cooking, 2 large drawers made under it, under the drawers two door wings, and in this space 1 shelf is installed. Cupboard is installed at the poling between the door to the tambour and high wardrobe, 1 pcs. Table for installation of two-burner electrical range. Table of width 700 mm, length 600 mm, height 900 mm. Part of the table lid is covered with Duralumin sheet of size 600 x 400 mm for mounting electrical range. The table is installed at the end wall between the door to the utility unit and a high wardrobe. Folding table under the window from laminated woodchip board of length 1000, width 500 mm - 1 pcs.; Box from laminated woodchip board for vegetables of the size 1800x450x450. The box is closed at the top by two hinged lids hinged with dimensions of 900x480 mm. Lids are used as a seats, fit with cotton or other soft material, which is covered with a leatherette or a similar material. Box is installed next to the wall between two tall wardrobes. Folding table from laminated woodchip board with narrow lid 200 x 600 mm on 4 legs, table height 730 mm. On two long sides two hinged lids of size 600 x 600 mm are attached. If necessary to open the table, side covers, one or both, are raised and fixed with a split leg each, attached also on hinges to the motionless legs. Stools-4 legs and legs joint from painted metal shape, seat from laminated woodchip board, 4 pcs.; Color of all the furniture in tambour is white. 9) Heating Performed by electric oil heaters, which are purchased separately and are not included into these specifications. 10) Electrical part Wiring – Hidden, copper wire, in gofer, implemented in compliance with the requirements of Electrical Installation Code. Technical description: voltage 220/400 V, 50 Hz Kitchen: Dome light for energy-saving lamp on the ceiling center; the lights switch on the poling; double electrical outlet on the poling; and single outlet with a grounding contact on the end wall above the table for electrical range. Tambour: Dome light for energy-saving lamp on the ceiling center; double outlet on the poling with kitchen; lights switch on the outer wall near to entrance door. Outer dome light switch on the outer wall next to the entrance door, distribution switchboard complete set with four automatic circuit breakers of 16 amperes on the wall opposite the entrance door at a height of 1600 mm. Power supply cable for distribution switchboard comes out near the outer door, on the end special weatherproof outlet Living room: 2 dome lights for energy-saving lamps on the ceiling at the room axis line; 1 double outlet on the poling; 2 single outlets with grounding contact on the outer wall between the windows and between the window and the door; lights switch on the poling near to door. Outer wall, facade – hermetic dome light above the entrance door Electrical grounding (earthing): Is done by d=16mm grid made electrodes, that are self-outlined with No.40 steel tape by electric arc welding; Earthing wire, galvanized, with cruciform clamp; Office unit earthing is conducted at the mounting location with providing of 4-6 Ohm resistance. Electric wiring – Fully installed and hooked up. 11) Thermal protection Floor: s = 90 mm U= 0,54 W/m² K Roof: s = 130 mm U= 0,37 W/m² K Walls: s = 165 mm U= 0,59 W/m² K Poling: s = 50 mm U= 0,59 W/m² K Windows: s = 4/16/4 mm U= 2,40 W/m² K 12) Loading capacity Floor loading: maximum allowable load - 2,0 kN/m² (200 kg/m²) Snow load: maximum allowable load - 1,0 kN/m² (100 kg/m²) Wind loading: 25 m/s (90 km/h) | pics | 1 |  |  |

| LOT 2: Buildings based on LSTK (light steel thin-walled structures) for the organization of a cordon for the inspection of a protected natural area. Number of storeys - 1 Height - 2,7 m The total area is 37.9 sq.m | Pcs | 3 |  |  |
| --- | --- | --- | --- | --- |
| Сonstruction |
| 1 | Building materials and constructions | sq.m. | 37,9 |  |  |
| 2 | Main frame designs from profiles | kg | 1662,0 |  |  |
| 3 | Additional elements (corners, anchors, washers, sealing tape, roofing screws, etc.) |  | 8% |  |  |
| 4 | Hardware (fasteners) | Pcs | 1600,0 |  |  |
| 5 | Galvanized steel profile ПШ-45 | m.p. | 115,0 |  |  |
| 6 | OSB-3 for exterior wall cladding | sq.m. | 93,0 |  |  |
| 7 | Wallboard gypsum plasterboard | sq.m. | 114,0 |  |  |
| 8 | Wallboard moisture-proof gypsum board | sq.m. | 114,0 |  |  |
| 9 | Drywall, moisture resistant | sq.m. | 36,0 |  |  |
| 10 | Self-tapping screws for fixing plasterboard | kg | 10,0 |  |  |
| 11 | ГКЛ profiles ППН28х27 0,4мм | m.p. | 45,0 |  |  |
| 12 | ГКЛ profiles ППС60х27 0,4мм | m.p. | 54,0 |  |  |
| 13 | ГКЛ profiles ПН50х40 0,5мм | m.p. | 105,0 |  |  |
| 14 | ГКЛ profiles ПС50х50 0,5мм | m.p. | 165,0 |  |  |
| 15 | Thermal insulation URSA GLASSWOOL P-15 (plates) | sq.m. | 503,3 |  |  |
| 16 | Heater URSA GEO M-11-Light | sq.m. | 50,4 |  |  |
| 17 | The membrane of the wind - waterproof | roll | 3,0 |  |  |
| 18 | Membrane of vapor barrier | roll | 2,0 |  |  |
| 19 | Profiled sheeting on the roof of HC35-0.7 mm | m.p. | 62,0 |  |  |
| 20 | Roofing accessories |  |  |  |  |
| 21 | Profiled flooring NS35-0.7 mm | sq.m. | 37,0 |  |  |
| 23 | Frame from the channel 16 for the base of the house | kg | 525,4 |  |  |
| 24 | Piles of reinforced concrete | pics | 9,0 |  |  |
| 25 | Screed with a thickness of 50mm thermozone in bags | pics | 23,0 |  |  |
| 26 | Laminate flooring | sq.m. | 45,0 |  |  |
| 27 | Internal finishing putty + water emulsion | sq.m. | 150,0 |  |  |
| 28 | External finish liquid plaster for travertine | sq.m. | 93,0 |  |  |
| 29 | Windows IMZO external 1,0х1,5 | pics | 2 |  |  |
| 30 | Windows IMZO external 1,0х0,5 | pics | 2 |  |  |
| 31 | Inside doors | pics | 2 |  |  |
| 32 | External door | pics | 1 |  |  |
| 33 | Gas bottle + cooker with two burners | pics | 1 |  |  |
| 34 | Electric wiring + switches + sockets | set |  |  |  |
| 35 | Furnishings |  | according to technical requirements |  |  |
| Column foundation |
| 36 | Building materials and constructions | sq.m. | 37,9 |  |  |
| 37 | Frame from the channel 16 for the base of the house | kg | 511,2 |  |  |
| 38 | Racks of metal pipes with a diameter of 150mm 1 = 4mm | Kg | 192,0 |  |  |
| 39 | Concrete M150 | м3 | 1,5 |  |  |
| 40 |  |  | Approximate dimensions(m) |  |  |
| 41 | External door | 1 | 210х1 |  |  |
| 42 | Internal door (interior) | 2 | 210х1 |  |  |
| 43 | Outside window | 2 | 1х1.5 |  |  |
| 44 | Ventilation window (fraimous) | 2 | 1х0.5 |  |  |
| 45 | Bunk bed | 2 | 2Х1 |  |  |
| 46 | Closet wardrobe | 1 | 1х0.7х2 |  |  |
| 47 | Dining table | 1 | 1.2х0.6х75 |  |  |
| 48 | Metal chair | 4 | 0.4х0.4х0.45 |  |  |
|  | Total Prices of Goods |  |
|  | Transportation costs |  |
|  | Packing, Insurance and other costs |  |
|  | Installation |  |
|  | Total All-Inclusive Bid Price |  |

| UNDP Requirements | Bidder’s Response |
| --- | --- |
| Validity of Offer: 60 days In exceptional circumstances, UNDP may request the Offeror to extend the validity of the Quotation beyond what has been initially indicated in this RFQ. In such case the extension shall be confirmed in writing, without any modification whatsoever of the Quotation. | ☐ Yes ☐ No ☐ Please explain in case of “No”: _____________________ |
| Warranty Period Offered (as applicable): not less than 12 months | ☐ Yes ☐ No ☐ Please explain in case of “No”: _____________________ |
| Description of Warranty Coverage (as applicable): Standard manufacturer’s Warranty | ☐ Yes ☐ No ☐ Please explain in case of “No”: _____________________ |
| Description of After Sales Service (as applicable): Warranty on Parts and Labor for minimum period of 12 moths Technical Support Provision of Service Unit when pulled out for maintenance/ repair Others: exchange for new similar product on any item if found not in operation after delivery by Vendor | ☐ Yes ☐ No ☐ Please explain in case of “No”: _____________________ |
| Delivery Terms (linked to INCOTERMS 2010): ☐ FCA ☐ CPT ☐ CIP DAP places of installation as state below Other: DDP places of installation as state below /customs cleared in the territory of the Republic of Uzbekistan Customs clearance, if needed, shall be done by UNDP | ☐ Yes ☐ No ☐ Please explain in case of “No”: _____________________ |
| Payment Terms: Payment to local Vendors (legal address in Uzbekistan): in UZS: 15% advance payment after signing the contract by both parties and 85% final payment upon delivery and acceptance of goods by UNDP. For foreign Vendors, in US Dollars (registered outside of Uzbekistan): 100% payment after delivery and acceptance of goods by UNDP. | ☐ Yes ☐ No ☐ Please explain in case of “No”: _____________________ |
| Delivery terms: As soon as possible but not more than 30 calendar days from the day of receipt of advance payment by Vendor “Turnkey” delivery of Office unit should include: transportation to the place of installation and the setup Attention: If the delivery period, stated in the quotation exceeds the delivery period stated above, the respective offer may be declined. Exact Address/es of Delivery and Installation locations: Lot 1 - Uzbekistan, Tashkent region, Bostanlyk district, Pskem river, Karabulak settlement latitude 41.746021 longitude 70.155153 Lot 2, Site 1- Uzbekistan, Tashkent region, Parkent district, about 5 km from the village of Sanginek, Suvashkan (41.2195280, 69.8522460) Lot 2, Site 2 - Uzbekistan, Tashkent region, Parkent district, about 18 km from the city of Krasnogorsk, Kengkutan (41.1421900; 69.8337240). Lot 2, Site 3 - Uzbekistan, Tashkent region, Bostanlyk district, r. Chatkal. (41.555242; 70.1116034) | ☐ Yes ☐ No ☐ Please explain in case of “No”: _____________________ |
| All documentations, including catalogs, instructions and operating manuals, shall be in: English ☐ French ☐ Spanish Others: Russian | ☐ Yes ☐ No ☐ Please explain in case of “No”: _____________________ |
| Liquidated Damages: ☐ Will not be imposed Will be imposed under the following conditions: Percentage of contract price per day of delay: 0.5% of total contract price for each day of delay up to a maximum 10% of the contract amount, along with subsequent termination of the contract without right to reimburse incurred expenditures. Max. no. of days of delay: 20 calendar days. After which UNDP may terminate the contract. | ☐ Accept ☐ Does not accept ☐ Please explain in case of “Does not accept”: |
| Please confirm that your company is not included in the UN Security Council 1267/1989 list, UN Procurement Division List or other UN Ineligibility List; | ☐ Not listed ☐ Listed ☐ Please explain in case of “Listed”: |
| Please confirm that you accept the UN Supplier Code of Conduct, available at https://www.un.org/Depts/ptd/about-us/un-supplier-code-conduct | ☐ Accept ☐ Does not accept ☐ Please explain in case of “Does not accept”: |
| Offeror’s Legal Name [insert Bidder’s legal name] |
| Legal Address in the Country of Registration: [insert Bidder’s legal address in country of registration] |
| Offeror’s Authorized Representative Information Name: [insert Authorized Representative’s name] Address: [insert Authorized Representative’s Address] Telephone/Fax numbers: [insert Authorized Representative’s telephone/fax numbers] Email Address: [insert Authorized Representative’s email address] |

[Name and Signature of the Supplier’s Authorized Person]

[Designation]

[Date]

Must be linked to INCO Terms chosen.