Reconstruction and ground and horticultural arrangements of existing terrace

GTC - Skopje

BILL OF QUANTITIES

|  |  | DESCRIPTION OF POSITION | UOM | QTY | Single price | Total price |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 1 | PREPARATORY ACTIVITIES |  |  |  |  |  |  |
|  |  | Demounting existing hydro-isolation, with transportation to a landfill |  |  |  |  |  |  |
|  | 1.1 |  | m2 | 1,560 |  | 0.00 |  |  |
|  |  | Demounting existing top siphon, with transportation to a landfill |  |  |  |  |  |  |
|  | 1.2 |  | No. | 6 |  | 0.00 |  |  |
|  |  | Demounting an existing lighting set, placed on a parapet wall |  |  |  |  |  |  |
|  | 1.3 |  | m | 152 |  | 0.00 |  |  |
|  | 1.4 | Fine cleaning and water-washing of surface | m2 | 1,560 |  | 0.00 |  |  |
|  |  | TOTAL: |  |  |  | 0.00 |  |  |
|  | 2 | ISOLATION ACTIVITIES |  |  |  |  |  |  |
|  |  | Purchase, transportation and building in PVC foil, at |  |  |  |  |  |  |
|  |  | d=2mm, welded with hot air, placed between two Geotextile units |  |  |  |  |  |  |
|  | 2.1 |  | m2 | 2050 |  | 0.00 |  |  |
|  |  | Purchase, transportation and mounting of GEOTEXTILE, 300 |  |  |  |  |  |  |
|  | 2.2 | g/m2 | m2 | 4100 |  | 0.00 |  |  |
|  | 2.3 | Purchase, transportation and placement of closing PVC battens on the building parapet chains, using fill of permanent flexible kit | m | 520 |  | 0.00 |  |  |
|  |  | Purchase, transportation and placement of a drain HL69 |  |  |  |  |  |  |
|  | 2.4 | above an existing drain | No. | 7 |  | 0.00 |  |  |
|  |  | Processing of penetration items through a hydro-isolation – ventilations and alike |  |  |  |  |  |  |
|  | 2.5 |  | No. | 10 |  | 0.00 |  |  |
|  |  | Protective coverage of hydro-isolation with a cover d=5cm |  |  |  |  |  |  |
|  | 2.6 |  | m2 | 1,560 |  | 0.00 |  |  |
|  |  | Parts envisaged as pedestrian zones between basin B1 and existing building, as per drawing submitted as annex |  |  |  |  |  |  |
|  | 2.7 |  | m2 | 734 |  | 0.00 |  |  |
|  |  | TOTAL: |  |  |  | 0.00 |  |  |
|  | 3 | CONSTRUCTION – CRAFT WORKS |  |  |  |  |  |  |
|  | 3.1 | Arrangement of a catering facility – COFFEE BAR |  |  |  |  |  |  |
|  |  | Mounting of steel construction made of box-shape steel profiles, as per annexed project and specification of |  |  |  |  |  |  |
|  |  | materials |  |  |  |  |  |  |
|  | 3.1.1 |  | kg | 4,104 |  | 0.00 |  |  |
|  |  | Construction of outside walls made of SIPOREX blocks, at |  |  |  |  |  |  |
|  |  | d=20cm, blocks at dimension 60x50x20cm, fastened with |  |  |  |  |  |  |
|  | 3.1.2 | appropriate glue, as per the project | m2 | 97.79 |  | 0.00 |  |  |
|  |  | Placement of bedding foundation above a steel floor construction, made of OSB panels, placed in two layers, |  |  |  |  |  |  |
|  |  | lower layer of OSB panel, at d=15mm and upper layer of OSB panel, at d=9mm; manner of placement: by using folds |  |  |  |  |  |  |
|  |  | of min. 30 cm and dilatation fugue up to a facade wall 3 cm |  |  |  |  |  |  |
|  | 3.1.3 | thick | m2 | 144.20 |  | 0.00 |  |  |

Page 1

| Laying down thermal isolation of stone wool in a lower zone |  |  |  |
| --- | --- | --- | --- |
| between the bedding steel construction, below the bedding construction, at d=15cm |  |  |  |
| 3.1.4 | m2 | 144.20 | 0.00 |

Page 2

|  | Preparation of inner walls at d=12cm made of plaster card boards (foundation of two boards each) on appropriate |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | sub-construction, by placing mineral wool within the wall, between GKP. Height: 320cm |  |  |  |  |
|  | Note: in the sanitary facilities, the walls should be made of water-proof plaster card board |  |  |  |  |
| 3.1.5 |  | m2 | 132.09 |  | 0.00 |
|  | Preparation of loft conversion made of plaster card board on |  |  |  |  |
|  | appropriate sub-construction, at a floor height of 320 cm, by |  |  |  |  |
|  | placing mineral wool in the upper loft zone |  |  |  |  |
| 3.1.6 |  | m2 | 144.20 |  | 0.00 |
|  | Horizontal (floor) hydro-isolation in sanitary facilities and |  |  |  |  |
|  | in a kitchen, by coating in two layers and placement of |  |  |  |  |
|  | angle bands of abutment of the wall and the floor, by |  |  |  |  |
|  | coating the walls at a height of 30 cm from the floor |  |  |  |  |
| 3.1.7 |  | m2 | 35.96 |  | 0.00 |
|  | Purchase, transportation and installation of laminate at d=8mm, Class 1, design and colour as per investor’s choice, |  |  |  |  |
|  | placed on insulating felt at d=2mm, by placing wall battens |  |  |  |  |
| 3.1.8 |  | m2 | 87.67 |  | 0.00 |
|  | Purchase, transportation and instalment of floor and wall |  |  |  |  |
| 3.1.9 | ceramic boards, Class 1, as per investor’s choice |  |  |  |  |
|  | floor: | m2 | 51.36 |  | 0.00 |
|  | wall (toilettes at height of up to 160cm, kitchen up to 150cm): | m2 | 76.47 |  | 0.00 |
|  | Double polishing and painting of walls, in a colour as per |  |  |  |  |
| 3.1.10 | Investor’s choice |  |  |  |  |
|  | walls: | m2 | 231.55 |  | 0.00 |
|  | lofts: | m2 | 144.20 |  | 0.00 |
|  | Construction of contact facade of graphite Styrofoam panels at d=8cm, using all necessary layers and colour as per |  |  |  |  |
| 3.1.11 | Investor’s choice: Note: including staging or platforms | m2 | 110.71 |  | 0.00 |
|  | Construction and mounting facade portals, made of thermal |  |  |  |  |
|  | aluminium profiles, with necessary manacles and fill, |  |  |  |  |
| 3.1.12 | following a carpentry scheme |  |  |  |  |
|  | 126x318cm | No. | 7 |  | 0.00 |
|  | 134x318cm | No. | 1 |  | 0.00 |
|  | 171x318cm | No. | 6 |  | 0.00 |
|  | 208x318cm | No. | 1 |  | 0.00 |
|  | 126x62cm | No. | 5 |  | 0.00 |
|  | 134x62cm | No. | 1 |  | 0.00 |
|  | 208x62cm | No. | 1 |  | 0.00 |
|  | 254x62cm | No. | 1 |  | 0.00 |
|  | 344x62cm | No. | 1 |  | 0.00 |
|  | Construction and mounting inner doors, made of thermal |  |  |  |  |
|  | aluminium profiles, with necessary chain and handles, as well |  |  |  |  |
| 3.1.13 | as feels, following a carpentry scheme |  |  |  |  |
|  | 81x210cm | No. | 9 |  | 0.00 |
|  | 109x210cm | No. | 1 |  | 0.00 |

Page 3

|  | Purchase and placement of sandwich ribbed metal sheet |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 3.1.14 | on steel sub-construction | m2 | 184 |  | 0.00 |
|  | Purchase and placement of wind battens on fitting |  |  |  |  |
| 3.1.15 | sub-construction, as lateral fasteners of the roof cover | m' | 57.3 |  | 0.00 |

Page 4

|  | Purchase and placement of snow proof boards, placed in two |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | rows on the lengthier side of the roof, with in-between |  |  |  |  |
| 3.1.16 | distance of 125cm, snow proof boards at L=150cm and V=15cm | pcs | 13 |  | 0.00 |
|  | Purchase and placement of horizontal and vertical gutter at |  |  |  |  |
|  | dimension 12,5x12,5cm, made of galvanised steel metal |  |  |  |  |
|  | sheet, placed on appropriate carriers of the steel roof |  |  |  |  |
| 3.1.17 | construction | m' | 28 |  | 0.00 |
| 3.2 | TERRACE |  |  |  |  |
|  | Full construction of eaves with envisaged modular pergola, |  |  |  |  |
| 3.2.1 | covered with movable PVC canvases – BUILDING: 1 | m2 | 135 |  | 0.00 |
|  | Platform made of steel profiles, coated with composite boards |  |  |  |  |
|  | (imitation of decking), type: WPC (Wood & Plastic Composite) |  |  |  |  |
|  | dim. 280/14/2,2cm, platform at a height of 30 cm (BUILDING 1) |  |  |  |  |
| 3.2.2 |  | kg | 1,470 |  | 0.00 |
|  | Platform made of steel profiles, coated with composite boards |  |  |  |  |
|  | (imitation of decking), type: WPC (Wood & Plastic Composite) |  |  |  |  |
|  | dim. 280/14/2,2cm, platform at a height of 40 cm (BUILDING |  |  |  |  |
| 3.2.3 | 2) | kg | 1,380 |  | 0.00 |
|  | Wall coating over an existing parapet with SIPOREX blocks |  |  |  |  |
| 3.2.4 | at d=20cm, in three rows | m1 | 74 |  | 0.00 |
|  | Construction of stairs (stepping area), at dim.1,80xh0,30 |  |  |  |  |
|  | made of granite tiles (to prevent sliding), stairs heading |  |  |  |  |
| 3.25 | towards roof terrace | m1 | 80 |  | 0.00 |
|  | Construction of stairs (stepping area), at dim.3,15x0,90 |  |  |  |  |
|  | made of granite tiles (to prevent sliding), stairs heading |  |  |  |  |
| 3.2.6 | towards the terrace | m1 | 23 |  | 0.00 |
|  | Construction of pedestrian surfaces made of becaton tiles, |  |  |  |  |
|  | 3-4 cm thick, placed on a fitting foundation, by necessary |  |  |  |  |
| 3.2.7 | compression | m2 | 458 |  | 0.00 |
|  | Purchase and placement of gardening becaton curb-stones |  |  |  |  |
| 3.2.8 | at dim. 12/5/50cm | m1 | 39 |  | 0.00 |
|  | Purchase and placement of stone panels or concrete panels |  |  |  |  |
|  | at d=5cm (processing: natural, counter-sliding), at dim. |  |  |  |  |
| 3.2.9 | 1,20x0,40m | No. | 125 |  | 0.00 |
|  | Construction of lateral walls made of SIPOREX to form |  |  |  |  |
|  | jardinières, coated with a cover of stone boards |  |  |  |  |
| 3.2.10 |  | m2 | 82.65 |  | 0.00 |
|  | Purchase and mounting of composite boards on steel |  |  |  |  |
| 3.2.11 | platforms, platforms marked with No. 4 | m2 | 190.00 |  | 0.00 |
|  | Processing of damaged parts of existing parapet walls and |  |  |  |  |
|  | full painting with counter-corrosion one-component |  |  |  |  |
|  | water-proof mixture for protection of concrete surfaces in |  |  |  |  |
|  | white colour (RAL 9003 or RAL 9002), by previous removal |  |  |  |  |
| 3.2.12 | of existing coating, in developed surface of ssa. 50cm | m | 122.00 |  | 0.00 |
|  | TOTAL: |  |  | 0.00 |

Page 5

| 4 | WATER SUPPLY AND DRAINAGE |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 4.1 | WATER SUPPLY INSTALATION (GREEN GARDEN) |  |  |  |  |
| 4.1.1 | Marking and staking out a water supply route | m' | 74.76 |  | 0.00 |
|  | Purchase, transportation and mounting a galvanised pipe with |  |  |  |  |
| 4.1.2 | F2" | m' | 51.56 |  | 0.00 |
|  | Purchase, transportation and mounting a galvanised pipe with |  |  |  |  |
| 4.1.3 | F6/4" | m' | 16.80 |  | 0.00 |
|  | Purchase, transportation and mounting a galvanised pipe with |  |  |  |  |
| 4.1.4 | F5/4" | m' | 3.65 |  | 0.00 |
|  | Purchase, transportation and mounting a galvanised pipe with |  |  |  |  |
| 4.1.5 | F1" | m' | 3.15 |  | 0.00 |
| 4.1.6 | Purchase, transportation and mounting a galvanised fitting | kg | 150.00 |  | 0.00 |
| 4.1.7 | Purchase, transportation and mounting a valve F2" | pcs | 1 |  | 0.00 |
| 4.1.8 | Purchase, transportation and mounting a valve F6/4" | pcs | 1 |  | 0.00 |
| 4.1.9 | Purchase, transportation and mounting a valve F5/4" | pcs | 1 |  | 0.00 |
| 4.1.10 | Purchase, transportation and mounting a valve F1" | pcs | 3 |  | 0.00 |
|  | Purchase, transportation and mounting a combined water |  |  |  |  |
| 4.1.11 | gauge F50/20 | pcs | 1 |  | 0.00 |
| 4.1.12 | Pipe fittings for water line |  |  |  | 0.00 |
|  | T fitting F2"/6/4" | pcs | 1 |  | 0.00 |
|  | T fitting FF2"/5/4" | pcs | 1 |  | 0.00 |
|  | T fitting F1"/3/4" | pcs | 6 |  | 0.00 |
|  | Reducing nipples F3/4"/1/2" | pcs | 12 |  | 0.00 |
|  | Elbows F3/4" | pcs | 6 |  | 0.00 |
|  | Elbows F1/2" | pcs | 4 |  | 0.00 |
|  | Valve F2" | pcs | 1 |  | 0.00 |
|  | Valve F6/4" | pcs | 1 |  | 0.00 |
|  | Valve 5/4" | pcs | 3 |  | 0.00 |
| 4.1.13 | Pipe fittings for sewerage line |  |  |  | 0.00 |
|  | Top siphon (running trap) F75mm | pcs | 3 |  | 0.00 |
|  | S-curve F100mm | pcs | 4 |  | 0.00 |
|  | T piece 100/75mm | pcs | 8 |  | 0.00 |
|  | S-curve F40mm | pcs | 8 |  | 0.00 |
|  | T piece 150/100mm | pcs | 3 |  | 0.00 |
|  | Revision pieces 40mm | pcs | 3 |  | 0.00 |
| 4.2 | WATER INSTALLATION (COFFEE BAR) |  |  |  | 0.00 |
|  | Purchase, transportation and mounting a galvanised pipe |  |  |  |  |
| 4.2.1 | F1" | m' | 50 |  | 0.00 |
|  | Purchase, transportation and mounting a galvanised pipe |  |  |  |  |
| 4.2.2 | F3/4" | m' | 6.50 |  | 0.00 |
|  | Purchase, transportation and mounting a galvanised pipe |  |  |  |  |
| 4.2.3 | F1" | m' | 7.50 |  | 0.00 |
| 4.2.4 | Purchase, transportation and mounting a galvanised fitting | kg | 110.00 |  | 0.00 |
| 4.2.5 | Purchase, transportation and mounting a valve F1" | pcs | 1 |  | 0.00 |
| 4.2.6 | Purchase, transportation and mounting a valve F3/4" | pcs | 1 |  | 0.00 |
| 4.2.7 | Purchase, transportation and mounting a valve F1/2" | pcs | 12 |  | 0.00 |
| 4.2.8 | Purchase, transportation and mounting a water gauge F3/4" | pcs | 1 |  | 0.00 |
| 4.2.9 | Pipe fittings for water line |  |  |  | 0.00 |
|  | T fitting F2"/1" | pcs | 1 |  | 0.00 |
|  | T fitting F1"/3/4" | pcs | 2 |  | 0.00 |
|  | T fitting F1"/1/2" | pcs | 6 |  | 0.00 |
|  | Reducing nipples F3/4"/1/2" | pcs | 5 |  | 0.00 |
|  | Elbows F3/4" | pcs | 3 |  | 0.00 |

Page 6

|  | Elbows F1/2" | pcs | 12 |  | 0.00 |
| --- | --- | --- | --- | --- | --- |
|  | Valve F1" | pcs | 1 |  | 0.00 |
|  | Valve F3/4" | pcs | 2 |  | 0.00 |
|  | Valve 1/2" | pcs | 12 |  | 0.00 |
| 4.2.10 | Pipe fittings for sewerage line |  |  |  | 0.00 |
|  | Siphon (running trap) F75mm | pcs | 12 |  | 0.00 |

Page 7

|  | S-curve F75mm | pcs | 6 |  | 0.00 |
| --- | --- | --- | --- | --- | --- |
|  | T fitting 75/50mm | pcs | 8 |  | 0.00 |
|  | S-curve F40mm | pcs | 8 |  | 0.00 |
|  | T fitting 100/75mm | pcs | 3 |  | 0.00 |
|  | Revision fittings 40mm | pcs | 3 |  | 0.00 |
|  | TOTAL: |  |  |  | 0.00 |
| 5 | EQUIPMENT |  |  |  |  |
|  | Modular shell made of steel profiles, made of 4 segments, |  |  |  |  |
|  | collection system: sliding in metal rails, placed on wheels, |  |  |  |  |
|  | developed dimension: 10,84 metres (4x271cm) (No. A) - as |  |  |  |  |
| 5.1 | per submitted DETAIL | kg | 480 |  | 0.00 |
|  | Construction of a fountain 23x4 metres, with all necessary |  |  |  |  |
|  | filters, with a trough made of SIPOREX blocks, |  |  |  |  |
| 5.2 | d=60x50x20cm, v=80cm (No. B1) |  |  |  |  |
|  | Conducting hydro-isolation of bedding surface | m2 | 80.33 |  | 0.00 |
|  | Conducting hydro-isolation of wall surfaces at a height of |  |  |  |  |
|  | 60cm, in two layers, by placing angle band, at L=56,40m', |  |  |  |  |
|  | at abutment of the floor with the wall | m2 | 33.84 |  | 0.00 |
|  | Pasting pool tiles (floor), at dimension 20x11cm and fugue |  |  |  |  |
|  | of 1cm, by using appropriate glue | m2 | 80.33 |  | 0.00 |
|  | Pasting pool tiles (wall), at dimension 20x11cm and fugue |  |  |  |  |
|  | of 1 cm, by using appropriate glue | m2 | 33.84 |  | 0.00 |
|  | Geysers 60T, with height of geyser/stream of 150cm, with |  |  |  |  |
|  | necessary pressure of 4,6m/~-0,46 atm | No. | 3 |  | 0.00 |
|  | Pump, 2,2KV/3HP/230-400V, V-50Hz/35m3/hour | No. | 1 |  | 0.00 |
|  | Necessary installation + fitting + Valves | No. | 1 |  | 0.00 |
|  | Lighting | No. | 1 |  | 0.00 |
|  | TREATMENT |  |  |  |  |
|  | Filter 500mm/7,8m3/hour | No. | 1 |  | 0.00 |
|  | Pump 0,33 HP/230-400V-50Hz/7m3 / hour | No. | 1 |  | 0.00 |
|  | Installation +fitting + valves | No. | 1 |  | 0.00 |
|  | Gutter | No. | 1 |  | 0.00 |
|  | Skimmer | No. | 1 |  | 0.00 |
|  | Construction of a small fountain with R=150cm, with all |  |  |  |  |
|  | necessary filters, with trough made of SIPOREX blocks, at |  |  |  |  |
|  | d=15cm and V=40cm, outside coating material: artificial |  |  |  |  |
| 5.3 | granite (B3) |  |  |  |  |
|  | Conducting hydro-isolation of floor surface | m2 | 5.72 |  | 0.00 |
|  | Conducting hydro-isolation of wall surfaces at a height of |  |  |  |  |
|  | 60cm, in two layers, by placing ankle band with L=8,48m' at |  |  |  |  |
|  | abutment of the floor with the wall | m2 | 3.39 |  | 0.00 |
|  | Pasting pool tiles (floor) at dimension 20x11cm and fugue of |  |  |  |  |
|  | 1 cm, by using appropriate glue | m2 | 5.72 |  | 0.00 |
|  | Pasting pool tiles (wall) at dimension 20x11cm and fugue of |  |  |  |  |
|  | 1cm, by using appropriate glue | m2 | 3.39 |  | 0.00 |
|  | Pasting artificial granite tiles (wall) with fugue of 1 cm, |  |  |  |  |
|  | by using appropriate glue | m2 | 3.39 |  | 0.00 |
|  | Geyser 40T, height 0,75cm/4,60m3/hour, 2,40m/hour/0,25atm | No. | 1 |  | 0.00 |
|  | Geyser 40T, height 150cm/5,90m3/hour, 4,00m/hour/0,40atm | No. | 1 |  | 0.00 |

Page 8

|  | Pump 1,1Kv/1,5HP/230-400V-50Hz/16m3/hour | No. | 1 |  | 0.00 |
| --- | --- | --- | --- | --- | --- |
|  | Installation + fitting + Valves | No. | 1 |  | 0.00 |
|  | Gutter | No. | 1 |  | 0.00 |
|  | Skimmer | No. | 1 |  | 0.00 |
|  | LED Lighting | No. | 1 |  | 0.00 |
|  | Electrical command board | No. | 1 |  | 0.00 |

Page 9

|  | Construction and mounting a waterfall fountain with filter, |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | trough surface 25m2, material: artificial granite (B2), with |  |  |  |  |
| 5.4 | width of curtain at 600cm, INOX AISI 316 |  |  |  |  |
|  | Conducting hydro-isolation of floor surface | m2 | 14.81 |  | 0.00 |
|  | Conducting hydro-isolation of wall surfaces at a height of |  |  |  |  |
|  | 35cm (of troughs) at a height of 250cm (wall), in two layers, |  |  |  |  |
|  | by placing ankle band of L=23.65m', on an abutment of the floor and the wall | m2 | 21.86 |  | 0.00 |
|  | Pasting pool tiles (floor), at dimension 20x11cm and fugue of |  |  |  |  |
|  | 1cm, by using appropriate glue | m2 | 14.81 |  | 0.00 |
|  | Pasting pool tiles (wall), at dimension 20x11 cm and fugue of |  |  |  |  |
|  | 1cm, by using appropriate glue | m2 | 21.86 |  | 0.00 |
|  | Pump 2x2Kv-3Hp/230-400V-50Hz/,52m3/hour | No. | 1 |  | 0.00 |
|  | Installation + fitting + valves | No. | 1 |  | 0.00 |
|  | TREATMENT |  |  |  | 0.00 |
|  | Filter 500mm/7,8m3/hour | No. | 1 |  | 0.00 |
|  | Pump 0,33Hp/230-400V-50Hz/7m3/hour | No. | 1 |  | 0.00 |
|  | Installation + fitting + valves | No. | 1 |  | 0.00 |
|  | Gutter | No. | 1 |  | 0.00 |
|  | Skimmer | No. | 1 |  | 0.00 |
|  | LED lighting | No. | 1 |  | 0.00 |
|  | Electrical command board | No. | 1 |  | 0.00 |
|  | Preparation and placement of bike holder, dim. 65x55cm, |  |  |  |  |
|  | material: thick-wall steel profiles with F100mm, painted in |  |  |  |  |
| 5.5 | green colour (as per DETAIL) | pcs | 5 |  | 0.00 |
|  | Preparation of a semicircular booth, with L=12,40 metres, |  |  |  |  |
|  | composed of 4 segments, with dim. of 310cm and seat width |  |  |  |  |
|  | of 60cm. Material: steel construction with seats made of PVC |  |  |  |  |
|  | boards (wood imitation) (No.7), as per adopted DETAIL of |  |  |  |  |
| 5.6 | segment benches | No. | 2 |  | 0.00 |
|  | Preparation of a semicircular booth, with L=7,60 metres |  |  |  |  |
|  | composed of 2 segments, with dim. of 380cm and seat width |  |  |  |  |
|  | of 60cm. Material: steel construction with seats made of PVC |  |  |  |  |
|  | boards (wood imitation) (No.7), as per adopted DETAIL of |  |  |  |  |
| 5.7 | segment benches | No. | 1 |  | 0.00 |
|  | Preparation of circular benches made of steel construction, |  |  |  |  |
|  | coated with PVC boards (wood imitation), with L=15m' and |  |  |  |  |
|  | seat width of 60cm, composed of 3 segments, with |  |  |  |  |
| 5.8 | L=375cm/60cm, as per adopted DETAIL of segment benches | No. | 2 |  | 0.00 |
|  | Segment benches (circular segment), made of steel |  |  |  |  |
|  | construction, coated with composite boards (wood imitation), |  |  |  |  |
|  | with seat width of 60cm, as per adopted DETAIL of segment |  |  |  |  |
| 5.9 | benches |  |  |  | 0.00 |
|  | L=240cm | No. | 2 |  | 0.00 |
|  | L=260cm | No. | 1 |  | 0.00 |
|  | L=290cm | No. | 1 |  | 0.00 |
|  | L=360cm | No. | 1 |  | 0.00 |
|  | L=420cm | No. | 1 |  | 0.00 |
|  | L=460cm | No. | 1 |  | 0.00 |

Page 10

|  |  | Preparation of a chess field 480x480cm (8x60cm), a set with |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | chess pieces, made of glass-plastic panels, at d=2x3cm, with |  |  |  |  |
|  |  | foil in between, placed on a steel construction with distribution |  |  |  |  |
|  |  | 60/60cm, coated with two panels AQUAPANEL, painted in |  |  |  |  |
|  | 5.10 | white colour, as per DETAIL | No. | 1 |  | 0.00 |
|  |  | Preparation and placement of single seating benches, at |  |  |  |  |
|  |  | dim.160x60x60cm, seat and rest support, covered with |  |  |  |  |
|  | 5.11 | composite boards in wood pattern | No. | 24 |  | 0.00 |
|  |  |  |  |  | Total | 0.00 |
|  | 6 | FENCES |  |  |  |  |
|  |  | Purchase, preparation and mounting aluminium fence, |  |  |  |  |
|  |  | fill: laminated (PAMPLEKS) glass 3.3.1., |  |  |  |  |
|  | 6.1 | height:104cm, as per DETAIL | m | 122.00 |  | 0.00 |
|  |  | Purchase, preparation and mounting aluminium fence, |  |  |  |  |
|  | 6.2 | fill: hawsers, height: 90cm, as per DETAIL | m | 19.42 |  | 0.00 |
|  |  | TOTAL: |  |  |  | 0.00 |

Page 11

|  | 7 | ELECTRICITY |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 7.1 | ENERGY SUPPLY |  |  |  |  |  |
| 7.1.1 | Delivery and placement of supply cable from existing GRT – GTC |  |  |  |  |  |
|  |  | to GRO-Terrace and insuring the supply cable by placing safety fuse |  |  |  |  |  |
|  |  | in GRT-GTC |  |  |  |  |  |
| - | NXHMH 5x16mm² | m | 100.00 |  | 0.00 |  |
| 7.1.2 | Automatic safety fuse iC60N-63A/C 1p (single-pole) | pcs | 3.00 |  | 0.00 |  |
|  |  | Digging out a ditch into earth of 3 category and filling it with two |  |  |  |  |  |
|  |  | layers of 10 cm each of gravel, dimensions 0,4x0,4m, to place |  |  |  |  |  |
|  |  | cables and for grounding arrangements | m | 1.00 |  | 0.00 |  |
|  |  |  |  |  | TOTAL: |  |  |  | 0.00 |  |
| 7.2 | HIGH POWER INSTALLATION AND EQUIPMENT |  |  |  |  |  |
| 7.2.1 | Delivery and placement of cable in an earth ditch, a set of |  |  |  |  |  |
|  |  | installation of switchboards and entire supporting material, |  |  |  |  |  |
|  |  | connection and examination of operability. |  |  |  |  |  |
|  | - | NXHMH 5x10mm² | m | 50.00 |  | 0.00 |  |
|  | - | NXHMH 5x6mm² | m | 110.00 |  | 0.00 |  |
| - | NXHMH 5x2.5mm² | m | 250.00 |  | 0.00 |  |
| - | NXHMH 3x2.5mm² | m | 490.00 |  | 0.00 |  |
| 7.2.2 | Delivery and placement of self-extinguishing flexible hose F25 |  |  |  | 0.00 |  |
|  |  |  | m | 250.00 |  | 0.00 |  |
| 7.2.3 | Delivery and mounting a GRO - Terrace, IP65. A set with all |  |  |  |  |  |
|  |  | necessary material and scheming, - part for safety fuses and part |  |  |  |  |  |
|  |  | for rails made of copper. The board should be perforated with below conduit, in accordance with the entry-exit conductors, as |  |  |  |  |  |
|  |  | the one-pole scheme. GRO should be mounted on a fundament, at |  |  |  |  |  |
|  |  | maximum height of 0,4m, below a readymade floor, and the |  |  |  |  |  |
|  |  | following equipment should be installed within it: |  |  |  |  |  |
|  |  |  |  |  |  | pcs | 1.00 |  | 0.00 |  |
| - | N.N. Three-pole electric switch with built-in remote switch-off winding |  |  |  |  |  |
|  |  | type: NSX100B, TM63D, 100A/63A - 3p - |  |  |  |  |  |
|  |  | “Schneider Electric” | pcs | 1.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-6A/B 1p (one-pole) | pcs | 2.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-10A/B 1p (one-pole) | pcs | 5.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-16A/B 1p (one-pole) | pcs | 2.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-16A/B 3p (three-pole) | pcs | 2.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-20A/C 3p (three-pole) | pcs | 3.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-40A/B 3p (three-pole) | pcs | 1.00 |  | 0.00 |  |
|  | - | ST contactor for rail installation |  |  |  |  |  |
|  |  | type: iCT 16A ,220VAC, 3p | pcs | 1.00 |  | 0.00 |  |
|  | - | ST contactor for rail installation |  |  |  |  |  |
|  |  | type: iCT 16A ,220VAC, 1p | pcs | 5.00 |  | 0.00 |  |
|  | - | One-pole rugged clip, type: iSSW- 3 positions. 20A | pcs | 4.00 |  | 0.00 |  |
| - | Timer for light command for rail installation |  |  |  |  |  |
|  |  | type: TIMER, IHP 1. 220VAC. 16A | pcs | 2.00 |  | 0.00 |  |
|  | - | Photo-rely with plumb-line | pcs | 2.00 |  | 0.00 |  |

Page 12

- Set with clamps, lateral and front carriers, reserve rails for thread of additional safety fuses, ID reglet flashings,

| supporting scheming material | Pcs | 1.00 | 0.00 |
| --- | --- | --- | --- |

Page 13

| 7.2.4 | Delivery and mounting a RO - Fountain, F1,F2,F3 |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | self-supporting cabinet, IP65. A set with entire supporting |  |  |  |  |  |
|  |  | material and scheming, - part for safety fuses and part for copper |  |  |  |  |  |
|  |  | rails. The cabinet should be perforated with conduit from below, in accordance with the entry-exit conductors, as per one-pole scheme. RO should be mounted on a fundament, and the |  |  |  |  |  |
|  |  | following equipment should be installed within it: |  |  |  |  |  |
|  |  |  |  |  | pcs | 3.00 |  | 0.00 |  |
| - | Voltage N.N. four-pole clip, In=40A, Ik=36kA, |  |  |  |  |  |
|  |  | mounting a DIN rail |  |  | pcs | 3.00 |  | 0.00 |  |
|  | - | Drain pipe for over-voltage of mounting rail type: iPF |  |  |  |  |  |
|  |  | 3P+N,10kA/5kA |  |  | pcs | 3.00 |  | 0.00 |  |
|  | - | Automatic safety fuse iC60N-6A/B 1p (one-pole) | pcs | 3.00 |  | 0.00 |  |
|  | - | Automatic safety fuse iC60N-10A/B 1p (one-pole) | pcs | 6.00 |  | 0.00 |  |
|  | - | Automatic safety fuse iC60N-16A/C 1p (one-pole) | pcs | 9.00 |  | 0.00 |  |
|  | - | Automatic safety fuse iC60N-40A/B 3p (three-pole) | pcs | 3.00 |  | 0.00 |  |
| - | Automatic safety fuse E60N-40A/C, 3P+N (four-pole) | pcs | 3.00 |  | 0.00 |  |
|  | - | ST contactor for rail mounting |  |  |  |  |  |  |  |
|  |  | type: iCT 16A ,220VAC, 1p |  |  | pcs | 6.00 |  | 0.00 |  |
|  | - | One-pole rugged clip type: iSSW- 3 positions. 20A | pcs | 6.00 |  | 0.00 |  |
| - | Timer for light command for rail mounting |  |  |  |  |  |
|  |  | type: TIMER, IHP 1. 220VAC. 16A | pcs | 3.00 |  | 0.00 |  |
|  | - | Photo-rely with plumber-line |  |  | pcs | 3.00 |  | 0.00 |  |
| - | A set with clamps, lateral and front carriers, reserve rails for |  |  |  |  |  |
|  |  | threads of additional safety fuses, ID reglet flashings, |  |  |  |  |  |
|  |  | supporting scheming material |  |  | pcs | 3.00 |  | 0.00 |  |
|  |  |  |  |  |  |  | TOTAL: |  |  |  | 0.00 |  |
| 7.3 | LIGHTING |  |  |  |  |  |  |  |
| 7.3.1 | Delivery and mounting lighting devices, as per space |  |  |  |  |  |
|  |  | specification. A set with entire supporting materials, connection |  |  |  |  |  |
|  |  | and examination of operability. |  |  |  |  |  |
| - | Candelabra | MORPHIS c.177, h=3 | , LED, 1x24W, 3000K |  |  |  |  |  |
|  |  |  |  |  | M |  |  |  |  |  |
|  |  | ,(a set with a pillar at h=250cm and automatic safety fuse |  |  |  |  |  |
|  |  | iC60N-10A/B 1p ), type:a |  |  | pcs | 14.00 |  | 0.00 |  |
|  | - | Pillar light Ibis 2 LED c.451, h=75cm, 20W, 3000K |  |  |  |  |  |
|  |  | type: b |  |  |  |  | pcs | 26.00 |  | 0.00 |  |
|  |  | Floor light, MIRA 65 c.5383, 5W, |  |  |  |  |  |
|  |  | 240V,3000K, type: C |  |  | pcs | 4.00 |  | 0.00 |  |
| - | BRICK LIGHT c.410, 6W, 3000K , type: d | pcs | 14.00 |  | 0.00 |  |
|  |  |  |  |  |  |  | TOTAL: |  |  |  | 0.00 |  |
| 7.4 | CONSTRUCTION, EARTH AND INSTALLATION WORKS |  |  |  |  |  |
| 7.4.1. | Digging out a ditch into the earth of 3 category and filling with two |  |  |  |  |  |
|  |  | layers of 10 cm each of gravel, dimensions 0,4x0,4m, for |  |  |  |  |  |
|  |  | placement of grounding cables and band | m | 250.00 |  | 0.00 |  |
| 7.4.2. | Delivery and placement of concrete fundaments, with dimensions |  |  |  |  |  |
|  |  | 50x50x40cm, for light of type: a | pcs | 14.00 |  | 0.00 |  |
| 7.4.3. | Delivery and placement of concrete fundaments, with dimensions |  |  |  |  |  |
|  |  | 30x15x20cm, for light of type: b | pcs | 26.00 |  | 0.00 |  |

Page 14

| 7.4.4. | Delivery and placement of plastic shields into the ditch, alongside |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | the entire length of cables | pcs | 250.00 |  | 0.00 |  |
| 7.4.5. | Delivery and placement of hot air galvanised iron band 25x44mm, |  |  |  |  |  |
|  |  | for the purpose of grounding, in a excavated ditch | m | 250.00 |  | 0.00 |  |
| 7.4.6. | Delivery, placement and connection of hot air galvanised iron band |  |  |  |  |  |
|  |  | 25x4mm, with average length of 1m, which in one end is |  |  |  |  |  |
|  |  | fastened against the metal pillar with a bore M8, and in the other |  |  |  |  |  |
|  |  | end with a junction band – the band is connected with the |  |  |  |  |  |
|  |  | main grounding. The juncture shall be coated with bitumen. |  |  |  |  |  |
|  |  |  | pcs | 14.00 |  | 0.00 |  |
| 7.4.7. | Delivery and placement of warning plastic band “Dangerous” |  |  |  |  |  |
|  |  |  | m | 250.00 |  | 0.00 |  |
| 7.4.8. | Examination of entire installation by measuring the grounding |  |  |  |  |  |
|  |  | and issuing attestation of measuring spot – pillar | pcs | 14.00 |  | 0.00 |  |
|  |  |  |  |  |  | TOTAL: |  |  |  | 0.00 |  |
| 7.5 | GENERAL POSITIONS |  |  |  |  |  |
| 7.5.1. | Visit paid by an expert, check each installation separately, check |  |  |  |  |  |
|  |  | each connection spot, put into operation and issuance of |  |  |  |  |  |
|  |  | attestation | pcs | 1.00 |  | 0.00 |  |
| 7.5.2. | Assistance, connection and technical support when mounting |  |  |  |  |  |
|  |  | electrical equipment. A set with supporting material, connection |  |  |  |  |  |
|  |  | and testing the operability | pcs | 1.00 |  | 0.00 |  |
| 7.5.3. | Drafting documentation on the state of completed activities | pcs | 1.00 |  | 0.00 |  |
|  |  |  |  |  |  | TOTAL: |  |  |  | 0.00 |  |
|  |  |  | SUMMARY A |  |  |  |  |  |
| 7.1 | POWER SUPPLY |  |  |  | 0.00 |  |
| 7.2 | HIGH-VOLTAGE INSTALLATION AND EQUIPMENT |  |  |  | 0.00 |  |
| 7.3 | LIGHTING |  |  |  | 0.00 |  |
| 7.4 | CONSTRUCTION, EARTH AND INSTALLATION WORKS |  |  |  | 0.00 |  |
| 7.5 | GENERAL POSITIONS |  |  |  | 0.00 |  |
|  |  |  |  |  |  | GRAND TOTAL A |  |  |  | 0.00 |  |
| 7.6 | HIGH-VOLTAGE POWER INSTALLATION AND EQUIPMENT |  |  |  |  |  |
| 7.6.1 | Delivery and insertion of a cable into an earth ditch and of cables into a building, by placing metal rails on brackets, |  |  |  |  |  |
|  |  | set on each 30cm alongside the entire length of the |  |  |  |  |  |
|  |  | conductor against the wall and the loft. A set with installation |  |  |  |  |  |
|  |  | switchboards and entire supporting material, connection and |  |  |  |  |  |
|  |  | testing the operability. |  |  |  |  |  |
|  | - | NXHMH 5x10mm² | m | 80.00 |  | 0.00 |  |
|  |  | *Delivery and placement of plastic shields into the ditch |  |  |  |  |  |
|  |  | along the entire length of the supply cable to the Coffee Bar |  |  |  |  |  |
|  |  | facility | Pcs | 70.00 |  | 0.00 |  |

Page 15

|  |  | *Delivery and placement of warning plastic band |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | “Dangerous" |  | M | 70.00 |  | 0.00 |  |
| - | NYM-J 3x2.5mm² |  | m | 300.00 |  | 0.00 |  |
|  | - | NYM-J 3x1.5mm² |  | m | 290.00 |  | 0.00 |  |
| 7.6.2 | Delivery and mounting a RT – Coffee Bar. A set with overall |  |  |  |  |  |
|  |  | supporting material and scheming – part for safety fuses and |  |  |  |  |  |
|  |  | part for copper rails. The switchboard should be perforated with conduit from below, in accordance with entry-exit |  |  |  |  |  |
|  |  | conductors, as per one-pole scheme. |  |  |  |  |  |
|  |  |  |  | pcs | 1.00 |  | 0.00 |  |
|  | - | Four-pole rugged clamp, 63A with 2 pos. 0 and 1 | pcs | 1.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-6A/B 1p | (one-pole) | pcs | 1.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-10A/B 1p | (one-pole) | pcs | 4.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-16A/B 1p | (one-pole) | pcs | 12.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-20A/C 3p (three-pole) | pcs | 2.00 |  | 0.00 |  |
| - | Automatic safety fuse iC60N-40A/B 3p | (three-pole) | pcs | 1.00 |  | 0.00 |  |
| - | Automatic safety fuse E60N-40A/C, 3P+N, (four-pole) | pcs | 1.00 |  | 0.00 |  |
| - | ST contactor for rail mounting |  |  |  |  |  |  |
|  |  | type: iCT 16A ,220VAC, 1p |  | pcs | 5.00 |  | 0.00 |  |
| - | One-pole rugged clamp, type: iSSW- 3 positions. 20A | pcs | 2.00 |  | 0.00 |  |
| - | Timer for light command during rail mounting |  |  |  |  |  |
|  |  | type: TIMER, IHP 1. 220VAC. 16A | pcs | 1.00 |  | 0.00 |  |
|  | - | Photo-relay with plumb-line |  | pcs | 1.00 |  | 0.00 |  |
| - | Over-voltage arrestor for rail mounting, type: iPF |  |  |  |  |  |
|  |  | 3P+N,20kA/5kA |  | pcs | 1.00 |  | 0.00 |  |
| - | Protective differential power clamp, AC300mA- |  |  |  |  |  |
|  |  | 40A 3p (three-pole) |  | pcs | 1.00 |  | 0.00 |  |
| - | A set with landscaping clamps, lateral and frontal carriers, reserve rails for thread of additional safety fuses, ID reglet |  |  |  |  |  |
|  |  | flashings, supporting scheming material |  |  |  |  |  |
|  |  |  |  | pcs | 1.00 |  | 0.00 |  |
|  |  | Delivery and mounting a modular system of equipment. |  |  |  |  |  |
|  |  | A set with overall supporting material, connection and testing |  |  |  |  |  |
|  |  | of operability, as follows: |  |  |  | 0.00 |  |
|  | - | wall box 120x100 |  | pcs | 4 |  | 0.00 |  |
|  | - | wall box for 2 modules |  | pcs | 10 |  | 0.00 |  |
|  | - | wall box for 4 modules |  | pcs | 12 |  | 0.00 |  |
|  | - | carrier for 1/2 module |  | pcs | 10 |  | 0.00 |  |
|  | - | carrier for 4 modules |  | pcs | 12 |  | 0.00 |  |
|  | - | mask for 1/2 module |  | pcs | 10 |  | 0.00 |  |
|  | - | mask for 4 modules |  | pcs | 12 |  | 0.00 |  |
|  | - | Circuit breaker - 1 module 10AX |  | pcs | 8 |  | 0.00 |  |
|  | - | Circuit breaker - 2 module 10AX |  | pcs | 3 |  | 0.00 |  |
|  | - | Socket 2 modules 10/16A 2P+E |  | pcs | 26 |  | 0.00 |  |
| - | Mounting electro-gallantry – modular system. A set with |  |  |  |  |  |
|  |  | overall supporting material, connection and testing of |  |  |  |  |  |
|  |  | operability |  | pcs | 1 |  | 0.00 |  |
|  |  |  |  |  | TOTAL: |  |  |  | 0.00 |  |
| 7.7 | LIGHTING |  |  |  |  |  |  |
| 7.7.1 | Delivery and mounting flashing items, as per space |  |  |  |  |  |
|  |  | Specification. A set with overall supporting material, |  |  |  |  |  |
|  |  | connection and testing of operability. |  |  |  |  |  |

Page 16

| - | Hanging light |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | type: Philips 40228/11/16/ E27, 70W, type: a | pcs | 10.00 |  | 0.00 |  |
|  | - | LED 1x25W, round bulb, build-in, type: b | pcs | 18.00 |  | 0.00 |  |
| - | Hanging light |  |  |  |  |  |
|  |  | type: PHILIPS 40725/17/16, LED, 6W, type: c | pcs | 6.00 |  | 0.00 |  |
| - | Movement and presence sensor, 100W | pcs | 7.00 |  | 0.00 |  |
|  |  |  |  | TOTAL: |  |  |  | 0.00 |  |
| 7.8 | EMERGENCY LIGHT |  |  |  |  |  |
| 7.8.1 | Delivery and mounting an emergency light with own source |  |  |  |  |  |
|  |  | of voltage in case of interruption of network voltage, with |  |  |  |  |  |
|  |  | 1 hour independent operation. A set with supporting material |  |  |  |  |  |
|  |  | and connection, operational. |  |  |  |  |  |
| - | Emergency light with 6W, LED with inscription "EXIT", with |  |  |  |  |  |
|  |  | own supply for 1 hour | pcs | 8 |  | 0.00 |  |

Page 17

| - | Emergency light with 6W, LED with a direction arrow, with own supply for 1 hour |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | pcs | 1 |  | 0.00 |  |
| 7.8.2 | Delivery and mounting of metal landscaping rails on brackets, |  |  |  |  |  |
|  |  |  | placed on each 30 cm, along the length of the conductor |  |  |  |  |  |
|  |  |  | against the wall and the loft. Partly, the conductor is |  |  |  |  |  |
|  |  |  | placed in plaster cardboard wall and along the attic. |  |  |  | 0.00 |  |
|  |  |  | NYM-J 3x1.5mm² - black | m | 60 |  | 0.00 |  |
|  |  |  |  |  |  | TOTAL: |  |  |  | 0.00 |  |
| 7.9 | Lightning rod |  |  |  |  |  |
| 7.9.1 | Delivery and mounting of hot air galvanised iron band |  |  |  |  |  |
|  |  |  | FeZn 25x4mm for connecting to the joint grounding of GTC | m | 100 |  | 0.00 |  |
| 7.9.2 | Delivery of material and placement of hot air galvanised iron |  |  |  |  |  |
|  |  |  | band FeZn 25x4mm, along an outside wall of the facility to |  |  |  |  |  |
|  |  |  | the test-box | m | 4 |  | 0.00 |  |
| 7.9.3 | Delivery of material and placement of hot air galvanised iron |  |  |  |  |  |
|  |  |  | band 20x3mm, along an outside wall of a test-box | m | 4 |  | 0.00 |  |
| 7.9.4 | Delivery and mounting of cross-pieces, 60x60mm, |  |  |  |  |  |
|  |  |  | connecting the grounding band into the earth, MKS |  |  |  |  |  |
|  |  |  | N.B4.936/3 | pcs | 1 |  | 0.00 |  |
| 7.9.5 | Purchase of material and arranging a measurement spot with a compartment |  |  |  |  |  |
|  |  |  |  | pcs | 2 |  | 0.00 |  |
| 7.9.6 | Delivery of material and placement of hot air galvanised iron band 20x3mm, on fitting roof holders and connection of all |  |  |  |  |  |
|  |  |  | metal roof fittings and all vertical parts. |  |  |  |  |  |
|  |  |  |  | m | 72 |  | 0.00 |  |
| 7.9.7 | Delivery and mounting band holders along the roof |  |  |  |  |  |
|  |  |  | MKS.N.B4 925/C | pcs | 78 |  | 0.00 |  |
| 7.9.8 | Delivery and mounting a gutter clamp MKS.N.B4 908, | pcs | 2 |  | 0.00 |  |
| 7.9.9 | Delivery and mounting a test-box | pcs | 2 |  | 0.00 |  |
|  |  |  |  |  |  | TOTAL: |  |  |  | 0.00 |  |
| 7.10 | FIRE-FIGHTING INSTALLATION |  |  |  |  |  |
| 7.10.1 | Delivery and mounting of addressable fire-fighting |  |  |  |  |  |
|  |  |  | switchboard with min. 2 tabs; LCD display, 3xUSB, 2xRS232 |  |  |  |  |  |
|  |  |  | 20 characters each, 4-16 programming relay exits, with |  |  |  |  |  |
|  |  |  | Ethernet port | pcs | 1.00 |  | 0.00 |  |
| 7.10.2 | Delivery and mounting a manual wall fire alarm device | pcs | 1.00 |  | 0.00 |  |
| 7.10.3 | Delivery and mounting on a wall of an alarm with sound volume of 105dB, 12VDC, for internal installation |  |  |  |  |  |
|  |  |  |  | pcs | 1.00 |  | 0.00 |  |
| 7.10.4 | Delivery and placement of a cable |  |  |  |  |  |
|  |  |  | type: YSTY 2x2x0,80mm2 | m | 80.00 |  | 0.00 |  |
| 7.10.5 | Delivery and placement of a cable |  |  |  |  |  |
|  |  |  | type: NYM-J 3x1, 5mm2 | m | 5.00 |  | 0.00 |  |
| 7.10.6 | Delivery and –mounting of a thermo-differential addressable |  |  |  |  |  |
|  |  |  | fire alarm | pcs | 1.00 |  | 0.00 |  |
| 7.10.7 | Delivery and mounting an optical addressable fire alarm | pcs | 7.00 |  | 0.00 |  |
| 7.10.8 | Testing, programming, putting into operation, submission of |  |  |  | 0.00 |  |
|  |  |  | technical documentation and staff training | pcs | 1 |  |  |  |

Page 18

TOTAL:

7.11 GENERAL POSITIONS

| 7.11.1 Drafting documentation on state of completed works | Pcs | 1.00 |
| --- | --- | --- |

0.00

0.00

Page 19

| TOTAL: | 0.00 |
| --- | --- |

|  |  |  | SUMMARY B |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 7.6 | HIGH-VOLTAGE INSTALLATION AND EQUIPMENT |  |  | 0.00 |  |  |
|  | 7.7 | LIGHTING |  |  | 0.00 |  |  |
|  | 7.8 | EMERGENCY LIGHTING |  |  | 0.00 |  |  |
|  | 7.9 | Lightning rod |  |  | 0.00 |  |  |
|  | 7.10 | FIRE-FIGHTING INSTALLATION |  |  | 0.00 |  |  |
|  | 7.11 | GENERAL POSITIONS |  |  | 0.00 |  |  |
|  |  |  |  | GRAND TOTAL |  |  | 0.00 |  |  |
|  |  |  |  | GRAND TOTAL A+B |  |  | 0.00 |  |  |
|  | 8 | HORTICULTURE |  |  |  |  |  |
|  |  | Preparatory and earth activities |  |  |  |  |  |
|  |  | Drainage layer of light-weight rocks for jardinières, at depth of 10cm, with granulation of 6-14mm, with weight in dry condition of | m3 | 20 |  |  |  |
|  |  | 660 kg/m3 |  |  | 0.00 |  |  |
|  | 8.1 |  |  |  |  |  |  |
|  |  | Transportation of light-weight rocks to the (transportation with a crane) and unloading | m3 | 20 | 0.00 |  |  |
|  | 8.2 |  |  |  |  |  |  |
|  |  | Spreading a drainage layer in jardinières, at depth of 10 cm | m3 | 20 | 0.00 |  |  |
|  | 8.3 |  |  |  |  |  |  |
|  |  | Light mixture for roof jardinières, with weight of 750kg/m3 in | m3 | 200 | 0.00 |  |  |
|  | 8.4 | dry condition |  |  |  |  |  |
|  |  | Transportation of light mixture to the location (transportation with a crane) and unloading. | m3 | 200 | 0.00 |  |  |
|  | 8.5 |  |  |  |  |  |  |
|  |  | Filling jardinières and spreading light mixture | m3 | 200 | 0.00 |  |  |
|  | 8.6 |  |  |  |  |  |  |  |  |
|  |  | Special protective layer for protection of the roof from a root plant | m2 | 550 |  |  |  |
|  |  | system, made of PVC or HDPE, with thickness of 1mm-2.5kg/m2 |  |  | 0.00 |  |  |
|  | 8.7 |  |  |  |  |  |  |
|  |  | Arranging a special protective layer for protection of the roof from | m2 | 550 |  |  |  |
|  |  | a roof system plants, made of PVC or HDPE, with thickness of 1mm, |  |  |  |  |  |
|  |  | by pruning, folding, pasting and bending around gutters, and alike |  |  | 0.00 |  |  |
|  | 8.8 |  |  |  |  |  |  |  |  |
|  |  | Modular system for roof garden, made of polypropylene, at height | m2 | 475 |  |  |  |
|  |  | of 6 cm, minimum repression of 6000 kg/m2 and water |  |  | 0.00 |  |  |
|  |  | permeability of 40 l/m2 and weight not greater than 4 kg/m2 |  |  |  |  |  |
|  | 8.9 |  |  |  |  |  |  |
|  | 8.10 | Geotextile 200 gr./m2 | m2 | 475 | 0.00 |  |  |
|  |  | Arranging a modular system for roof garden, with necessary cut | m2 | 475 | 0.00 |  |  |
|  | 8.11 |  |  |  |  |  |  |
|  |  | Volcanic rock, granulation 7-12 with weight in dry condition of | m3 | 25 | 0.00 |  |  |
|  | 8.12 | 350-430 kg/m3 |  |  |  |  |  |
|  |  | Transportation of volcanic rock to the location (transportation with a crane) and unloading | m3 | 25 | 0.00 |  |  |
|  | 8.13 |  |  |  |  |  |  |
|  | 8.14 | Spreading (filling) of modules with volcanic rocks | m3 | 25 | 0.00 |  |  |
|  |  | Special light mixture for roof garden 750kg/m3 in dry condition | m3 | 170 | 0.00 |  |  |
|  | 8.15 |  |  |  |  |  |  |
|  |  | Transportation of special mixture to the location (transportation with a crane) and unloading | m3 | 170 | 0.00 |  |  |
|  | 8.16 |  |  |  |  |  |  |
|  |  | Spreading a special mixture on a roof, on the top of | m3 | 170 | 0.00 |  |  |
|  | 8.17 | installed modules and volcanic rocks, by planning |  |  |  |  |  |

Page 20

| 8.18 | Ready-made clod grass 30kg/m2 | m2 | 475 |  | 0.00 |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Transportation of clod grass to the location (crane transportation) | m2 | 475 |  | 0.00 |  |
| 8.19 | and unloading |  |  |  |  |  |
| 8.20 | Arranging a ready-made clod grass | m2 | 475 |  | 0.00 |  |

Page 21

|  | Types of nursery plants |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Juniperus virginiana Grey Owl clt 350, volume of habitués 3.5- | pcs | 8 |  | 0.00 |  |
| 8.21 | 4m 110kg/piece |  |  |  |  |  |
|  | Ligustrum texanum ovalifolium clt 50, H=60/80 cm 30kg/piece | pcs | 24 |  | 0.00 |  |
| 8.22 |  |  |  |  |  |  |
| 8.23 | Acer platanoides Globosum clt 285 c 30/35 250kg/piece | pcs | 5 |  | 0.00 |  |
| 8.24 | Agapanthus clt 5 1,5kg/piece | pcs | 170 |  | 0.00 |  |
|  | Juniperus media Old Gold clt.220 volume of habitués 2- | pcs | 5 |  | 0.00 |  |
| 8.25 | 2.5m 95kg/piece |  |  |  |  |  |
| 8.26 | Acer palmatum Bloodgood clt 500, H=5-5.5m 295kg/piece | pcs | 1 |  | 0.00 |  |
| 8.27 | Buxus sempervirens varieagata clt 50 H=50/60 | pcs | 26 |  | 0.00 |  |
|  | Buxus macrophylla Pyramidalis clt 220 H=160-180 | pcs | 2 |  | 0.00 |  |
| 8.28 | 155kg/piece |  |  |  |  |  |
|  | Carpinus betulus Pyramidalis- with earth branches clt 350 H=4- | pcs | 3 |  | 0.00 |  |
| 8.29 | 4.5 m 320kg/piece |  |  |  |  |  |
| 8.30 | Rousmarinus prostratus clt35 25kg/piece | pcs | 12 |  | 0.00 |  |
| 8.31 | Liriope muscari "Monroe Yellow" clt 3 1.5kg/piece | pcs | 368 |  | 0.00 |  |
| 8.32 | Nandina domestica Golf Stream clt 25 H=80+ 15kg/piece | pcs | 30 |  | 0.00 |  |
|  | Cupressus arizonika Fastigiata Aurea clt 50 N=400/450 | pcs | 2 |  | 0.00 |  |
| 8.33 | 75kg./piece |  |  |  |  |  |
| 8.34 | Magnolia Kobus clt 370 c 30/35 | pcs | 4 |  | 0.00 |  |
|  | Picea glauca Globosa clt 130 volume of habitués 2-2.5m | pcs | 8 |  | 0.00 |  |
| 8.35 | 125kg/piece |  |  |  |  |  |
| 8.36 | Daphne blagayana clt 5 3kg/piece | pcs | 240 |  | 0.00 |  |
| 8.37 | Acer rubrum Morgan clt 500 c 35/40 385kg/piece | pcs | 2 |  | 0.00 |  |
| 8.38 | Nassella tenuissima clt 5 | pcs | 312 |  | 0.00 |  |
|  | Taxus baccata fastigiata Aurea clt110 H=170/180 250kg/piece | pcs | 6 |  | 0.00 |  |
| 8.39 |  |  |  |  |  |  |
| 8.40 | Sarcococca hookeriana Humilis clt 5 3kg/piece | pcs | 171 |  | 0.00 |  |
|  | Prunus laurocerasus Otto Luyken clt 50 volume of habitués 1- | pcs | 32 |  | 0.00 |  |
| 8.41 | 1,25 m |  |  |  |  |  |
|  | Photinia fraseri Red robin clt 75 c14/16-tree-like | pcs | 3 |  | 0.00 |  |
| 8.42 | 110kg/piece |  |  |  |  |  |
| 8.43 | Celtis Australi clt.350 c30/35 tree-like 750kg/piece | pcs | 1 |  | 0.00 |  |
|  | Magnolia Grandiflora clt 225 c20/25- tree-like 550 kg/piece | pcs | 1 |  | 0.00 |  |
| 8.44 |  |  |  |  |  |  |
| 8.45 | Hypericum perforatum clt5 3kg/piece | pcs | 25 |  | 0.00 |  |
| 8.46 | Lavandula Officinalis clt5 5kg/piece | pcs | 21 |  | 0.00 |  |
| 8.47 | Acorus gramineus varieagatus clt 3 1.5kg/piece | pcs | 156 |  | 0.00 |  |
| 8.48 | Hypericum patulumclt3 1.5kg/piece | pcs | 48 |  | 0.00 |  |
| 8.49 | Lonicera Pileata clt35 40/60 12kg/piece | pcs | 19 |  | 0.00 |  |
| 8.50 | Photinia fraseri Fire Power clt35 35kg/piece | pcs | 23 |  | 0.00 |  |
|  | Pinus nigra Austriaca clt 350 c=25/30- tree-like 395 kg/piece | pcs | 4 |  | 0.00 |  |
| 8.51 |  |  |  |  |  |  |
|  | Transportation and planting of nursery plants |  |  |  |  |  |
|  | Transportation (elevation) of big-size deciduous nursery plant with | pcs | 15 |  | 0.00 |  |
| 8.52 | a crane and arrangement |  |  |  |  |  |
|  | Transportation (elevation) of big-size evergreen nursery plants with a crane and arrangement | pcs | 5 |  | 0.00 |  |
| 8.53 |  |  |  |  |  |  |
|  | Transportation (elevation) of medium-size evergreen nursery plants with a crane and arrangement | pcs | 28 |  | 0.00 |  |
| 8.54 |  |  |  |  |  |  |
| 8.55 | Transportation (elevation) of shrubs with a crane and arrangement | pcs | 154 |  | 0.00 |  |

Page 22

|  | Transportation (elevation) of small-size shrubs with a crane and | pcs | 1209 |  | 0.00 |  |
| --- | --- | --- | --- | --- | --- | --- |
| 8.56 | arrangement |  |  |  |  |  |
| 8.57 | Planting big-size deciduous nursery plants | pcs | 15 |  | 0.00 |  |
| 8.58 | Planting big-size evergreen nursery plants | pcs | 5 |  | 0.00 |  |
| 8.59 | Planting medium-size evergreen nursery plants | pcs | 28 |  | 0.00 |  |
| 8.60 | Planting shrubs | pcs | 154 |  | 0.00 |  |
| 8.61 | Planting small-size shrubs | pcs | 1209 |  | 0.00 |  |
|  | Green walls and roofs |  |  |  |  |  |
|  | Modules 61x30,5x7cm for green roof with sub-construction for | m2 |  |  |  |  |
|  | mounting and irrigation system and light mixture 75kg/m2 |  | 150 |  | 0.00 |  |
| 8.62 |  |  |  |  |  |  |
| 8.63 | Mounting modules for green roof | m2 | 150 |  | 0.00 |  |
| 8.64 | Sedum SPP 25kg/piece | m2 | 150 |  | 0.00 |  |
|  | Modules for vertical green walls with sub-construction for | m2 | 54 |  | 0.00 |  |
| 8.65 | mounting and water recirculation tank 225kg/piece |  |  |  |  |  |
| 8.66 | Mounting modules for vertical walls | m2 | 54 |  | 0.00 |  |
| 8.67 | Heuchera clt1 1kg/piece | pcs | 324 |  | 0.00 |  |
| 8.68 | Acorus gramineus varieagatus clt 1 1.5kg/piece | pcs | 324 |  | 0.00 |  |
| 8.69 | Hemerocalis Stela D'Oro clt 1 1.5kg/piece | pcs | 324 |  | 0.00 |  |
| 8.70 | Carex spp clt 1 1,5kg/piece | pcs | 324 |  | 0.00 |  |
| 8.71 | Ajuga reptans clt 1 0,5kg/piece | pcs | 324 |  | 0.00 |  |
| 8.72 | Festuca Glauca clt 1 0,5kg/piece | pcs | 324 |  | 0.00 |  |
|  | Other materials |  |  |  |  |  |
| 8.73 | Mulch | Litres | 15000 |  | 0.00 |  |
|  | Maintenance |  |  |  |  |  |
| 8.74 | Full maintenance within guarantee period | Month | 12 |  | 0.00 |  |
|  | Total |  |  |  | 0.00 |  |
| 9 | SPECIFICATION OF PARTS OF IRRIGATION SYSTEM |  |  |  |  |
| 1. HDPE and LDPE HOSES PE 100 |  |  |  |  |  |
| F16 |  | m' | 100 |  | 0.00 |  |
| F40 |  | m' | 100 |  | 0.00 |  |
| F32 |  | m' | 300 |  | 0.00 |  |
| F16 drop |  | m' | 2800 |  | 0.00 |  |
| 2. ELECTROMAGNETIC VALVES |  |  |  |  |  |
| 24 volts 1" flow from 0.24 to 6.8 m3/hour | pcs | 13 |  | 0.00 |  |
| 3. HAND-OPERATED GLOBE VALVES PE AND PVC |  |  |  |  |  |
| PE Manual valve zh-zh 1" x 1" | pcs | 13 |  | 0.00 |  |
| PE Manual valve zh-zh 11/4" x 11/4" | pcs | 1 |  | 0.00 |  |
| 4. PLASTIC MANHOLES FOR EL. VALVES |  |  |  |  |  |
| Round PP manhole for valves 8" | pcs | 3 |  | 0.00 |  |
| Rectangular PP manhole for valves "Jumbo" | pcs | 4 |  | 0.00 |  |
| 5. PE QUICK CONNECTOR |  |  |  |  |  |
| Quick connector 40 x 40 | pcs | 4 |  | 0.00 |  |
| Quick connector 32 x 32 | pcs | 6 |  | 0.00 |  |
| 6. PE CONNECTOR MALE |  |  |  |  |  |
| Male connector 40" x 11/4" | pcs | 2 |  | 0.00 |  |
| Male connector 32" x 1" | pcs | 3 |  | 0.00 |  |
| 7.PE QUICK CONNECTOR |  |  |  |  |  |
| Quick TE connector 40 x 40 x 40 | pcs | 3 |  | 0.00 |  |
| Quick TE connector 32 x 32 x 32 | pcs | 10 |  | 0.00 |  |
| 8. PE STOP |  |  |  |  |  |
| F40 |  | pcs | 4 |  | 0.00 |  |

Page 23

|  | F32 |  | pcs | 20 |  | 0.00 |
| --- | --- | --- | --- | --- | --- | --- |
|  | 9. PE ELBOW |  |  |  |  |
|  | PE Elbow 32 x 32 | pcs | 31 |  | 0.00 |
|  | 10. PE DOUBLE NIPPLE |  |  |  |  |
|  | Nipple 1" x 1" | pcs | 26 |  | 0.00 |
|  | 11. PE UNION |  |  |  |  |
|  | Union 1" x 1" | pcs | 13 |  | 0.00 |
|  | 12. PE GARDENING ELBOW |  |  |  |  |
|  | Gardening elbow 16 x 1/2" | pcs | 50 |  | 0.00 |
|  | Gardening elbow 16 x 16 | pcs | 300 |  | 0.00 |
|  | 13. PE GARDENING EXTENSION |  |  |  |  |
|  | Hose connector drop by drop on main line 16 x 16 | pcs | 200 |  | 0.00 |
|  | Gardening extension 16 x 16 | pcs | 100 |  | 0.00 |
|  | 14.PE TE GARDENING EXTENSION |  |  |  |  |
|  | Gardening TE extension 16 x 16 x 16 | pcs | 200 |  | 0.00 |
|  | 15. PE HOOK HOSE HOLDER DROP BY DROP |  |  |  |  |
|  | Hose holder 16 – 20 | pcs | 2800 |  | 0.00 |
|  | 16.COMMAND AND CONNECTION CABLES FTP |  |  |  |  |
|  | FTP connection cable - waterproof 2 x 1.5 | m' | 150 |  | 0.00 |
|  | Waterproof bit-sockets | pcs | 39 |  | 0.00 |
|  | 17. PRESSURE REGULATORS, RAIN SENSOR |  |  |  |  |
|  | Rain sensor | pcs | 2 |  | 0.00 |
|  | 18. CONTROLLERS AND DECODERS |  |  |  |  |
|  | Decoder - 1 station | pcs | 3 |  | 0.00 |
|  | Decoder - 2 stations | pcs | 2 |  | 0.00 |
|  | Decoder – 4 stations | pcs | 2 |  | 0.00 |
|  | Controller with max.50 lines | pcs | 1 |  | 0.00 |
|  | 19. TEFLON TAPE AND DBI ELEMENTS |  |  |  |  |
|  | Teflon tape 19 x 15 x 0.20 | lump | 60 |  | 0.00 |
|  | Ribbed hose Ø25 for cable protection | m' | 150 |  | 0.00 |
|  | Metal controller box, with padlock | pcs | 1 |  | 0.00 |
|  | 20.COLLARS WITH BOLTS |  |  |  |  |
|  | Collar 40 x 1'' | pcs | 13 |  | 0.00 |
|  | Collar 32 x 1'' | pcs | 13 |  | 0.00 |
|  | Collar 32 x 1/2'' | pcs | 22 |  | 0.00 |
|  | 21. FITTINGS FOR IRRIGATION OF ROOT BALL PBC |  |  |  |  |
|  | PE element for irrigation of root ball, at a height of 45,7 cm | pcs | 44 |  | 0.00 |
|  | 22. INSTALLATION ACTIVITIES |  |  |  |  |
|  | Installation of el. valves with necessary materials | pcs | 13 |  | 0.00 |
|  | Installation and levelling of manholes for the valves | pcs | 4 |  | 0.00 |
|  | Placement and connection of FTP cable | m' | 150 |  | 0.00 |
|  | Placement and connection of F16 | m' | 100 |  | 0.00 |
|  | Placement and connection of drop by drop hose and PE F16 | m' | 2800 |  | 0.00 |
|  | Installation and connection of a controller | pcs | 1 |  | 0.00 |
|  | Installation and connection of rain sensor, with fittings | pcs | 2 |  | 0.00 |
|  | Installation of decoders with IP address | pcs | 7 |  | 0.00 |
|  | SPECIFICATION |  |  |  |  |
|  | 1. HDPE and LDPE HOSES PE 100 |  |  |  |  |
|  | 2. ELECTROMAGNETIC VALVES |  |  |  |  |
|  | 3. HAND-OPERATED GLOBE VALVES PE and PVC |  |  |  |  |
|  | 4. PLASTIC MANHOLES FOR EL. VALVES |  |  |  |  |
|  | 5. PE QUICK CONNECTOR |  |  |  |  |
|  | 6. PE CONNECTOR MAIL |  |  |  |  |
|  | 7. PE TE QUICK CONNECTOR |  |  |  |  |

Page 24

| 8.PE STOP |  |  |  |  |
| --- | --- | --- | --- | --- |
| 9. PE ELBOW |  |  |  |  |
| 10. | PE DOBULE NIPPLE |  |  |  |  |
| 11. | PE UNION |  |  |  |  |
| 12. | PE GARDENNING ELBOW |  |  |  |  |
| 13. | PE GARDENNING EXTENSION |  |  |  |  |
| 14. | PE TE GARDENNING EXTENSION |  |  |  |  |
| 15. PE HOOK HOSE HOLDER DROP BY DROP |  |  |  |  |
| 16. COMMAND AND CONNECTION CABLE FTP |  |  |  |  |
| 17. PRESSURE REGULATOR, RAIN SENSOR |  |  |  |  |
| 18. CONTROLLERS AND DECODERS |  |  |  |  |
| 19. TEFLON TAPE AND DBI ELEMENTS |  |  |  |  |
| 20. COLLARS WITH BOLTS |  |  |  |  |
| 21. METAL FITTINGS FOR IRRIGATION OF ROOT BALL RVS |  |  |  |  |
| 22. INSTALLATION ACTIVITIES |  |  |  |  |
| Total excluding VAT |  |  |  | 0.00 |

Page 25

|  |  | SUMMARY |
| --- | --- | --- |
| 1 | PREPARATORY ACTIVITIES |  |  |  |  | 0.00 |
| 2 | INSULATION ACTIVITIES |  |  |  |  | 0.00 |
| 3 | CONSTRUCTION – CRAFT ACTIVITIES |  |  |  |  | 0.00 |
| 4 | WATER SUPPLY AND DRAINAGE |  |  |  |  | 0.00 |
| 5 | EQUIPMENT |  |  |  |  | 0.00 |
| 6 | FENCES |  |  |  |  | 0.00 |
| 7 | ELECTRICITY |  |  |  |  | 0.00 |
| 8 | HORTICULTURE |  |  |  |  | 0.00 |
| 9 | IRRIGATION SYSTEM |  |  |  |  | 0.00 |
|  | TOTAL: |  |  |  |  | 0.00 |
|  | VAT 18% |  |  |  |  | 0.00 |
|  | GRAND TOTAL: |  |  |  |  | 0.00 |

Page 26