Annex 1

| # | Item to be supplied Description/Specifications | Quantity | Delivery Date |
| --- | --- | --- | --- |
| 1 | Concrete – 3000 psi (20 mPa). 3/8" aggregate footings | 100 cy | Beginning 21 days after issue of PO (see below additional details) |
| 2 | Reinforcing steel – ½” diameter, 40 ksi minimum. | 23,000 lf | 21 days after issue of PO |
| 3 | Reinforcing steel – 5/8” diameter, 40 ksi minimum. | 9,500 lf | 21 days after issue of PO |
| 4 | Concrete Block - nominal 8x8x16”, 2 cells, fc’=1800 psi minimum | 16,500 blocks | Beginning 21 days after issue of PO (see below additional details) |
| 5 | Decorative concrete block (optional selection) | 1000 | Beginning 21 days after issue of PO (see below additional details) |
| 6 | Mortar, Type S, 80 lb. bag. | 550 bags | Beginning 21 days after issue of PO (see below additional details) |
| 7 | Spray Foam Sealer. 3M fire & pest resistant. 16 oz. | 110 cans | 21 days after issue of PO |
| 8 | Grout, non-shrink. 50 lb. | 10 bags | 21 days after issue of PO |
| 9 | J bolts, 5/8x12" with nut and washer | 20 | 21 days after issue of PO |
| 10 | 1 ½” rebar chair -50 pack | 8 | 21 days after issue of PO |
| 11 | 16.5 gage rebar tie wire 400 ft. | 3 | 21 days after issue of PO |

Technical Specifications

Additional Notes and Instructions:

All concrete delivered to the site to be a minimum 20 mPa (3000 pounds per square inch) compressive strength at 28 days  and consist of air entrained   Portland Cement with total air content of not less than 5% and not more than 7% cement content.. Slump not to be more than 4 “no less than ½” as determined by the slump cone test ASTM C-143.

Blocks – 8x8x16 2-cell concrete masonry units.     fm = 1500 psi

Mortar – Portland Cement Type S - fc=1800psi

Reinforcing steel – ½” diameter, 40 ksi minimum.

Reinforcing steel – 5/8” diameter, 40 ksi minimum.

Delivery to the site is to begin 21 days or sooner  following  issuance of PO

Item 1 - Concrete, will be delivered on two separate days as scheduled with the Construction Manager.

Items 2 & 3 - Reinforcing Steel are to be delivered within 21 days following the issuance of the purchase order.

Items 4 & 5 – are delivered to the site beginning within 21 days following the issuance of the purchase order at the rate of 2500 blocks per week.  Item 5 is optional and should only be delivered if requested by the Construction Manager.

Item 6 Mortar – is to be delivered to the site beginning within 21 days of the issuance of the purchase order at the rate of 100 bags per week.

Items 7 -11 are to be delivered within 21 days of the issuance of the purchase order.

Annex 2

FORM FOR SUBMITTING SUPPLIER’S  QUOTATION

(This Form must be submitted only using the Supplier’s Official Letterhead/Stationery)

We, the undersigned, hereby accept in full the UNDP General Terms and Conditions, and hereby offer to supply the items listed below in conformity with the specification and requirements of UNDP as per RFQ Reference No. _______:

TABLE 1 :  Offer to Supply Goods Compliant with Technical Specifications and Requirements

| # | Item to be supplied Description/Specifications | Quantity | Delivery Date | Other Information | Unit Price | Total Cost (USD) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Concrete – 3000 psi (20 mPa). 3/8" aggregate footings | 100 cy | Beginning 21 days after issue of PO, as per Annex I | Price is per cubic yard delivered to the site. |  |  |
| 2 | Reinforcing steel – ½” diameter, 40 ksi minimum. | 23,000 lf | 21 days after issue of PO | Delivered to Site |  |  |
| 3 | Reinforcing steel – 5/8” diameter, 40 ksi minimum. | 9,500 lf | 21 days after issue of PO | Delivered to Site |  |  |
| 4 | Concrete Block - nominal 8x8x16”, 2 cells, fc’=1800 psi minimum | 16,500 blocks | Beginning 21 days after issue of PO, as per Annex I | Delivered to Site |  |  |
| 5 | Decorative concrete block (optional selection) | 1000 | Beginning 21 days after issue of PO, as per Annex I | Delivered to Site |  |  |
| 6 | Mortar, Type S, 80 lb. bag. | 550 bags | Beginning 21 days after issue of PO, as per Annex I | Delivered to Site |  |  |
| 7 | Spray Foam Sealer. 3M fire & pest resistant. 16 oz. | 110 cans | 21 days after issue of PO |  |  |  |
| 8 | Grout, non-shrink. 50 lb. | 10 bags | 21 days after issue of PO | Delivered to Site |  |  |
| 9 | J bolts, 5/8x12" with nut and washer | 20 | 21 days after issue of PO | Delivered to Site |  |  |
| 10 | 1 ½” rebar chair -50 pack | 8 | 21 days after issue of PO |  |  |  |
| 11 | 16.5 gage rebar tie wire 400 ft. | 3 | 21 days after issue of PO |  |  |  |
|  | Shipping to Destination |  |  |  |
|  | Other Charges (Please Specify) |  |  |  |
|  | GRAND TOTAL |  |  | USD |

TABLE 2 : Offer to Comply with Other Conditions and Related Requirements

| Other Information pertaining to our Quotation are as follows : | Your Responses |
| --- | --- |
|  | Yes, we will comply | No, we cannot comply | If you cannot comply, pls. indicate counter proposal |
| Delivery Lead Time |  |  |  |
| Ability to supply all items and specifications indicated in Annex I |  |  |  |
| Country/ies Of Origin: |  |  |  |
| Minimum one (1) year warranty on material |  |  |  |
| Validity of Quotation for 90 days |  |  |  |
| All Provisions of the UNDP General Terms and Conditions |  |  |  |

All other information that we have not provided automatically implies our full compliance with the requirements, terms and conditions of the RFQ.

[Name and Signature of the Supplier’s Authorized Person]

[Designation]

[Date]

This serves as a guide to the Supplier in preparing the quotation and price schedule.

Official Letterhead/Stationery must indicate contact details – addresses, email, phone and fax numbers – for verification purposes

If the country of origin requires Export License for the goods being procured, or other relevant documents that the country of destination may require, the supplier must submit them to UNDP if awarded the PO/contract.