SCOPE OF WORK

The UNDP, Nigeria invites Bids for installation of solar inverter system to the underlisted Schools in Borno State. The schools are:

Izge Secondary School, Izge, Gwoza LGA

(Lat: 11.007778; Long: 13.328333)

The works consist of:

<Preliminary Works>

- Conduct testing of materials

- Pay police regulations and other charges

- Conduct site clearing, setting our and keep progress record and pictures

- Provide access road, site store, temporary fence and sheds, name boards (UNDP Signage) and power source

- Ensure safety and health facilities/regulations

- Provision of ventilation for installation room, storage for rubbish and other requisite facilities

- Ensure security of both human, equipment and material on site.

Installation of Solar Inverter System>

- Supply and install 5KVA/48V sine-wave inverter system

- Provide and install 200AH/12V deep cycle battery

- Provide and install 200W/24V Polycrystalline solar panels

- Provide and install 60A/48V charge controller

- Provide cabling for all components according to technical specification

- Provide for interconnection of ALL UNDP Blocks within the school Premise

- Provide for testing, commissioning and other civil works

<Terms of Payment>

UNDP will pay the contractor/vendor 20% upon signing of contract and submission of required documents (performance bold, warranty, insurance etc), and 80% upon completion of project.

<Warranty Requirement>

UNDP requires the contractor to give a written warranty of 6months on all supplied and installed solar and inverter materials