| Annex-1 Scope of Work and Bill of Quantities |  |  |
| --- | --- | --- |
| CIVIL WORKS |  |  |
| Block: A |  |  |
| Item No. | Description of Works | Quantity | Unit |
| 1.0 | BACK FILLING WITH MECHANICAL COMPACTION |  |  |
|  | Back filling in foundation and sides of foundation with approved soil obtained from the excavation at site and stacked at site or brought from outside in layer not exceeding 15 cm thick (compacted thickness) including transportation of soil, spreading in required line and level, sprinkling water, ramming, compacting with mechanical rammers, testing, etc. to obtain 95% proctor density,all complete as per drawing, specification and instructions of the Consultant. | 105.00 | cu.ft |
| 2.0 | SAND GRAVEL COMPACTION |  |  |
|  | Supplying and laying sand mix gravel (40:60) of required depth over compacted earth including compaction using mechanical compactor. Compaction should be tested for 100 % Proctor Density all complete as per drawing, specification and instruction of the Consultant. The contractor must provide compaction test from the certified laboratory. | 94.18 | cu.ft |

| Item No. | Description of Works | Quantity | Unit |
| --- | --- | --- | --- |
| 3.0 | CONCRETE WORKS |  |  |
| 3.1 | 4inch THICK PCC(1:2:4) FLOORING WITH NOMINAL REINFORCEMENT |  |  |
|  | Providing and laying machine mixed Plain Cement Concrete (1:2:4) cement, sand and 20mm down to 8mm gauge stone aggregate with single layer of 4.75 mm diameter Torkari reinforcement bars placed at 150 mm centres bothways including mixing, laying finishing to approved level, lines and dimensions including necessary centering and shuttering ,all complete as per drawings, specification and instruction of the Consultant. | 188.35 | sq.ft |
| 4.0 | BRICK MASONRY WORK |  |  |
| 4.1 | 9 inch Brickwork in substructure and superstructure. |  |  |
|  | Providing and laying first class in substructure and brickface work in superstructure , "Down Draught Hoffman Kiln" fired local bricks of thickness 9 inch in 12mm thick cement sand mortar (1:4) in foundation and upto plinth level, including cost of soaking of bricks in water, provision for recesses, openings, toothings, scaffolding, curing filling and raking out joints wherever required, all complete as per drawings, specifications and the instruction of site Consultant. | 54.96 | cu.ft |
| 5.0 | FLOORING WORKS |  |  |
| 5.1 | IPC FLOORING (1:2:4) |  |  |
|  | Providing and laying Integrated Plain Concrete ( IPC ) of 50mm thickness on flooring with 1 : 2 : 4 ratio of cement, sand and aggregates (13mm gauge) including 3 mm thick cement punning with (1:1) laid in perfect line and level with proper trowel rubbing/broom finish work to achieve smooth punning like finishing, all complete as per drawings, specifications and the instruction of the Consultant. The depth and pattern of the cement floor finish shall be maintained keeping on the view of the thickness of upcoming floor finish layer. | 188.35 | sq.ft |

| Item No. | Description of Works | Quantity | Unit |
| --- | --- | --- | --- |
| 6.0 | POINTING WORK ON BRICK SURFACE |  |  |
|  | Providing and applying at all levels Pointing Works with white cement based ready to use plaster (Birla plast or squivalent) at face side of brick masonry joint after proper including mixing mortar, laying in perfect line, level and plumb and finishing in regular and even surface. The contractor must clean the facade from all impurities (metals, fungi,graffiti etc.) by using with pressurized water mixed with Aminia ,all complete as per drawings, specification and instruction of the Consultant. | 56.33 | sq.ft |
| 7.0 | WATER REPELLANT SILICON BASED COATING ON BRICK SURFACE |  |  |
|  | Providing and applying approved Water Repellant Coating on Exposed Brick Surface including cleaning brick surface using brick cleaning chemical, single or multi-stage scaffolding, etc. ,all complete as per drawings, specification and instruction of the Consultant. The concentrate should be mixed with water in 1:1 ratio. | 56.33 | sq.ft |
| 8.0 | MS RAILING WORK |  |  |
| 8.1 | MS Railing |  |  |
|  | Providing, fabrication and installation in position MS railing in staircase including cutting to required shape and size, welding joints, installation of base anchor plates of appropriate size with required numbers of expansion bolts of required size, providing required size bends, finishing weld joints to produce smooth surface made of 25x25x2 mm MS square pipe baluster @ 100mm c/c, 38x38x2 mm MS square pipe baluster @ 1050mm c/c , guard rail made of 50x25mmx2 MS rec pipe, 38x38x2 mm square pipe at the bottom rail and 2 layers of 2mm thick 40mm dia. MS pipe Hand rail and 32x4mm flat bar at an interval of 1050mm c/c ,all complete as per drawings, specification and instruction of the Consultant. | 59.00 | r.ft |

| ABSTRACT OF COST - CIVIL WORKS |  |  |
| --- | --- | --- |
| Block: B |  |  |
| Item No. | Description of Works | Quantity | Unit |
| 1.0 | BACK FILLING WITH MECHANICAL COMPACTION |  |  |
|  | Back filling in foundation and sides of foundation with approved soil obtained from the excavation at site and stacked at site or brought from outside in layer not exceeding 15 cm thick (compacted thickness) including transportation of soil, spreading in required line and level, sprinkling water, ramming, compacting with mechanical rammers, testing, etc. to obtain 95% proctor density,all complete as per drawing, specification and instructions of the Consultant. | 57.00 | cu.ft |
| 2.0 | SAND GRAVEL COMPACTION |  |  |
|  | Supplying and laying sand mix gravel (40:60) of required depth over compacted earth including compaction using mechanical compactor. Compaction should be tested for 100 % Proctor Density all complete as per drawing, specification and instruction of the Consultant. The contractor must provide compaction test from the certified laboratory. | 61.91 | cu.ft |

| Item No. | Description of Works | Quantity | Unit |
| --- | --- | --- | --- |
| 3.0 | CONCRETE WORKS |  |  |
| 3.1 | 4inch THICK PCC(1:2:4) FLOORING WITH NOMINAL REINFORCEMENT |  |  |
|  | Providing and laying machine mixed Plain Cement Concrete (1:2:4) cement, sand and 20mm down to 8mm gauge stone aggregate with single layer of 4.75 mm diameter Torkari reinforcement bars placed at 150 mm centres bothways including mixing, laying finishing to approved level, lines and dimensions including necessary centering and shuttering ,all complete as per drawings, specification and instruction of the Consultant. | 92.80 | sq.ft |
| 4.0 | BRICK MASONRY WORK |  |  |
| 4.1 | 9 inch Brickwork in substructure and superstructure. |  |  |
|  | Providing and laying first class in substructure and brickface work in superstructure , "Down Draught Hoffman Kiln" fired local bricks of thickness 9 inch in 12mm thick cement sand mortar (1:4) in foundation and upto plinth level, including cost of soaking of bricks in water, provision for recesses, openings, toothings, scaffolding, curing filling and raking out joints wherever required, all complete as per drawings, specifications and the instruction of site Consultant. | 72.57 | cu.ft |
| 5.0 | FLOORING WORKS |  |  |
| 5.1 | IPC FLOORING (1:2:4) |  |  |
|  | Providing and laying Integrated Plain Concrete ( IPC ) of 50mm thickness on flooring with 1 : 2 : 4 ratio of cement, sand and aggregates (13mm gauge) including 3 mm thick cement punning with (1:1) laid in perfect line and level with proper trowel rubbing/broom finish work to achieve smooth punning like finishing, all complete as per drawings, specifications and the instruction of the Consultant. The depth and pattern of the cement floor finish shall be maintained keeping on the view of the thickness of upcoming floor finish layer. | 109.76 | sq.ft |

| Item No. | Description of Works | Quantity | Unit |
| --- | --- | --- | --- |
| 6.0 | POINTING WORK ON BRICK SURFACE |  |  |
|  | Providing and applying at all levels Pointing Works with white cement based ready to use plaster (Birla plast or squivalent) at face side of brick masonry joint after proper including mixing mortar, laying in perfect line, level and plumb and finishing in regular and even surface. The contractor must clean the facade from all impurities (metals, fungi,graffiti etc.) by using with pressurized water mixed with Aminia ,all complete as per drawings, specification and instruction of the Consultant. | 44.10 | sq.ft |
| 7.0 | WATER REPELLANT SILICON BASED COATING ON BRICK SURFACE |  |  |
|  | Providing and applying approved Water Repellant Coating on Exposed Brick Surface including cleaning brick surface using brick cleaning chemical, single or multi-stage scaffolding, etc. ,all complete as per drawings, specification and instruction of the Consultant. The concentrate should be mixed with water in 1:1 ratio. | 44.10 | sq.ft |
| 8.0 | MS RAILING WORK |  |  |
| 8.1 | MS Railing-Type 1 |  |  |
|  | Providing, fabrication and installation in position MS railing in staircase including cutting to required shape and size, welding joints, installation of base anchor plates of appropriate size with required numbers of expansion bolts of required size, providing required size bends, finishing weld joints to produce smooth surface made of 25x25x2 mm MS square pipe baluster @ 100mm c/c, 38x38x2 mm MS square pipe baluster @ 1050mm c/c , guard rail made of 50x25mmx2 MS rec pipe, 38x38x2 mm square pipe at the bottom rail and 2 layers of 2mm thick 40mm dia. MS pipe Hand rail and 32x4mm flat bar at an interval of 1050mm c/c ,all complete as per drawings, specification and instruction of the Consultant. | 43.67 | r.ft |
| 9.0 | RCC Slab |  |  |
|  | roviding and laying 3" thick slab of ratio (1:1.5:3) with 8mm dia rod of size 31"x 18" with liftin,all complete as per drawings, specification and instruction of the Consultant | 19.00 | nos |

| ABSTRACT OF COST - CIVIL WORKS |  |  |
| --- | --- | --- |
| Block:C |  |  |
| Item No. | Description of Works | Quantity | Unit |
| 1.0 | BACK FILLING WITH MECHANICAL COMPACTION |  |  |
|  | Back filling in foundation and sides of foundation with approved soil obtained from the excavation at site and stacked at site or brought from outside in layer not exceeding 15 cm thick (compacted thickness) including transportation of soil, spreading in required line and level, sprinkling water, ramming, compacting with mechanical rammers, testing, etc. to obtain 95% proctor density,all complete as per drawing, specification and instructions of the Consultant. | 50.00 | cu.ft |
| 2.0 | SAND GRAVEL COMPACTION |  |  |
|  | Supplying and laying sand mix gravel (40:60) of required depth over compacted earth including compaction using mechanical compactor. Compaction should be tested for 100 % Proctor Density all complete as per drawing, specification and instruction of the Consultant. The contractor must provide compaction test from the certified laboratory. | 64.85 | cu.ft |

| Item No. | Description of Works | Quantity | Unit |
| --- | --- | --- | --- |
| 3.0 | CONCRETE WORKS |  |  |
| 3.1 | 4inch THICK PCC(1:2:4) FLOORING WITH NOMINAL REINFORCEMENT |  |  |
|  | Providing and laying machine mixed Plain Cement Concrete (1:2:4) cement, sand and 20mm down to 8mm gauge stone aggregate with single layer of 4.75 mm diameter Torkari reinforcement bars placed at 150 mm centres bothways including mixing, laying finishing to approved level, lines and dimensions including necessary centering and shuttering ,all complete as per drawings, specification and instruction of the Consultant. | 97.19 | sq.ft |
| 4.0 | BRICK MASONRY WORK |  |  |
| 4.1 | 9 inch Brickwork in substructure and superstructure. |  |  |
|  | Providing and laying first class in substructure and brickface work in superstructure , "Down Draught Hoffman Kiln" fired local bricks of thickness 9 inch in 12mm thick cement sand mortar (1:4) in foundation and upto plinth level, including cost of soaking of bricks in water, provision for recesses, openings, toothings, scaffolding, curing filling and raking out joints wherever required, all complete as per drawings, specifications and the instruction of site Consultant. | 76.90 | cu.ft |
| 5.0 | FLOORING WORKS |  |  |
| 5.1 | IPC FLOORING (1:2:4) |  |  |
|  | Providing and laying Integrated Plain Concrete ( IPC ) of 50mm thickness on flooring with 1 : 2 : 4 ratio of cement, sand and aggregates (13mm gauge) including 3 mm thick cement punning with (1:1) laid in perfect line and level with proper trowel rubbing/broom finish work to achieve smooth punning like finishing, all complete as per drawings, specifications and the instruction of the Consultant. The depth and pattern of the cement floor finish shall be maintained keeping on the view of the thickness of upcoming floor finish layer. | 123.79 | sq.ft |

| Item No. | Description of Works | Quantity | Unit |
| --- | --- | --- | --- |
| 6.0 | POINTING WORK ON BRICK SURFACE |  |  |
|  | Providing and applying at all levels Pointing Works with white cement based ready to use plaster (Birla plast or squivalent) at face side of brick masonry joint after proper including mixing mortar, laying in perfect line, level and plumb and finishing in regular and even surface. The contractor must clean the facade from all impurities (metals, fungi,graffiti etc.) by using with pressurized water mixed with Aminia ,all complete as per drawings, specification and instruction of the Consultant. | 51.29 | sq.ft |
| 7.0 | Exterior Acrylic Weather Coat Paint |  |  |
|  | Providing and applying two or more coats of first quality hundred percent exterior acrylic weather coat paint of approved shade and pattern over a coat of weather coat exterior primer to the exterior walls of buildings etc. after proper surface preperation,all complete as per drawings, specifications and the instruction of the Consultant. | 51.29 | sq.ft |
| 8.0 | MS RAILING WORK |  |  |
| 8.1 | MS Railing-Type 1 |  |  |
|  | Providing, fabrication and installation in position MS railing in staircase including cutting to required shape and size, welding joints, installation of base anchor plates of appropriate size with required numbers of expansion bolts of required size, providing required size bends, finishing weld joints to produce smooth surface made of 25x25x2 mm MS square pipe baluster @ 100mm c/c, 38x38x2 mm MS square pipe baluster @ 1050mm c/c , guard rail made of 50x25mmx2 MS rec pipe, 38x38x2 mm square pipe at the bottom rail and 2 layers of 2mm thick 40mm dia. MS pipe Hand rail and 32x4mm flat bar at an interval of 1050mm c/c ,all complete as per drawings, specification and instruction of the Consultant. | 49.08 | r.ft |
| 9.0 | RCC Slab |  |  |
|  | roviding and laying 3" thick slab of ratio (1:1.5:3) with 8mm dia rod of size 31"x 18" with liftin,all complete as per drawings, specification and instruction of the Consultant | 18.00 | nos |

| FOOTPATH RAMPS |
| --- |
| Item No. | Description of Works | Quantity | Unit |
| 1.0 | CONCRETE WORKS |  |  |
| 1.1 | THICK PCC(1:2:4) FLOORING |  |  |
|  | Providing and laying machine mixed Plain Cement Concrete (1:2:4) cement, sand and 20mm down to 8mm gauge stone aggregate including mixing, laying finishing to approved level, lines and dimensions including necessary centering and shuttering ,all complete as per drawings, specification and instruction of the Consultant. | 11.00 | nos |

| FOOTPATH RAMPS |
| --- |
| Item No. | Description of Works | Quantity | Unit |
| 1.0 | Sliding Door |  |  |
|  | Aluminium sliding door and ventilation fixing with 2.5 mm thick aluminium partition panel and 5mm thk glass in Black color on both sides | 70.00 | Sq.Ft |