| Agreed Inv. No. Change Signature and date Orig. Inv. No. | Item Name and specification Type, grade, designation of document or datasheet Code of equipment, product, material Manufacturer Measurement unit Quantity Unit weight, kg Note 1 2 3 4 5 6 7 8 9 Equipment and materials Control and regulation facilities ShSAU #1 (P1 system) Control cabinet VAC-EF-SBD1D 3 D3D350125TeKt (1.5 kW) VKT pcs 1 TE Channel temperature detector NTF-Pt1000 VKT pcs 1 SIC 1z Frequency converter 1.5 kW/380 V VKT pcs 1 PDS Differential-type pressure switch OBM 81-10 VKT pcs 1 PDS Differential-type pressure switch OBM 83-3 VKT pcs 1 TES Overheat protection thermostat TK24 VKT pcs 1 TES Room thermostat RAA20 VKT pcs 1 M Air choke motor GNA 326.1E / 12 Siemens pcs 1 Double-throw switch AC 22 IEK pcs 1 ShSAU #1 (P2 system) Control cabinet VAC-EF-SB (1.74 kW) VKT pcs 1 TE Channel temperature detector NTF-Pt1000 VKT pcs 1 SIC 1z Frequency converter 2.2 kW/380 V VKT pcs 1 PDS Differential-type pressure switch OBM 81-10 VKT pcs 1 PDS Differential-type pressure switch OBM 83-3 VKT pcs 1 TES Overheat protection thermostat TK24 VKT pcs 1 TES Room thermostat RAA20 VKT pcs 1 M Air choke motor GNA 326.1E / 12 Siemens pcs 1 Double-throw switch AC 22 IEK pcs 1 2011-116-02/04 – AOB.C O Central Prison Hospital MPK-15, Turkmenbashi settlement, Mary velayat, Turkmenistan Change Acc. No. Level Document No. Signature Date Prepared by 2012 Department with 50 beds for treatment of MDR patients Level Page Pages total Approved by RP 1 4 Automation. Equipment specifications |
| --- | --- |