INVITATION TO BID

Supply, Installation and connection of minimum 2, maximum 6 Small Scale Wind Turbines with total installed capacity of minimum 21 kW, maximum 24 kW and with one year Operation, Maintenance and Capacity building services for Upper Blinkwater: RMLM: Eastern Cape, South Africa

ITB No.:	65037

Project:	Small Wind Power Integration in the Upper Blinkwater Mini-grid project

Country:	South Africa

Issued on:	14th April 2020

Contents

Section 1. Letter of Invitation	5

Section 2. Instruction to Bidders	8

A. GENERAL PROVISIONS	8

1. Introduction…………………………………………………………………………………………………………………………….………………………….....8

2. Fraud & Corruption, Gifts and Hospitality……………………………………………………………………………………………………………..8

3. Eligibility………………………………………………………………………………………………………………………………………………………………...8

4. Conflict of Interests…………………………………………………………………………………………………………………………………………….….9

B. PREPARATION OF BIDS……………………………………………………………………………………………………………………………………………9

5. GeneralConsiderations…………………………………………………………………………………………………………….……………………….…….9

6. Cost of Preparation of Bid………………………………………………………………………………………..…………………………………….………10

7. Language………………………………………………………………………………………………………………………………………………………….…….10

8. Documents Comprising the Bid……………………………………………………………………………………………………………………….……..10

9. Documents Establishing the Eligibility and Qualifications of the Bidder………………………………………………………………...10

10. Technical Bid Format and Content…………………………………………………………………………………………………………………….….10

11. Price Schedule………………………………………………………………………………………………………………………………………………….……10

12. Bid Security…………………………………………………………………………………………………………………………………………………….……..10

13. Currencies……………………………………………………………………………………………………………………………………………………………..11

14. Joint Venture, Consortium or Association……………………………………………………………………………………………………………..11

15. Only One Bid………………………………………………………………………………………………………………………………………………………….12

16. Bid ValidityPeriod…………………………………………………………………………………………………………………………………………………..12

17. Extension of Bid Validity Period……………………………………………………………………………………………………………………………..12

18. Clarification of Bid (from the Bidders) …………………………………………………………………………………………………………………13

19. Amendment of Bids……………………………………………………………………………………………………………………………………………..13

20. Alternative Bids…………………………………………………………………………………………………………………………………………………....13

21. Pre-Bid Conference………………………………………………………………………………………………………………………………………………13

C. SUBMISSION AND OPENING OF BIDS…………………………………………………………………………………………………...………………..14

22. Submission………………………………………………………………………………………………………………………………………….………………..14

Hard copy (manual) submission…………………………………………………………………………………………………………….…………………14

Email and eTendering submissions…………………………………………………………………………………………………………….…………….14

23. Deadline for Submission of Bids and Late Bids…………………………………………………………………………………………………….14

24. Withdrawal, Substitution, and Modification of Bids……………………………………………………………………………………………..15

25. Bid Opening…………………………………………………………………………………………………………….……………………………………………15

D. EVALUATION OF BIDS. …………………………………………………………………………………………………………….……………………………..15

26. Confidentiality…………………………………………………………………………………………………………….………………………………………..15

27. Evaluation of Bids…………………………………………………………………………………………………………….…………………………………..15

28. Preliminary Examination…………………………………………………………………………………………………………….…………………………16

29. Evaluation of Eligibility and Qualification………………………………………………………………………………………………………….…16

30. Evaluation of Technical Bid and prices…………………………………………………………………………………………………………….…..16

31. Due diligence…………………………………………………………………………………………………………….…………………………………………16

32. Clarification of Bids…………………………………………………………………………………………………………….………………………………..17

33. Responsiveness of Bid…………………………………………………………………………………………………………….……………………………17

34. Nonconformities, Reparable Errors and Omissions……………………………………………………………………………………………..17

E. AWARD OF CONTRACT…………………………………………………………………………………………………………….…………………………….18

35. Right to Accept, Reject, Any or All Bids…………………………………………………………………………………………………………….…18

36. Award Criteria…………………………………………………………………………………………………………….………………………………………..18

37. Debriefing…………………………………………………………………………………………………………….……………………………………………...18

38. Right to Vary Requirements at the Time of Award………………………………………………………………………………………………18

39. Contract Signature…………………………………………………………………………………………………………….…………………………………18

40. Contract Type and General Terms and Conditions………………………………………………………………………………………………18

41. Performance Security…………………………………………………………………………………………………………….……………………………..18

42. Bank Guarantee for Advanced Payment…………………………………………………………………………………………………………….…18

43. Liquidated Damages..………………………………………………………………………………………………………….………………………………..19

44. Payment Provisions…………………………………………………………………………………………………………….……………………………19

45. Vendor Protest…………………………………………………………………………………………………………….…………………………………...19

46. Other Provisions…………………………………………………………………………………………………………….………………………………….19

Section 3. Bid Data Sheet	20

Section 4. Evaluation Criteria	23

Section 5a: Schedule of Requirements and Technical Specifications/Bill of Quantities	32

Section 5b: Other Related Requirements	46

Section 6: Returnable Bidding Forms / Checklist	49

Form A: Bid Submission Form	51

Form B: Bidder Information Form	52

Form C: Joint Venture/Consortium/Association Information Form	54

Form D: Eligibility and Qualification Form	54

Form E: Technical Bid FORMAT	57

# Section 1. Letter of Invitation

The United Nations Development Programme (UNDP) hereby invites you to submit a Bid to this “Invitation to   Bid” (ITB) for the above-referenced subject.

Background and Introduction

The Eastern Cape (EC) Province of South Africa (SA) and the Lower Saxony State of Germany have been engaged in a longstanding twinning partnership arrangement resulting in a mini-grid pilot that was initiated to electrify the small village of Upper Blinkwater (UB) in the Raymond Mhlaba Local Municipality (RMLM).  The village is comprised of approximately 70 households, a school and a church and surrounded by mountains (-32°34'37.59"S, 26°33'26.14"E).  The project represents a model for supplying high quality energy to deep rural villages which are not due to be connected to the national electricity grid in the foreseeable future, providing improved living conditions and economic opportunities for inhabitants. It seeks to demonstrate that even in the absence of a comprehensive power grid, communities can be provided with electricity by relying predominantly on renewable energies. This represents a first of its kind technical and institutional model for rural electrification which, if successful, can be implemented in other rural villages in the region. This holistic village development concept aims to provide much needed socio-economic development opportunities for inhabitants, slowing down rural-urban migration.

With careful attention to the demand requirements of the village, the mini-grid power system was developed and includes a 75 kWp photovoltaic (PV) system, 370 kWh battery storage, and a 40 kW backup diesel generator (400 l diesel storage – all with an integrated vending system, smart meters and demand side management interface.

The EC Government, through the Department of Economic Development, Environmental Affairs and Tourism (DEDEAT), expressed an interest in collaborating with South Africa Wind Energy Project (SAWEP) Phase 2 to add the wind component into the UB mini-grid project. The PV and diesel genset components of the UB project are already at an advanced stage which makes it a win-win situation for SAWEP and the UB project.

SAWEP is supported by the United Nations Development Programme (UNDP) with resources from the Global Environment Facility (GEF), and implemented by the Department of Minerals Resources and Energy (DMRE) and the South African National Energy Development Institute (SANEDI) with a variety of partners: https://sawep.co.za

The addition of preferred locally manufactured small scale wind turbines is a cost-effective and robust manner in support of local industries, which will complement this project with small-scale wind turbines that operate at lower heights than large turbines and where wind speed is not optimal, since the area is mountainous. The Council for Scientific and Industrial Research (CSIR) Energy Centre by virtue of its accumulated technical expertise acquired through the institutionalisation of the Wind Atlas for South Africa (WASA), undertook a six months LIDAR (April to September 2019) wind measurement campaign that was augmented with data of a wind mast installed.  Using the closest proximity nodes from the CSIR wind & PV aggregation study annual wind time series to allow an annual view of the wind resource and in turn using the measure, correlate and predict (MCP) method, facilitated modelling and analysis for the wind turbine installation site wind climate (-32°34'34.88"S, 26°33'7.08"E).  Using the derived wind climate and applying a Feasibility Analysis Matrix informed the specification for this bid.

This contract is for the engineering, procurement, installation, connection to the PV, genset system, testing and commissioning of minimum 2, maximum 6 small scale certified wind turbines with total capacity ranging from 21 kW to 24 kW and with one year of operation, maintenance and capacity building services to the UB community.

The work shall include all labour, materials and equipment necessary to design, install and commission the Works, as well as the maintenance component. All work not expressly called for in this document, but necessary for the complete and proper erection, operation and maintenance of the facility, shall be performed and furnished by the Contractor at no additional cost.

The contract includes Operation & Maintenance (O&M) services for the defects period which is twelve (12) months from the Practical completion date.  During this period, the Client appointed personnel shall be trained by the successful Contractor on how to operate and maintain the wind component facility. The wind component facility shall be commissioned and commercially operating by no later than 5 months from contract signing.  The Contractor will be required to include a detailed project schedule with their submission, to demonstrate how they intend to meet the milestones, hold-points and the COD deadline.

This ITB includes the following documents and the General Terms and Conditions of Contract which is inserted in the Bid Data Sheet:

Section 1: This Letter of Invitation

Section 2: Instruction to Bidders

Section 3: Bid Data Sheet (BDS)

Section 4: Evaluation Criteria

Section 5: Schedule of Requirements and Technical Specifications

Section 6: Returnable Bidding Forms

- Form A: Bid Submission Form

- Form B: Bidder Information Form

- Form C: Joint Venture/Consortium/Association Information Form

- Form D: Qualification Form

- Form E: Format of Technical Bid

- Form F: Price Schedule

If you are interested in submitting a Bid in response to this ITB, please prepare your Bid in accordance with the requirements and procedure as set out in this ITB and submit it by the Deadline for Submission of Bids set out in Bid Data Sheet.

Please acknowledge receipt of this ITB by sending an email to procurement.enquiries@undp.org , indicating whether you intend to submit a Bid or otherwise. You may also utilize the “Accept Invitation” function in eTendering system, where applicable. This will enable you to receive amendments or updates to the ITB. Should you require further clarifications, kindly communicate with the contact person/s identified in the attached Data Sheet as the focal point for queries on this ITB.

UNDP looks forward to receiving your Bid and thank you in advance for your interest in UNDP procurement opportunities.

Issued by 						Approved by:

____________________________				____________________________

| Name: Lerato Maimela Title: Procurement Associate Date: April 14, 2020 | Name: Gabriel Dava Title: Deputy Country Director (Operations) Date: April 14, 2020 |
| --- | --- |

# Section 2. Instruction to Bidders

| GENERAL PROVISIONS |
| --- |
| Introduction | Bidders shall adhere to all the requirements of this ITB, including any amendments made in writing by UNDP. This ITB is conducted in accordance with the UNDP Programme and Operations Policies and Procedures (POPP) on Contracts and Procurement which can be accessed at https://popp.undp.org/SitePages/POPPBSUnit.aspx?TermID=254a9f96-b883-476a-8ef8-e81f93a2b38d Any Bid submitted will be regarded as an offer by the Bidder and does not constitute or imply the acceptance of the Bid by UNDP. UNDP is under no obligation to award a contract to any Bidder as a result of this ITB. UNDP reserves the right to cancel the procurement process at any stage without any liability of any kind for UNDP, upon notice to the bidders or publication of cancellation notice on UNDP website. As part of the bid, it is desired that the Bidder registers at the United Nations Global Marketplace (UNGM) website (www.ungm.org). The Bidder may still submit a bid even if not registered with the UNGM. However, if the Bidder is selected for contract award, the Bidder must register on the UNGM prior to contract signature. |
| Fraud & Corruption, Gifts and Hospitality | UNDP strictly enforces a policy of zero tolerance on proscribed practices, including fraud, corruption, collusion, unethical or unprofessional practices, and obstruction of UNDP vendors and requires all bidders/vendors observe the highest standard of ethics during the procurement process and contract implementation. UNDP’s Anti-Fraud Policy can be found at http://www.undp.org/content/undp/en/home/operations/accountability/audit/office_of_audit_andinvestigation.html#anti Bidders/vendors shall not offer gifts or hospitality of any kind to UNDP staff members including recreational trips to sporting or cultural events, theme parks or offers of holidays, transportation, or invitations to extravagant lunches or dinners. In pursuance of this policy, UNDP: (a) Shall reject a bid if it determines that the selected bidder has engaged in any corrupt or fraudulent practices in competing for the contract in question; (b) Shall declare a vendor ineligible, either indefinitely or for a stated period, to be awarded a contract if at any time it determines that the vendor has engaged in any corrupt or fraudulent practices in competing for, or in executing a UNDP contract. All Bidders must adhere to the UN Supplier Code of Conduct, which may be found at http://www.un.org/depts/ptd/pdf/conduct_english.pdf |
| Eligibility | A vendor should not be suspended, debarred, or otherwise identified as ineligible by any UN Organization or the World Bank Group or any other international Organization. Vendors are therefore required to disclose to UNDP whether they are subject to any sanction or temporary suspension imposed by these organizations. It is the Bidder’s responsibility to ensure that its employees, joint venture members, sub-contractors, service providers, suppliers and/or their employees meet the eligibility requirements as established by UNDP. |
| Conflict of Interests | Bidders must strictly avoid conflicts with other assignments or their own interests, and act without consideration for future work. Bidders found to have a conflict of interest shall be disqualified. Without limitation on the generality of the above, Bidders, and any of their affiliates, shall be considered to have a conflict of interest with one or more parties in this solicitation process, if they: Are or have been associated in the past, with a firm or any of its affiliates which have been engaged by UNDP to provide services for the preparation of the design, specifications, Terms of Reference, cost analysis/estimation, and other documents to be used for the procurement of the goods and services in this selection process; Were involved in the preparation and/or design of the programme/project related to the goods and/or services requested under this ITB; or Are found to be in conflict for any other reason, as may be established by, or at the discretion of UNDP. In the event of any uncertainty in the interpretation of a potential conflict of interest, Bidders must disclose to UNDP, and seek UNDP’s confirmation on whether or not such conflict exists. Similarly, the Bidders must disclose in their Bid their knowledge of the following: If the owners, part-owners, officers, directors, controlling shareholders, of the bidding entity or key personnel who are family members of UNDP staff involved in the procurement functions and/or the Government of the country or any Implementing Partner receiving goods and/or services under this ITB; and All other circumstances that could potentially lead to actual or perceived conflict of interest, collusion or unfair competition practices. Failure to disclose such an information may result in the rejection of the Bid or Bids affected by the non-disclosure. The eligibility of Bidders that are wholly or partly owned by the Government shall be subject to UNDP’s further evaluation and review of various factors such as being registered, operated and managed as an independent business entity, the extent of Government ownership/share, receipt of subsidies, mandate and access to information in relation to this ITB, among others. Conditions that may lead to undue advantage against other Bidders may result in the eventual rejection of the Bid. |
| PREPARATION OF BIDS |
| General Considerations | In preparing the Bid, the Bidder is expected to examine the ITB in detail. Material deficiencies in providing the information requested in the ITB may result in rejection of the Bid. The Bidder will not be permitted to take advantage of any errors or omissions in the ITB. Should such errors or omissions be discovered, the Bidder must notify the UNDP accordingly. |
| Cost of Preparation of Bid | The Bidder shall bear all costs related to the preparation and/or submission of the Bid, regardless of whether its Bid is selected or not. UNDP shall not be responsible or liable for those costs, regardless of the conduct or outcome of the procurement process. |
| Language | The Bid, as well as any and all related correspondence exchanged by the Bidder and UNDP, shall be written in the language (s) specified in the BDS. |
| Documents Comprising the Bid | The Bid shall comprise of the following documents and related forms which details are provided in the BDS: Documents Establishing the Eligibility and Qualifications of the Bidder; Technical Bid; Price Schedule; Bid Security, if required by BDS; Any attachments and/or appendices to the Bid. |
| Documents Establishing the Eligibility and Qualifications of the Bidder | The Bidder shall furnish documentary evidence of its status as an eligible and qualified vendor, using the Forms provided under Section 6 and providing documents required in those forms. In order to award a contract to a Bidder, its qualifications must be documented to UNDP’s satisfaction. |
| Technical Bid Format and Content | The Bidder is required to submit a Technical Bid using the Standard Forms and templates provided in Section 6 of the ITB. Samples of items, when required as per Section 5, shall be provided within the time specified and unless otherwise specified by the Purchaser, at no expense to the UNDP. If not destroyed by testing, samples will be returned at Bidder’s request and expense, unless otherwise specified. When applicable and required as per Section 5, the Bidder shall describe the necessary training programme available for the maintenance and operation of the equipment offered as well as the cost to the UNDP. Unless otherwise specified, such training as well as training materials shall be provided in the language of the Bid as specified in the BDS. When applicable and required as per Section 5, the Bidder shall certify the availability of spare parts for a period of at least five (5) years from date of delivery, or as otherwise specified in this ITB. |
| Price Schedule | The Price Schedule shall be prepared using the Form provided in Section 6 of the ITB and taking into consideration the requirements in the ITB. Any requirement described in the Technical Bid but not priced in the Price Schedule, shall be assumed to be included in the prices of other activities or items, as well as in the final total price. |
| Bid Security | A Bid Security, if required by BDS, shall be provided in the amount and form indicated in the BDS. The Bid Security shall be valid for a minimum of thirty (30) days after the final date of validity of the Bid. The Bid Security shall be included along with the Bid. If Bid Security is required by the ITB but is not found in the Bid, the offer shall be rejected. If the Bid Security amount or its validity period is found to be less than what is required by UNDP, UNDP shall reject the Bid. In the event an electronic submission is allowed in the BDS, Bidders shall include a copy of the Bid Security in their bid and the original of the Bid Security must be sent via courier or hand delivery as per the instructions in BDS. The Bid Security may be forfeited by UNDP, and the Bid rejected, in the event of any, or combination, of the following conditions: If the Bidder withdraws its offer during the period of the Bid Validity specified in the BDS, or; In the event the successful Bidder fails: to sign the Contract after UNDP has issued an award; or to furnish the Performance Security, insurances, or other documents that UNDP may require as a condition precedent to the effectivity of the contract that may be awarded to the Bidder. |
| Currencies | All prices shall be quoted in the currency or currencies indicated in the BDS. Where Bids are quoted in different currencies, for the purposes of comparison of all Bids: UNDP will convert the currency quoted in the Bid into the UNDP preferred currency, in accordance with the prevailing UN operational rate of exchange on the last day of submission of Bids; and In the event that UNDP selects a Bid for award that is quoted in a currency different from the preferred currency in the BDS, UNDP shall reserve the right to award the contract in the currency of UNDP’s preference, using the conversion method specified above. |
| Joint Venture, Consortium or Association | If the Bidder is a group of legal entities that will form or have formed a Joint Venture (JV), Consortium or Association for the Bid, they shall confirm in their Bid that : (i) they have designated one party to act as a lead entity, duly vested with authority to legally bind the members of the JV, Consortium or Association jointly and severally, which shall be evidenced by a duly notarized Agreement among the legal entities, and submitted with the Bid; and (ii) if they are awarded the contract, the contract shall be entered into, by and between UNDP and the designated lead entity, who shall be acting for and on behalf of all the member entities comprising the joint venture. After the Deadline for Submission of Bid, the lead entity identified to represent the JV, Consortium or Association shall not be altered without the prior written consent of UNDP. The lead entity and the member entities of the JV, Consortium or Association shall abide by the provisions of Clause 9 herein in respect of submitting only one Bid. The description of the organization of the JV, Consortium or Association must clearly define the expected role of each of the entities in the joint venture in delivering the requirements of the ITB, both in the Bid and the JV, Consortium or Association Agreement. All entities that comprise the JV, Consortium or Association shall be subject to the eligibility and qualification assessment by UNDP. A JV, Consortium or Association in presenting its track record and experience should clearly differentiate between: Those that were undertaken together by the JV, Consortium or Association; and Those that were undertaken by the individual entities of the JV, Consortium or Association. Previous contracts completed by individual experts working privately but who are permanently or were temporarily associated with any of the member firms cannot be claimed as the experience of the JV, Consortium or Association or those of its members, but should only be claimed by the individual experts themselves in their presentation of their individual credentials JV, Consortium or Associations are encouraged for high value, multi-sectoral requirements when the spectrum of expertise and resources required may not be available within one firm. |
| Only One Bid | The Bidder (including the individual members of any Joint Venture) shall submit only one Bid, either in its own name or as part of a Joint Venture. Bids submitted by two (2) or more Bidders shall all be rejected if they are found to have any of the following: they have at least one controlling partner, director or shareholder in common; or any one of them receive or have received any direct or indirect subsidy from the other/s; or they have the same legal representative for purposes of this ITB; or they have a relationship with each other, directly or through common third parties, that puts them in a position to have access to information about, or influence on the Bid of another Bidder regarding this ITB process; they are subcontractors to each other’s Bid, or a subcontractor to one Bid also submits another Bid under its name as lead Bidder; or some key personnel proposed to be in the team of one Bidder participates in more than one Bid received for this ITB process. This condition relating to the personnel, does not apply to subcontractors being included in more than one Bid. |
| Bid Validity Period | Bids shall remain valid for the period specified in the BDS, commencing on the Deadline for Submission of Bids. A Bid valid for a shorter period may be rejected by UNDP and rendered non-responsive. During the Bid validity period, the Bidder shall maintain its original Bid without any change, including the availability of the Key Personnel, the proposed rates and the total price. |
| Extension of Bid Validity Period | In exceptional circumstances, prior to the expiration of the Bid validity period, UNDP may request Bidders to extend the period of validity of their Bids. The request and the responses shall be made in writing, and shall be considered integral to the Bid. If the Bidder agrees to extend the validity of its Bid, it shall be done without any change to the original Bid. The Bidder has the right to refuse to extend the validity of its Bid, in which case, the Bid shall not be further evaluated. |
| Clarification of Bid (from the Bidders) | Bidders may request clarifications on any of the ITB documents no later than the date indicated in the BDS. Any request for clarification must be sent in writing in the manner indicated in the BDS. If inquiries are sent other than specified channel, even if they are sent to a UNDP staff member, UNDP shall have no obligation to respond or confirm that the query was officially received. UNDP will provide the responses to clarifications through the method specified in the BDS. UNDP shall endeavour to provide responses to clarifications in an expeditious manner, but any delay in such response shall not cause an obligation on the part of UNDP to extend the submission date of the Bids, unless UNDP deems that such an extension is justified and necessary. |
| Amendment of Bids | At any time prior to the deadline of Bid submission, UNDP may for any reason, such as in response to a clarification requested by a Bidder, modify the ITB in the form of an amendment to the ITB. Amendments will be made available to all prospective bidders. If the amendment is substantial, UNDP may extend the Deadline for submission of Bid to give the Bidders reasonable time to incorporate the amendment into their Bids. |
| Alternative Bids | Unless otherwise specified in the BDS, alternative Bids shall not be considered. If submission of alternative Bid is allowed by BDS, a Bidder may submit an alternative Bid, but only if it also submits a Bid conforming to the ITB requirements. Where the conditions for its acceptance are met, or justifications are clearly established, UNDP reserves the right to award a contract based on an alternative Bid. If multiple/alternative bids are being submitted, they must be clearly marked as “Main Bid” and “Alternative Bid” |
| Pre-Bid Conference | When appropriate, a pre-bid conference will be conducted at the date, time and location specified in the BDS. All Bidders are encouraged to attend. Non-attendance, however, shall not result in disqualification of an interested Bidder. Minutes of the Bidder’s conference will be disseminated on the procurement website and shared by email or on the e-Tendering platform as specified in the BDS. No verbal statement made during the conference shall modify the terms and conditions of the ITB, unless specifically incorporated in the Minutes of the Bidder’s Conference or issued/posted as an amendment to ITB. |
| SUBMISSION AND OPENING OF BIDS |
| Submission | The Bidder shall submit a duly signed and complete Bid comprising the documents and forms in accordance with requirements in the BDS. The Price Schedule shall be submitted together with the Technical Bid. Bid can be delivered either personally, by courier, or by electronic method of transmission as specified in the BDS. The Bid shall be signed by the Bidder or person(s) duly authorized to commit the Bidder. The authorization shall be communicated through a document evidencing such authorization issued by the legal representative of the bidding entity, or a Power of Attorney, accompanying the Bid. Bidders must be aware that the mere act of submission of a Bid, in and of itself, implies that the Bidder fully accepts the UNDP General Contract Terms and Conditions. |
| Hard copy (manual) submission | Hard copy (manual) submission by courier or hand delivery allowed or specified in the BDS shall be governed as follows: a) The signed Bid shall be marked “Original”, and its copies marked “Copy” as appropriate. The number of copies is indicated in the BDS. All copies shall be made from the signed original only. If there are discrepancies between the original and the copies, the original shall prevail. (b) The Technical Bid and Price Schedule must be sealed and submitted together in an envelope, which shall: Bear the name of the Bidder; Be addressed to UNDP as specified in the BDS; and Bear a warning not to open before the time and date for Bid opening as specified in the BDS. If the envelope with the Bid is not sealed and marked as required, UNDP shall assume no responsibility for the misplacement, loss, or premature opening of the Bid. |
| Email and eTendering submissions | Electronic submission through email or eTendering, if allowed as specified in the BDS, shall be governed as follows: Electronic files that form part of the Bid must be in accordance with the format and requirements indicated in BDS; Documents which are required to be in original form (e.g. Bid Security, etc.) must be sent via courier or hand delivered as per the instructions in BDS. Detailed instructions on how to submit, modify or cancel a bid in the eTendering system are provided in the eTendering system Bidder User Guide and Instructional videos available on this link: http://www.undp.org/content/undp/en/home/operations/procurement/business/procurement-notices/resources/ |
| Deadline for Submission of Bids and Late Bids | Complete Bids must be received by UNDP in the manner, and no later than the date and time, specified in the BDS. UNDP shall only recognise the actual date and time that the bid was received by UNDP UNDP shall not consider any Bid that is received after the deadline for the submission of Bids. |
| Withdrawal, Substitution, and Modification of Bids | A Bidder may withdraw, substitute or modify its Bid after it has been submitted at any time prior to the deadline for submission. Manual and Email submissions: A bidder may withdraw, substitute or modify its Bid by sending a written notice to UNDP, duly signed by an authorized representative, and shall include a copy of the authorization (or a Power of Attorney). The corresponding substitution or modification of the Bid, if any, must accompany the respective written notice. All notices must be submitted in the same manner as specified for submission of Bids, by clearly marking them as “WITHDRAWAL” “SUBSTITUTION,” or “MODIFICATION” eTendering: A Bidder may withdraw, substitute or modify its Bid by Cancelling, Editing, and re-submitting the Bid directly in the system. It is the responsibility of the Bidder to properly follow the system instructions, duly edit and submit a substitution or modification of the Bid as needed. Detailed instructions on how to cancel or modify a Bid directly in the system are provided in the Bidder User Guide and Instructional videos. Bids requested to be withdrawn shall be returned unopened to the Bidders (only for manual submissions), except if the bid is withdrawn after the bid has been opened. |
| Bid Opening | UNDP will open the Bid in the presence of an ad-hoc committee formed by UNDP of at least two (2) members. The Bidders’ names, modifications, withdrawals, the condition of the envelope labels/seals, the number of folders/files and all other such other details as UNDP may consider appropriate, will be announced at the opening. No Bid shall be rejected at the opening stage, except for late submissions, in which case, the Bid shall be returned unopened to the Bidders. In the case of e-Tendering submission, bidders will receive an automatic notification once the Bid is opened. |
| EVALUATION OF BIDS |
| Confidentiality | Information relating to the examination, evaluation, and comparison of Bids, and the recommendation of contract award, shall not be disclosed to Bidders or any other persons not officially concerned with such process, even after publication of the contract award. Any effort by a Bidder or anyone on behalf of the Bidder to influence UNDP in the examination, evaluation and comparison of the Bids or contract award decisions may, at UNDP’s decision, result in the rejection of its Bid and may subsequently be subject to the application of prevailing UNDP’s vendor sanctions procedures. |
| Evaluation of Bids | UNDP will conduct the evaluation solely on the basis of the Bids received. Evaluation of Bids shall be undertaken in the following steps: Preliminary Examination including Eligibility Arithmetical check and ranking of bidders who passed preliminary examination by price. Qualification assessment (if pre-qualification was not done) Evaluation of Technical Bids Evaluation of prices Detailed evaluation will be focussed on the 3 - 5 lowest priced bids. Further higher priced bids shall be added for evaluation if necessary |
| Preliminary Examination | UNDP shall examine the Bids to determine whether they are complete with respect to minimum documentary requirements, whether the documents have been properly signed, and whether the Bids are generally in order, among other indicators that may be used at this stage. UNDP reserves the right to reject any Bid at this stage. |
| Evaluation of Eligibility and Qualification | Eligibility and Qualification of the Bidder will be evaluated against the Minimum Eligibility/Qualification requirements specified in the Section 4 (Evaluation Criteria). In general terms, vendors that meet the following criteria may be considered qualified: They are not included in the UN Security Council 1267/1989 Committee's list of terrorists and terrorist financiers, and in UNDP’s ineligible vendors’ list; They have a good financial standing and have access to adequate financial resources to perform the contract and all existing commercial commitments, They have the necessary similar experience, technical expertise, production capacity, quality certifications, quality assurance procedures and other resources applicable to the supply of goods and/or services required; They are able to comply fully with the UNDP General Terms and Conditions of Contract; They do not have a consistent history of court/arbitral award decisions against the Bidder; and They have a record of timely and satisfactory performance with their clients. |
| Evaluation of Technical Bid and prices | The evaluation team shall review and evaluate the Technical Bids on the basis of their responsiveness to the Schedule of Requirements and Technical Specifications and other documentation provided, applying the procedure indicated in the BDS and other ITB documents. When necessary, and if stated in the BDS, UNDP may invite technically responsive bidders for a presentation related to their technical Bids. The conditions for the presentation shall be provided in the bid document where required. |
| Due diligence | UNDP reserves the right to undertake a due diligence exercise, aimed at determining to its satisfaction, the validity of the information provided by the Bidder. Such exercise shall be fully documented and may include, but need not be limited to, all or any combination of the following: Verification of accuracy, correctness and authenticity of information provided by the Bidder; Validation of extent of compliance to the ITB requirements and evaluation criteria based on what has so far been found by the evaluation team; Inquiry and reference checking with Government entities with jurisdiction on the Bidder, or with previous clients, or any other entity that may have done business with the Bidder; Inquiry and reference checking with previous clients on the performance on on-going or completed contracts, including physical inspections of previous works, as deemed necessary; Physical inspection of the Bidder’s offices, branches or other places where business transpires, with or without notice to the Bidder; Other means that UNDP may deem appropriate, at any stage within the selection process, prior to awarding the contract. |
| Clarification of Bids | To assist in the examination, evaluation and comparison of Bids, UNDP may, at its discretion, request any Bidder for a clarification of its Bid. UNDP’s request for clarification and the response shall be in writing and no change in the prices or substance of the Bid shall be sought, offered, or permitted, except to provide clarification, and confirm the correction of any arithmetic errors discovered by UNDP in the evaluation of the Bids, in accordance with the ITB. Any unsolicited clarification submitted by a Bidder in respect to its Bid, which is not a response to a request by UNDP, shall not be considered during the review and evaluation of the Bids. |
| Responsiveness of Bid | UNDP’s determination of a Bid’s responsiveness will be based on the contents of the bid itself. A substantially responsive Bid is one that conforms to all the terms, conditions, specifications and other requirements of the ITB without material deviation, reservation, or omission. If a bid is not substantially responsive, it shall be rejected by UNDP and may not subsequently be made responsive by the Bidder by correction of the material deviation, reservation, or omission. |
| Nonconformities, Reparable Errors and Omissions | Provided that a Bid is substantially responsive, UNDP may waive any non-conformities or omissions in the Bid that, in the opinion of UNDP, do not constitute a material deviation. UNDP may request the Bidder to submit the necessary information or documentation, within a reasonable period, to rectify nonmaterial nonconformities or omissions in the Bid related to documentation requirements. Such omission shall not be related to any aspect of the price of the Bid. Failure of the Bidder to comply with the request may result in the rejection of its Bid. For the bids that have passed the preliminary examination, UNDP shall check and correct arithmetical errors as follows: if there is a discrepancy between the unit price and the line item total that is obtained by multiplying the unit price by the quantity, the unit price shall prevail and the line item total shall be corrected, unless in the opinion of UNDP there is an obvious misplacement of the decimal point in the unit price; in which case, the line item total as quoted shall govern and the unit price shall be corrected; if there is an error in a total corresponding to the addition or subtraction of subtotals, the subtotals shall prevail and the total shall be corrected; and if there is a discrepancy between words and figures, the amount in words shall prevail, unless the amount expressed in words is related to an arithmetic error, in which case the amount in figures shall prevail. If the Bidder does not accept the correction of errors made by UNDP, its Bid shall be rejected. |
| AWARD OF CONTRACT |
| Right to Accept, Reject, Any or All Bids | UNDP reserves the right to accept or reject any bid, to render any or all of the bids as non-responsive, and to reject all Bids at any time prior to award of contract, without incurring any liability, or obligation to inform the affected Bidder(s) of the grounds for UNDP’s action. UNDP shall not be obliged to award the contract to the lowest priced offer. |
| Award Criteria | Prior to expiration of the period of Bid validity, UNDP shall award the contract to the qualified and eligible Bidder that is found to be responsive to the requirements of the Schedule of Requirements and Technical Specification, and has offered the lowest price. |
| Debriefing | In the event that a Bidder is unsuccessful, the Bidder may request for a debriefing from UNDP. The purpose of the debriefing is to discuss the strengths and weaknesses of the Bidder’s submission, in order to assist the Bidder in improving its future Bids for UNDP procurement opportunities. The content of other Bids and how they compare to the Bidder’s submission shall not be discussed. |
| Right to Vary Requirements at the Time of Award | At the time of award of Contract, UNDP reserves the right to vary the quantity of goods and/or services, by up to a maximum twenty-five per cent (25%) of the total offer, without any change in the unit price or other terms and conditions. |
| Contract Signature | Within fifteen (15) days from the date of receipt of the Contract, the successful Bidder shall sign and date the Contract and return it to UNDP. Failure to do so may constitute sufficient grounds for the annulment of the award, and forfeiture of the Bid Security, if any, and on which event, UNDP may award the Contract to the Second highest rated or call for new Bids. |
| Contract Type and General Terms and Conditions | The types of Contract to be signed and the applicable UNDP Contract General Terms and Conditions, as specified in BDS, can be accessed at http://www.undp.org/content/undp/en/home/procurement/business/how-we-buy.html |
| Performance Security | A performance security, if required in the BDS, shall be provided in the amount specified in BDS and form available at https://popp.undp.org/_layouts/15/WopiFrame.aspx?sourcedoc=/UNDP_POPP_DOCUMENT_LIBRARY/Public/PSU_Solicitation_Performance%20Guarantee%20Form.docx&action=default within a maximum of fifteen (15) days of the contract signature by both parties. Where a performance security is required, the receipt of the performance security by UNDP shall be a condition for rendering the contract effective. |
| Bank Guarantee for Advanced Payment | Except when the interests of UNDP so require, it is UNDP’s standard practice to not make advance payment(s) (i.e., payments without having received any outputs). If an advance payment is allowed as per the BDS, and exceeds 20% of the total contract price, or USD 30,000, whichever is less, the Bidder shall submit a Bank Guarantee in the full amount of the advance payment in the form available at https://popp.undp.org/_layouts/15/WopiFrame.aspx?sourcedoc=/UNDP_POPP_DOCUMENT_LIBRARY/Public/PSU_Contract%20Management%20Payment%20and%20Taxes_Advanced%20Payment%20Guarantee%20Form.docx&action=default |
| Liquidated Damages | If specified in the BDS, UNDP shall apply Liquidated Damages for the damages and/or risks caused to UNDP resulting from the Contractor’s delays or breach of its obligations as per Contract. |
| Payment Provisions | Payment will be made only upon UNDP's acceptance of the goods and/or services performed. The terms of payment shall be within thirty (30) days, after receipt of invoice and certification of acceptance of goods and/or services issued by the proper authority in UNDP with direct supervision of the Contractor. Payment will be effected by bank transfer in the currency of the contract. |
| Vendor Protest | UNDP’s vendor protest procedure provides an opportunity for appeal to those persons or firms not awarded a contract through a competitive procurement process. In the event that a Bidder believes that it was not treated fairly, the following link provides further details regarding UNDP vendor protest procedures: http://www.undp.org/content/undp/en/home/procurement/business/protest-and-sanctions.html |
| Other Provisions | In the event that the Bidder offers a lower price to the host Government (e.g. General Services Administration (GSA) of the federal government of the United States of America) for similar goods and/or services, UNDP shall be entitled to the same lower price. The UNDP General Terms and Conditions shall have precedence. UNDP is entitled to receive the same pricing offered by the same Contractor in contracts with the United Nations and/or its Agencies. The UNDP General Terms and Conditions shall have precedence. The United Nations has established restrictions on employment of (former) UN staff who have been involved in the procurement process as per bulletin ST/SGB/2006/15 http://www.un.org/en/ga/search/view_doc.asp?symbol=ST/SGB/2006/15&referer |

# Section 3. Bid Data Sheet

The following data for the goods and/or services to be procured shall complement, supplement, or amend the provisions in the Invitation to Bid In the case of a conflict between the Instructions to Bidders, the Bid Data Sheet, and other annexes or references attached to the Bid Data Sheet, the provisions in the Bid Data Sheet shall prevail.

| BDS No. | Ref. to Section.2 | Data | Specific Instructions / Requirements |
| --- | --- | --- | --- |
| 1 | 7 | Language of the Bid | English |
| 2 |  | Submitting Bids for Parts or sub-parts of the Schedule of Requirements (partial bids) | Not Allowed |
| 3 | 20 | Alternative Bids | Shall not be considered |
| 4 | 21 | Pre-Bid conference | Will NOT be Conducted |
| 5 | 16 | Bid Validity Period | 90 days |
| 6 | 13 | Bid Security | Not Required |
| 7 | 41 | Advanced Payment upon signing of contract | Not Allowed |
| 8 | 42 | Liquidated Damages | Will be imposed as follows: 0.5 % of contract for every day of delay, up to a maximum duration of 1 calendar month. Thereafter, the contract may be terminated. |
| 9 | 40 | Performance Security | Not Required |
| 10 | 12 | Currency of Bid | United States Dollar or South African Rands |
| 11 | 31 | Deadline for submitting requests for clarifications/ questions | 5 WORKING days before the submission deadline |
| 12 | 31 | Contact Details for submitting clarifications/questions | Focal Person in UNDP: Lerato Maimela E-mail address: procurement.enquiries@undp.org; lerato.maimela@undp.org |
| 13 | 18, 19 and 21 | Manner of Disseminating Supplemental Information to the ITB and responses/clarifications to queries | Direct communication to prospective Proposers by email and Posting on the website: https://eur03.safelinks.protection.outlook.com/?url=http%3A%2F%2Fprocurement-notices.undp.org%2F&amp;data=02%7C01%7Clerato.maimela%40undp.org%7Cd178a00050c34a4b62b308d768096e10%7Cb3e5db5e2944483799f57488ace54319%7C0%7C0%7C637092262017360232&amp;sdata=nZjIN%2Bzl%2BFCh9StGijDN%2Faue4ZbyrYwN02E%2Fd8QTjVE%3D&amp;reserved=0 |
| 14 | 23 | Deadline for Submission | 12h00 midday 08th May 2020 South African Time |
| 14 | 22 | Allowable Manner of Submitting Bids | ☒ Courier/Hand Delivery ☒ Submission by email ☐ e-Tendering |
| 15 | 22 | Bid Submission Address | bid.pretoria@undp.org 351 Francis Baard Street, Metropark Building, Pretoria, 0001. |
| 16 | 22 | Electronic submission (email or eTendering) requirements | Format: PDF files only File names must be maximum 60 characters long and must not contain any letter or special character other than from Latin alphabet/keyboard. All files must be free of viruses and not corrupted. Max. File Size per transmission: 10MB Documents which are required in original (e.g. Bid Security) should be sent to the below address with a PDF copy submitted as part of the electronic submission: UNDP 351 Francis Baard Street, Metropark Bld, Pretoria, 0001. |
| 17 | 25 | Date, time and venue for the opening of bid | Date and Time: April 27, 2020 12:00 AM Venue: UNDP, 351 Francis Baard Str, METROPARK bld, Pretoria |
| 18 | 27, 36 | Evaluation Method for the Award of Contract | Lowest priced technically responsive, eligible and qualified bid. |
| 19 |  | Estimated date for commencement of Contract | June 1, 2020 |
| 20 |  | Maximum expected duration of contract | The wind turbines shall be commissioned and commercially operating by no later than 5 months from contract signature followed by one year defects period including Operation, Maintenance and Capacity building services. |
| 21 | 35 | UNDP will award the contract to: | One Proposer Only |
| 22 | 39 | Type of Contract | Contract for Goods and/or Services to UNDP http://www.undp.org/content/undp/en/home/procurement/business/how-we-buy.html |
| 23 | 39 | UNDP Contract Terms and Conditions that will apply | UNDP General Terms and Conditions for Works http://www.undp.org/content/undp/en/home/procurement/business/how-we-buy.html |
| 24 |  | Other Information Related to the ITB | [All other instructions and information not yet mentioned so far in this Data Sheet but are relevant to the ITB must be cited here, and any further entries that may be added below this table row] |

# Section 4. Evaluation Criteria

Preliminary Examination Criteria

Bids will be examined to determine whether they are complete and submitted in accordance with ITB requirements as per below criteria on a Yes/No basis:

- Appropriate signatures

- Power of Attorney

- Minimum Bid documents provided

- Bid Validity

- Bid Security (if required) submitted as per ITB requirements with compliant validity period

Minimum Eligibility and Qualification Criteria

Eligibility and Qualification will be evaluated on a Pass/Fail basis.

If the Bid is submitted as a Joint Venture/Consortium/Association, each member should meet the minimum criteria, unless otherwise specified.

| Subject | Criteria | Document Submission requirement |
| --- | --- | --- |
| ELIGIBILITY |  |  |
| Legal Status | Vendor is a legally registered entity. | Form B: Bidder Information Form |
| Eligibility | Vendor is not suspended, nor debarred, nor otherwise identified as ineligible by any UN Organization or the World Bank Group or any other international Organization in accordance with ITB clause 3. | Form A: Bid Submission Form |
| Conflict of Interest | No conflicts of interest in accordance with ITB clause 4. | Form A: Bid Submission Form |
| Bankruptcy | Has not declared bankruptcy, is not involved in bankruptcy or receivership proceedings, and there is no judgment or pending legal action against the vendor that could impair its operations in the foreseeable future. | Form A: Bid Submission Form |
| Certificates and Licenses | Duly authorized to act as Agent on behalf of the Manufacturer, or Power of Attorney, if bidder is not a manufacturer Official appointment as local representative, if Bidder is submitting a Bid on behalf of an entity located outside the country Patent Registration Certificates, if any of technologies submitted in the Bid is patented by the Bidder Export/Import Licenses, if applicable | Form B: Bidder Information Form |
|  | Provide valid manufacturers guarantees and warranties for all materials and products supplied according to the required warranty periods defined in the table below. Description Years Warranty Wind Turbine Generator 5( with possibility to extend) Tower 5( with possibility to extend) Workmanship 1 Midnite Classic MPPT Charge Controller/ wind turbine manufacturer recommended Charge Controller 5 (with possibility to extend) The Contractor shall provide valid manufacturers' guarantees and warranties for all materials and products supplied according to the required warranty periods defined in Table 1. The Contractor shall ensure that the conditions of delivery, storage, installation and use of materials and products are such that they remain under guarantee for the maximum period as specified by the manufacturers. The Contractor shall ensure any maintenance required by the Supplier is provided before Practical completion and that full records are kept and included in the O&M Manuals prior to Practical completion. The risks as well as the expenses of conditioning and shipping back of the defective parts or products will be borne by the Contractor during the Defects Period. All warranties and guarantees shall be passed on to the Client Representative upon transfer of ownership of the Facility. Furthermore, all documents necessary to ensure the enforcement of the warranties and guarantees are to be supplied by The Contractor to the Client Representative on Final Completion. The wind turbine must have a valid and applicable certification to SABS or international accepted standard e.g. USA (SWCC), UK (MCS) etc. Insurance The Contractor shall ensure that adequate insurance is in place to cover the value and consequential losses due to accident, theft or fire of the materials and equipment stored onsite and that no materials or equipment in excess of this limit are stored on site at any given time. Health and Safety All construction for this project must be completed in accordance with the occupational Health and Safety Act 85 of 1993. Civils The Contractor shall: provide valid manufacturers' guarantees and warranties for all materials and products supplied. take the utmost care to minimise the impact of his establishment and other construction activities on the environment. submit a Method Statement to the employer detailing his construction activities and what measures will be implemented to prevent the pollution. contact the employer as early as possible, and program for the execution of the works. only dump excess or unsuitable materials at sites, which have been authorized for that purpose by the Client Representative include full compensation in costing for all work necessary for the clearing of the surface in preparation for the construction of the Works. Electrical Systems and Distribution Boards The Contractor shall abide by the Electrical Installation Regulation of 2009 (EIR) which prescribes in subclause 7(1) that every user of an electrical installation SHALL have a valid certificate of compliance (CoC) for every such installation, and 7(4) requires that the same user obtains (at least) an additional CoC for any change and alteration to that installation in order to keep the CoC current and valid. The Contractor also requires in subclause 6(1) that anyone doing electrical installation work as a Contractor be so registered, and in subclause 5(1) work may only be done in accordance with the prescribed safety standard (SANS 10142-1), and no person may allow otherwise, and subclause 9(4) requires that a valid CoC be issued for all such work. All equipment and services supplied shall comply with the standards listed below. General Grid Connection Code for Renewable Power Plants (RPPs) Connected To the Electricity Transmission System (Ts) or the Distribution System (Ds) In South Africa Version 2.6 November 2012 Standard Conditions for Embedded Generation within Municipal Boundaries Version September 2011 South African Grid Code Network Version 8.0 July 2010 SANS 10142-1:2009: The wiring of premises Part 1: Low-voltage installations SANS 10142-2:2009: The wiring of premises Part 2: Medium- voltage installations above 1kV ac not exceeding 22kV ac and up to and including 3000kW installed capacity SANS 10142-3:2018: National Standard for Small Scale Embedded Generation installations IEC 60364-4-41: Low-voltage plants installation. Part 4-41 - Protection for safety — protection against shock IEC 60364-7-712: Electrical installations of buildings Part 7-712 - Requirements for special installations or locations Solar photovoltaic (PV) power supply systems Electrical Cabling SANS 1507 Part 1: General, Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V) SANS 1507 Part 2: Wiring Cables, Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V) SANS 1507 Part 3: PVC Distribution, Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V) SANS 1507 Part 4: XLPE Distribution Cables, Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V) SANS 1507 Part 5: halogen-free Distribution Cables, „Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V) SANS 10198 Parts 1-14: 2004 The selection, handling and installation of electric power cables of rating not exceeding 33 kV Part 1 to 14 Metering The South African Grid Code Electricity Act 41 of 1987 Electricity Regulation Act, 2006 IEC 60051-1 Direct acting indicating analogue electrical measuring instruments and their accessories - definitions and general requirements common to all parts IEC 61036 Alternating current static watt-hour meters for active energy IEC 62053 Electricity metering equipment (A.C.) - particular requirements IEC 62056 Electricity metering – Data exchange for meter reading, tariff and local control NRS 057/ SANS 474 Code of practice for electricity metering LV Distribution IEC 60269 Low-Voltage fuses IEC 60898 Electrical accessories - circuit breakers for overcurrent protection for household and similar installations IEC 61009 Residual current operated circuit-breakers with integral overcurrent protection for household and similar uses (RCBO's) Earthing NRS 097-2-1:2017 Section 4.2.6 NRS 097-2-1:2017 ANNEX B SANS 10292:2001 Earthing of low-voltage (LV) distribution systems Controls and Monitoring The control and performance monitoring system has been supplied in the solar installation portion of this project. Environmental The Contractor shall be responsible for identifying and complying with all environmental legal and other requirements applicable to the design, construction and operation of the Works. Commissioning The Contractor should inspect, test, commission and execute a performance test of the Works on site to demonstrate compliance with the Contract documents. Testing and Acceptance Testing and Acceptance includes the following Acceptance Tests: Mechanical Completion Test Mini-Grid Connection Test Practical Completion Test Final Completion Test The Contractor shall: Ensure that he employs suitably qualified professionals with appropriate accreditation to carry out The Acceptance Tests with an appropriate grade for the work. Ensure the supervising commissioning engineer has a minimum of 3 years' experience in the commissioning and performance testing of similar installations. Supply regime of tests 1 month prior to construction including pre-requisites, methodology, stopping and restarting procedure and instrumentation. Mechanical completion test When the Contractor has completed the Mechanical Completion Test of the Works successfully, then the Client Representative will issue the Mechanical Completion Certificate in which case mechanical completion will have occurred. The Contractor shall undertake the following: General Verify all parts of the Works are in line with approved Final Design Verify the Works is according to provisions of the Contract Verify all equipment and parts have been installed according to their manufacturer's Installation Manuals Verify all Safety Labels have been erected according to the Contract Wind Turbines Inspect wind turbines as installed and verify absence of any breakages or any signs of incorrect or incomplete installation Verify the wind turbine optimal operation arrangement Cabling Verify that all cables have been marked and numbered according to Contract and in line with respective Cable Schedules Check cable Pulling Test records Inspect DC cabling between wind turbines and verify that cable types, sizes and lengths as well as cable connector types are in accordance with the Contract Verify integrity of Surge Protection Devices and all earthing connections Inspect the Voltage Test records for completeness and validity of recorded measurements Inspect Insulation Test records on all cables and circuits Turbine tower structures Verify correct orientation and alignment of towers Verify overall set-out distances, surfacing, alignment and completeness of the assembly Verify that all cables and switches have been marked and numbered according to Contract and in line with respective Cable Schedules Inspect cable pulling test records Inspect all DC & AC cabling and verify that cable types, sizes and lengths are in accordance with the Contract and in line with respective Cable Schedules Verify all inverter parameters are set up within Manufacturer's recommendations and local regulations Verify that all cables and switches have been marked and numbered according to Contract and in line with respective Cable Schedules Inspect cable Pulling Test records Inspect AC cabling and switches and verify that types, sizes and lengths are in accordance with the Contract and in line with respective Schedules Verify Voltage Controls Inspect Insulation Test records on all cables and circuits Data acquisition system The Contractor shall provide the following: Verify all system components and respective electrical and data connections are according to provisions of Contract Verify broadband equipment and connections All the certifications and tests on components necessary for the Mechanical Completion Certificate All "Construction Issue" drawings and design documents Tools and Instrumentation for operation and maintenance of The Facility: Multimeter Ohmmeter for the earthing resistor measurement and all insulation testing Calibrator DC and AC current clamps Mini-Grid Connection Test The Contractor should Adhere to: SANS 10142-1-2: Section 8.3 Testing - Test Report for All Electrical Installations SAGC for VRE power plants Rev 2.9 - Testing and Compliance Monitoring Practical Completion Test The Practical completion Test shall take place once Mechanical Completion and the Grid Connection Tests have occurred and will be finalized by the issuance of a Practical completion Certificate in which case Practical completion will have occurred. The Contractor should confirm practical completion of: LV mini-grid, communications network and smart DB boards Protection device Alarms and signaling Monitoring and Data Acquisition Systems In the event of disruption of the Test due to Force Majeure, such as theft, vandalism or Grid failure, the test will be suspended and restarted. The Confirmed Provisional Performance Ratio estimate can take into account the deviation of the actual operating conditions of the plant from reference conditions STC (standard test condition). The "unexpected" down time of the system during the PAT period has to be zero. Final Completion Test The test period will commence from the date of practical completion until the issuance the final completion certificate, after which Final Completion will be deemed to have occurred. During the Final Completion Test the Contractor shall maintain an agreed upon % availability. In the event of disruption of the Test due to Force Majeure, such as theft, vandalism or Grid failure, the respective data will be disregarded. Before commencing the Contractor shall submit their proposed test protocol to the Client Representative for review and approval. The Test will then be conducted in accordance to the test protocol approved by the Client Representative. Performance during operation In order to ensure the proper operation of the Works, the Contractor shall provide equipment to continuously monitor and document the relevant conditions of the Plant at regular intervals by means of remote monitoring, data assessment and, if applicable, processing of malfunction messages. The monitoring system should also record consumption and be able to identify potential theft of electricity. Operation and Maintenance The Contractor shall provide all materials, consumables and, equipment required to maintain the system to achieve the required service life. Note that as part of the operation and maintenance portion of the quotation, provision must be made for capacity building within the RMLM to allow for long term operation and maintenance of the project. The Contractor shall discuss and agree with the Client Representative and submit an Operations and Maintenance Strategy for the Works for the Defects Period (first one year of operation) to include: Proposals for maintaining the Works in order to achieve the required service life and the required Performance Ratio and to demonstrate compliance with manufacturers' minimum maintenance requirements for respective warranty covers Proposals for monitoring the Works and maintaining the monitoring equipment over the life of the project Proposals for responding to emergencies, plant malfunctions, security breaches and notifications of restricted operation from the Client Representative. The Contractor shall be responsible for the operation and running maintenance / upkeep as well as technical operational management of the Works during the Defects Period, maintaining proper functioning of the Works with regards to availability and functionality and performance. The operation and maintenance activities performed and the repair activities supervised by the Contractor shall always and fully comply with all current requirements of: the applicable law, regulations and technical and safety standards the permitting authorities the grid operator the suppliers under their warranty/extension-of-warranty conditions the insurer In the scope of operational management, the Contractor shall assume the tasks which are necessary to ensure the trouble-free operation of the plant, that is, the provision of the technical activities rendered at the Works, such as supervision of the operating conditions, intervention in the event of extraordinary situations to prevent malfunctions and management of the systems. The Contractor shall undertake to perform the regularly scheduled inspect' on and periodic maintenance of the Works in conformity with the specifications of the component manufacturers as well as the coordination and monitoring of repairs (including repairs performed under the Factory Warranties of the suppliers). |  |
| QUALIFICATION |  |  |
| History of Non-Performing Contracts | Non-performance of a contract did not occur as a result of contractor default for the last 3 years. | Form D: Qualification Form |
| Litigation History | No consistent history of court/arbitral award decisions against the Bidder for the last 3 years. | Form D: Qualification Form |
| Previous Experience | Minimum 5 years of relevant experience. | Form D: Qualification Form |
|  | Minimum 3 contracts of similar value, nature and complexity implemented over the last 5years. (For JV/Consortium/Association, all Parties cumulatively should meet requirement). | Form D: Qualification Form |
| Financial Standing | Minimum average annual turnover of USD170k for the last 3 years. (For JV/Consortium/Association, all Parties cumulatively should meet requirement). | Form D: Qualification Form |
|  | Bidder must demonstrate the current soundness of its financial standing and indicate its prospective long-term profitability. (For JV/Consortium/Association, all Parties cumulatively should meet requirement). | Form D: Qualification Form |
| Technical Evaluation | The technical bids shall be evaluated on a pass/fail basis for compliance or non-compliance with the technical specifications identified in the bid document. | Form E: Technical Bid Form |
| Financial Evaluation | Detailed analysis of the price schedule based on requirements listed in Section 5 and quoted for by the bidders in Form F. Price comparison shall be based on the landed price, including transportation, insurance and the total cost of ownership (including spare parts, consumption, installation, commissioning, training, special packaging, etc., where applicable) Comparison with budget/internal estimates. | Form F: Price Schedule Form |

# Section 5a: Schedule of Requirements and Technical Specifications/Bill of Quantities

The company will be responsible for full civils and installation of the below indicated Equipment, capacity building during the Operation and Maintenance period of one year after the period of installation.

| Items to be Supplied | Quantity | Description / Specifications of Goods | Latest Delivery Date to site |
| --- | --- | --- | --- |
|  | Per turbine | Wind Generator: Rated Power: 2,500 – 10,400 Watt (at 11 m/s, standard sea-level conditions.) Rated annual energy 3,900 – 16,700 kWh (Estimated annual energy production assuming an annual average wind speed of 5 m/s (11.2 mph), a Rayleigh wind speed distribution, sea-level air density and 100% availability.) Rated Sound Level: 50 dB – 60 dB Start-Up Wind Speed: ~ 3.25 m/s Cut-out wind speed: 45 m/s (IEC wind turbine Class II extreme wind speed of 42.5 m/s and a minimum of a 20 year service life) Output Guarantee of 80% peak power, 95% availability Output Voltage: 48 Vdc or 110 Vdc Overspeed protection: Proposed Pitch Control Number of blades 3 Blade material: fibre glass Minimum 5 years Warranty - extendable Drive type: direct (no gearbox) Generator type: permanent magnet Control system: electronic Production (all wind turbines: min 2, max 6, min 21 kW, max 24 kW): projected AEP >= 20 MWh | Up to 2 months after signing of contract |
|  | Per turbine | Wind Generator Mast: Approximately 18 m in length, hot-dip galvanized, tapered, monopole. Minimum 5 years Warranty - extendable | Up to 2 months after signing of contract |
|  | 1 | Distribution Panel: AC/DC insurance, wind generator inverter | Up to 2 months after signing of contract |
|  | Per turbine | Connecting Cables: AC and DC connections | Up to 2 months after signing of contract |
|  | Per turbine | Voltage limiter 135 Vdc | Up to 2 months after signing of contract |
|  | Per turbine | Interface Module 175 Vdc | Up to 2 months after signing of contract |
|  | Per turbine | Midnite Classic MPPT Charge Controller/wind turbine manufacturer recommended charge controller Minimum 5 years Warranty - extendable | Up to 3 months after signing of contract |
|  |  | Security fencing, according to accompanying specification, dimensioned as required to suitably protect the wind turbines, goods and fixtures from the environment, tampering, vandalism and facilitate necessary maintenance- All goods and fixtures to be secured with appropriate enclosures as per supplier guidelines and warranty requirements and applicable SABS standards | Up to 3 months after signing of contract |
|  |  | Spares (A final list of spares will be negotiated with the successful tenderer.) | Up to 2 months after signing of contract |

Load Profile

The system will provide a minimum of a Tier 4 electricity supply to the community as outlined by the World Bank.

    - Production Facility

    - Number of off-takers = 69

    - Maximum power = 0.80 kW / house or 55.2 kW

    - Mean daily consumption = 4.40 kWh/d/house or 303 kWh/d

    - LV Reticulation

    - The LV reticulation shall be constructed to Eskom standards based on 1.2kVA ADMD per stand.

    - The ESKOM Pre Electrification Tool based on R1500 (pension grant), with 4% growth, 5% theft, 20 A pre-paid and 50kWh free basic units was used to determine the Herman/Beta values which was used to do the load flow analysis. The wind component facility shall reach Practical completion on or 5 months from contract signing.  The Defects Period including the Operation, Maintenance and Capacity building is twelve (12) months from the Practical completion date.

  - Scope of Work

The Contractor will be fully responsible for:

    - developing the detailed wind farm design in accordance with the requirements and specifications as set out in this document and will assume liability for the design.

Note: The UB Community site image and coordinates are included in Section 5b: Other Related Requirements

Note: The wind turbine installation site wind climate and coordinates are included in Section 5b: Other Related Requirements

    - design, supply of all materials and labour, manufacture, delivery to site, offloading, construction, erection, installation, off-site testing on-site testing, commissioning, performance testing, preparation of all drawings, details and design, as-built drawings, maintenance manuals and instructions, in accordance with the requirements detailed in this document.

    - operation and maintenance of the facility during the defects period up to one year after installation in accordance with the requirements described in this document, including the training with O&M manual of RM local municipality staff in the operation and maintenance of the Works.

    - Works Information:

The works shall include but are not limited to the following:

    - A minimum 21 kW, maximum 24 kW Wind Farm comprising of minimum 2, maximum 6 smalls scale wind turbines.

    - Network communication system.

    - All ancillary works including site establishment and access roads

    - Security fencing, according to accompanying specification, dimensioned as required to suitably protect the wind turbines, goods and fixtures from the environment, tampering, vandalism and facilitate necessary maintenance

    - All goods and fixtures secured with appropriate enclosures as per supplier guidelines and warranty requirements and applicable SABS standards

    - Spares, O&M, M&E and capacity building for defect period of one year.

    - Solid building or container/s to house items, equipment

Eastern Cape Dept. of Economic Development, Environmental Affairs and Tourism (DEDEAT) wishes to maximize on local content, and preference will be given to locally manufactured equipment. All spares will be stored in a designated building of the RMLM.

The facility will be owned and operated by RMLM and although it will be run as an islanded system, it needs to be upgradable in the future to meet grid codes and standards that will allow connection to the National Grid.

All works should be in compliance with IEC 61400 and in particular, IEC 61400-2:2013 which outlines safety philosophy, quality assurance, and engineering integrity and specifies requirements for the safety of small wind turbines (SWTs) including design, installation, maintenance and operation under specified external conditions.

It is the Contractor's responsibility to ensure that the final design fully complies with the specifications referenced in this document, as well as South African legislation and regulations.

Due consideration must be given to the prevailing environmental and service conditions and the Contractor shall ensure that manufacturers' warranties are suited to the site and service conditions. The Contractor shall follow manufacturers' instructions on the use of materials and products.

System performance and particularly the performance ratio Rp shall be calculated in accordance with IEC 61400-2:2013 – Wind system performance monitoring - Guidelines for measurement, data exchange and analysis. All components supplied shall be designed, manufactured and tested in accordance with the latest applicable IEC and SANS standards.

If there is a conflict of method, or level of provision, the Contractor shall adopt the specification, recommendation or regulation with the most stringent conditions. The Contractor shall submit details of any such conflicts and the provisions adopted.

The Contractor shall:

- Ensure appropriate certification in accordance with the appropriate Standards or Code of Practice.

- Ensure that all designs for Electrical Works are signed off by ECSA registered Professional Engineers.

    - Procurement

The Contractor shall:

- Ensure that all works, materials, parts, components etc. supplied shall be new, both in the construction of the Wind Facility and for the maintenance of the Wind Facility during the Defects Period. All supplied Wind Turbines shall be certified to SABS or internationally accepted standard e.g. USA (SWCC), UK (MCS) etc and meet local content requirements of DTI.

- Ensure materials and products delivered to site bear the manufacturer's name, brand name and any other data required to verify that their performance and specification complies with the requirements of this document.

- Ensure materials and products are appropriately CE marked or SABS approved. The Contractor shall select materials & products with regard to standardization and availability of spare parts and for ease of maintenance.

- Ensure the same manufacturer is used for materials or products of a similar type and that identical parts of similar products are interchangeable.

- Ensure that materials and components are transported and stored in accordance with manufacturer's guidelines.

    - Site Establishment (Site offices and ablutions on site)

The Contractor shall be responsible for all site establishment works required to enable the completion of The Works in compliance with the Performance Requirements detailed in this document including but not limited to:

- Electricity to the site

- Chemical Ablutions for staff.

- Safety and Security

    - Installation and Construction

The Contractor shall:

- Construct the facility and supply all equipment, infrastructure and staff resources required for the construction of the Works in accordance with the Performance Specifications for the whole of the Works detailed in this document including ancillary equipment required for construction.

- Follow manufacturers' instructions on the use of materials and products.

- Not use plant and equipment prior to Handover other than for testing, commissioning and demonstration.

- Ensure that the Works are provided in accordance with appropriate IEC and /or South African Standards and Codes of Practice.

- Employ only operatives who are skilled and responsible craftsmen, fully experienced in their respective trades and who have gained qualifications appropriate for the work being carried out.

- Take all necessary steps to safeguard the Works during construction to ensure that damage or deterioration has not occurred.

- Provide suitable packaging for the protection of all materials and equipment during delivery, storage, and where exposed to damage on site. The Contractor shall return reusable packaging to the supplier. The Contractor shall take particular care to protect and maintain plant and equipment delivered early, or provided under separate contracts.

- Examine materials and products supplied when delivered to site and immediately prior to installation. The Contractor shall replace any damaged or faulty materials or products.

- Store all materials on raised boarded platforms under weatherproof covers and/or according to manufacturers' specifications.

- Protect all materials and equipment which may be exposed to damage, inclement weather, or ultra violet light.

- Ensure that sensitive plant and equipment items are not exposed to dirt or dust at any time, to maintain manufacturers' warranties and long term reliability.

    - Commissioning

The Contractor shall:

- Carry out the commissioning of the facility and supply all equipment and documentation in order to carry out the commissioning of the facility in accordance with the specifications detailed in this document for the whole of the Works.

- Repair any damage to finished materials and equipment prior to handover of the Works.

    - Training

The Contractor shall provide training to staff selected by the Client regarding the operation and maintenance of the Works. During the O&M period, knowledge transfer shall take place via the close interaction of The Contractor with 3 individuals selected by the Client. The Contractor shall provide a minimum of 2 day training per quarter to coincide with the quarterly maintenance activities and at final handover at the end of the defects liability period (i.e. 8 days training). Training will occur on site or at a facility provided by the Client.

  - Guarantees, Warrantees and Certification

The Contractor shall:

Provide valid manufacturers guarantees and warranties for all materials and products supplied according to the required warranty periods defined in the table below.

| Description | Years Warranty |
| --- | --- |
| Wind Turbine Generator | 5 (with possibility to extend) |
| Tower | 5 (with possibility to extend) |
| Workmanship | 1 |
| Charge controller | 5 (with possibility to extend) |

The Contractor shall provide valid manufacturers' guarantees and warranties for all materials and products supplied according to the required warranty periods defined in Table 1.

The Contractor shall ensure that the conditions of delivery, storage, installation and use of materials and products are such that they remain under guarantee for the maximum period as specified by the manufacturers.

The Contractor shall ensure any maintenance required by the Supplier is provided before Practical completion and that full records are kept and included in the O&M Manuals prior to Practical completion.

The risks as well as the expenses of conditioning and shipping back of the defective parts or products will be borne by the Contractor during the Defects Period.

All warranties and guarantees shall be passed on to the Client Representative transfer of ownership of the Facility. Furthermore, all documents necessary to ensure the enforcement of the warranties and guarantees are to be supplied by The Contractor to the Client Representative on Final Completion.

The wind turbine must have a valid and applicable certification to SABS or international accepted standard e.g. USA (SWCC), UK (MCS) etc.

  - Insurance

The Contractor shall ensure that adequate insurance is in place to cover the value and consequential losses due to accident, theft or fire of the materials and equipment stored onsite and that no materials or equipment in excess of this limit are stored on site at any given time.

  - Health and Safety

All construction for this project must be completed in accordance with the occupational Health and Safety Act 85 of 1993.

  - Civils

The Contractor shall:

    - provide valid manufacturers' guarantees and warranties for all materials and products supplied.

    - take the utmost care to minimise the impact of his establishment and other construction activities on the environment.

    - submit a Method Statement to the employer detailing his construction activities and what measures will be implemented to prevent the pollution.

    - contact the employer as early as possible, and program for the execution of the works.

    - only dump excess or unsuitable materials at sites, which have been authorized for that purpose by the Client.

    - include full compensation in costing for all work necessary for the clearing of the surface in preparation for the construction of the Works.

  - Electrical Systems and Distribution Boards

The Contractor shall abide by the Electrical Installation Regulation of 2009 (EIR) which prescribes in subclause 7(1) that every user of an electrical installation SHALL have a valid certificate of compliance (CoC) for every such installation, and 7(4) requires that the same user obtains (at least) an additional CoC for any change and alteration to that installation in order to keep the CoC current and valid.

The Contractor also requires in subclause 6(1) that anyone doing electrical installation work as a Contractor be so registered, and in subclause 5(1) work may only be done in accordance with the prescribed safety standard (SANS 10142-1), and no person may allow otherwise, and subclause 9(4) requires that a valid CoC be issued for all such work.

All equipment and services supplied shall comply with the standards listed below.

    - General

- Grid Connection Code for Renewable Power Plants (RPPs) Connected To the Electricity Transmission System (Ts) or the Distribution System (Ds) In South Africa Version 2.6 November 2012

- Standard Conditions for Embedded Generation within Municipal Boundaries Version September 2011

- South African Grid Code Network Version 8.0 July 2010

- SANS 10142-1:2009: The wiring of premises Part 1: Low-voltage installations

- SANS 10142-2:2009: The wiring of premises Part 2: Medium- voltage installations above 1kV ac not exceeding 22kV ac and up to and including 3000kW installed capacity

- SANS 10142-3:2018: National Standard for Small Scale Embedded Generation installations

- IEC 60364-4-41: Low-voltage plants installation. Part 4-41 - Protection for safety — protection against shock

- IEC 60364-7-712: Electrical installations of buildings Part 7-712 - Requirements for special installations or locations Solar photovoltaic (PV) power supply systems

    - Electrical Cabling

- SANS 1507 Part 1: General, Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V)

- SANS 1507 Part 2: Wiring Cables, Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V)

- SANS 1507 Part 3: PVC Distribution, Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V)

- SANS 1507 Part 4: XLPE Distribution Cables, Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V)

- SANS 1507 Part 5: halogen-free Distribution Cables, „Electric cables with extruded solid dielectric insulation for fixed installations (300/500 V to 1900/3300 V)

- SANS 10198 Parts 1-14: 2004 The selection, handling and installation of electric power cables of rating not exceeding 33 kV Part 1 to 14

    - Metering

- The South African Grid Code

- Electricity Act 41 of 1987

- Electricity Regulation Act, 2006

- IEC 60051-1 Direct acting indicating analogue electrical measuring instruments and their accessories - definitions and general requirements common to all parts

- IEC 61036 Alternating current static watt-hour meters for active energy

- IEC 62053 Electricity metering equipment (A.C.) - particular requirements

- IEC 62056 Electricity metering – Data exchange for meter reading, tariff and local control

- NRS 057/ SANS 474 Code of practice for electricity metering

    - LV Distribution

- IEC 60269 Low-Voltage fuses

- IEC 60898 Electrical accessories - circuit breakers for overcurrent protection for household and similar installations

- IEC 61009 Residual current operated circuit-breakers with integral overcurrent protection for household and similar uses (RCBO's)

Earthing

- NRS 097-2-1:2017 Section 4.2.6

- NRS 097-2-1:2017 ANNEX B

- SANS 10292:2001 Earthing of low-voltage (LV) distribution systems

  - Controls and Monitoring

The control and performance monitoring system has been supplied in the solar installation portion of this project.

  - Environmental

The Contractor shall be responsible for identifying and complying with all environmental legal and other requirements applicable to the design, construction and operation of the Works.

1.20.	Security fencing

1.20.1 Technical Requirements

The Contractor shall ensure that the fence is designed and selected with specific attention to:-

- The contractor wind farm design and wind turbine supplier requirements

- the selection of high-quality materials conforming with relevant SANS/ISO standards:

- the stability of the mounting structure over the required life of the project;

- avoidance of using systems that have a tendency to work their way loose over time,

- maintainability and overall system lifecycle cost:

- warranties offered on the materials and components provided:

- the need to decommission and remove the system at the end of the project life;

Clearing:

The boundary line shall be cleared of all vegetation, trees, rocks, rubble and rubbish one meter on both sides and the same removed from site. The two meter boundary line described above shall be graded to an even surface so that the fence later described shall have a height of 2.000mm for mesh fence above ground level.

Galvanised Steel security fencing system:

Supply and securely fix to new galvanized steel posts new galvanized welded mesh fencing, including all bolts. Mesh to be formed out of strands > 3 mm thick galvanized wire, welded into apertures of 76.2 x 12.7 mm. Weld mesh panels to be > 3000 mm wide x 2000 mm high, securely fixed to fencing posts including the new gate.

Tensile strength of wire to be >500 N/mm2 with weld mesh strength of > 60%. Bottom of new mesh to be 75mm above ground level.

Mesh to be securely fixed to lipped channel slide locking posts. All fencing to be erected strictly to manufacturer’s specification and to the approval of the supervising inspector.

Provide hot dipped galvanised steel coated Shark Tooth Spike to 2000mm high fence fixed to top of panel section and gate by mechanical means.

Galvanised Steel security gate:

A sliding motor gate from new galvanized welded mesh should be fitted as indicated in the layout drawing. Mesh to be formed out of strands > 3 mm thick galvanized wire, welded into apertures of 76.2 x 12.7 mm. Weld mesh gate to be > 4000 mm wide x 2000 mm high. On completion supply one number 70mm stainless steel discus padlock, code A0075, grade 8 quality.

1.21	Commissioning

The Contractor should inspect, test, commission and execute a performance test of the Works on site to demonstrate compliance with the Contract documents.

1.22	Testing and Acceptance

General Requirements

Contractor should inspect, test, commission and execute a performance test of the Works on site to demonstrate compliance with the Contract documents.

Provide facilities necessary to enable the inspection, testing, commissioning and performance testing of the Works to be satisfactorily completed including labour, equipment, materials, instruments, consumable materials, electrical power, fuel, lubricants, water, and suchlike.

Provide staff with the relevant skills and competence for the inspection, testing, commissioning, performance testing and witnessing required.

Instruments

Provide any instruments or other equipment for the Client's Representatives to review the accuracy, quality and performance of the Works. Provide any assistance required by the Client's Representative in the use of instruments and measuring equipment.

Ensure that instruments used for survey work, checking, inspection, testing, commissioning and performance monitoring are correctly calibrated. Submit calibration certificates with test method statements and test records.

Defects

Where the performance of the Works fails to meet the requirements of the Contract Documents, submit a method statement for the proposed remedial works including measures to be taken to prevent any delay to the program for the Works.

Rectify any defects that become apparent during inspection, testing, commissioning and performance testing. Retest defective parts of the Works, and any associated interdependent systems, and demonstrate that the Works operates in accordance with the Contract Documents.

Submit without delay any record that indicates that any part of the Works inspected or tested does not comply with the Contract Documents along with a proposal for rectification.

Records

Maintain records and certificates of inspections, testing, commissioning and performance testing undertaken demonstrating compliance with the Contract Documents and other recognized standards including those carried out by third party testing agencies, and manufacturers.

Retain records on site and make the records available to the Client's Representative on request.

Ensure inspection, testing, commissioning, and performance testing records are dated, and are clearly and uniquely referenced with the agreed equipment identification codes. Ensure equipment identification codes are permanently marked and clearly visible after installation.

Certify that the Works has been tested to recognized standards and the requirements of the Statutory Authorities, the Statutory Undertakings/Utility Suppliers, and service providers.

Testing and Acceptance includes the following Acceptance Tests:

- Mechanical Completion Test

- Mini-Grid Connection Test

- Practical Completion Test

- Final Completion Test

The Contractor shall:

- Ensure that he employs suitably qualified professionals with appropriate accreditation to carry out The Acceptance Tests with an appropriate grade for the work.

- Ensure the supervising commissioning engineer has a minimum of 3 years' experience in the commissioning and performance testing of similar installations.

- Supply regime of tests 1 month prior to construction including pre-requisites, methodology, stopping and restarting procedure and instrumentation.

1.22.1	Mechanical completion test

When the Contractor has completed the Mechanical Completion Test of the Works successfully, then the Client Representative will issue the Mechanical Completion Certificate in which case mechanical completion will have occurred.

The Contractor shall undertake the following:

1.22.2	General

- Verify all parts of the Works are in line with approved Final Design

- Verify the Works is according to provisions of the Contract

- Verify all equipment and parts have been installed according to their manufacturer's Installation Manuals

- Verify all Safety Labels have been erected according to the Contract

1.22.3	Wind Turbines

- Inspect wind turbines as installed and verify absence of any breakages or any signs of incorrect or incomplete installation

- Verify the wind turbine optimal operation arrangement

1.22.4	Cabling

- Verify that all cables have been marked and numbered according to Contract and in line with respective Cable Schedules

- Check cable Pulling Test records

- Inspect DC cabling between wind turbines and verify that cable types, sizes and lengths as well as cable connector types are in accordance with the Contract

- Verify integrity of Surge Protection Devices and all earthing connections

- Inspect the Voltage Test records for completeness and validity of recorded measurements

- Inspect Insulation Test records on all cables and circuits

1.22.5	Turbine tower structures

- Verify correct orientation and alignment of towers

- Verify overall set-out distances, surfacing, alignment and completeness of the assembly

- Verify that all cables and switches have been marked and numbered according to Contract and in line with respective Cable Schedules

1.22.6	Inspect cable pulling test records

- Inspect all DC & AC cabling and verify that cable types, sizes and lengths are in accordance with the Contract and in line with respective Cable Schedules

- Verify all inverter parameters are set up within Manufacturer's recommendations and local regulations

- Verify that all cables and switches have been marked and numbered according to Contract and in line with respective Cable Schedules

- Inspect cable Pulling Test records

- Inspect AC cabling and switches and verify that types, sizes and lengths are in accordance with the Contract and in line with respective Schedules

- Verify Voltage Controls

- Inspect Insulation Test records on all cables and circuits

1.22.7	Data acquisition system

The Contractor shall provide the following:

- Verify all system components and respective electrical and data connections are according to provisions of Contract

- Verify broadband equipment and connections

- All the certifications and tests on components necessary for the Mechanical Completion Certificate

- All "Construction Issue" drawings and design documents

- Tools and Instrumentation for operation and maintenance of The Facility:

- Multimeter

- Ohmmeter for the earthing resistor measurement and all insulation testing

- Calibrator

- DC and AC current clamps

1.22.8	Mini-Grid Connection Test

The Contractor should Adhere to:

- SANS 10142-1-2: Section 8.3 Testing - Test Report for All Electrical Installations

- SAGC for VRE power plants Rev 2.9 - Testing and Compliance Monitoring

1.22.9	Practical Completion Test

The Practical completion Test shall take place once Mechanical Completion and the Grid Connection Tests have occurred and will be finalized by the issuance of a Practical completion Certificate in which case Practical completion will have occurred.

The Contractor should confirm practical completion of:

- LV mini-grid, communications network and smart DB boards

- Protection device

- Alarms and signaling

- Monitoring and Data Acquisition Systems

In the event of disruption of the Test due to Force Majeure, such as theft, vandalism or Grid failure, the test will be suspended and restarted.

The Confirmed Provisional Performance Ratio estimate can take into account the deviation of the actual operating conditions of the plant from reference conditions STC (standard test condition).

The "unexpected" down time of the system during the PAT period has to be zero.

1.22.10	Final Completion Test

The test period will commence from the date of practical completion until the issuance the final completion certificate, after which Final Completion will be deemed to have occurred.

During the Final Completion Test the Contractor shall maintain an agreed upon % availability. In the event of disruption of the Test due to Force Majeure, such as theft, vandalism or Grid failure, the respective data will be disregarded.

Before commencing the Contractor shall submit their proposed test protocol to the Client Representative for review and approval. The Test will then be conducted in accordance to the test protocol approved by the Client Representative.

1.23	Performance during operation

In order to ensure the proper operation of the Works, the Contractor shall provide equipment to continuously monitor and document the relevant conditions of the Plant at regular intervals by means of remote monitoring, data assessment and, if applicable, processing of malfunction messages. The monitoring system should also record consumption and be able to identify potential theft of electricity.

1.24	Operation and Maintenance

The Contractor shall provide all materials, consumables and, equipment required to maintain the system to achieve the required service life. Note that as part of the operation and maintenance portion of the quotation, provision must be made for capacity building within the RMLM to allow for long term operation and maintenance of the project.

The Contractor shall discuss and agree with the Client Representative and submit an Operations and Maintenance Strategy for the Works for the Defects Period (first year of operation) to include:

- Proposals for maintaining the Works in order to achieve the required service life and the required Performance Ratio and to demonstrate compliance with manufacturers' minimum maintenance requirements for respective warranty covers

- Proposals for monitoring the Works and maintaining the monitoring equipment over the life of the project

- Proposals for responding to emergencies, plant malfunctions, security breaches and notifications of restricted operation from the Client Representative.

The Contractor shall be responsible for the operation and running maintenance / upkeep as well as technical operational management of the Works during the Defects Period, maintaining proper functioning of the Works with regards to availability and functionality and performance.

The operation and maintenance activities performed and the repair activities supervised by the Contractor shall always and fully comply with all current requirements of:

- the applicable law, regulations and technical and safety standards

- the permitting authorities

- the grid operator

- the suppliers under their warranty/extension-of-warranty conditions

- the insurer

In the scope of operational management, the Contractor shall assume the tasks which are necessary to ensure the trouble-free operation of the plant, that is, the provision of the technical activities rendered at the Works, such as supervision of the operating conditions, intervention in the event of extraordinary situations to prevent malfunctions and management of the systems.

The Contractor shall undertake to perform the regularly scheduled inspect' on and periodic maintenance of the Works in conformity with the specifications of the component manufacturers as well as the coordination and monitoring of repairs (including repairs performed under the Factory Warranties of the suppliers).

The Contractor shall:

- Be responsible for the operations and maintenance (O&M) during the one year defects period.

- Be responsible for supplying all equipment and documentation required to ensure that the operations and maintenance is carried out in accordance with the specifications detailed in this document.

1.25	Reporting

The Contractor shall submit a technical report on the operation and maintenance of the Works to the Client Representative on a monthly basis. The report shall contain the following:

- The monthly technical availability (readiness for operation) of the Works accumulated by the respective date (in percent based on the wind resource) in relation to the year

- Figures on the estimated Wind Facility's production on a monthly basis

- Semi-annual inspections and quarterly maintenance work performed, conditions observed, compliance with the suppliers' maintenance requirements

- Details on any incidents which have been determined to be the result of maintenance-related activities

- Reporting of plant and monitoring system stoppages and their causes

- information produced from on-site inspections

- information regarding preventative and corrective maintenance activities

- updates on spares holdings

- A record of the malfunctions/defects and troubleshooting measures conducted during the ongoing period of time and those planned or expected for the subsequent periods

- A record of acceptance tests and certifications, as and when required

The Contractor shall present to the Client Representative a brief monthly report showing the energy production and the technical availability of the Plant. The Contractor shall also grant the Client and his/her Representative access to the remote monitoring system's Internet portal.

1.26	Drawings

As soon as is possible after the contract has been awarded to him, the Contractor must submit two (2) copies of the following drawings to the Engineer for approval:

Wind turbine site layout? (Coordinates of masts)

Wind turbine electrical connection to the mini-grid

1.27	Spare parts

Adequate racking should be supplied in the container for the spare parts and equipment. A final list of spares will be negotiated with the successful tenderer.

# Section 5b: Other Related Requirements

Further to the Schedule of Requirements in the preceding Table, Bidders are requested to take note of the following additional requirements, conditions, and related services pertaining to the fulfillment of the requirements: [check the condition that applies to this ITB, delete the entire row if condition is not applicable to the goods being procured]

Exact Address of Delivery/Installation Location

-32°34'34.88"S, 26°33'7.08"E

Installation site Wind Climate -32°34'34.88"S, 26°33'7.08"E

A = 4.9 m/s

K = 1.71

U = 4.40 m/s

P = 117 W/m2 (@ 1.225 kg/m3)

18 m AGL (above ground level)

| Customs, if required, clearing shall be done by: | Supplier |
| --- | --- |
| Ex-factory / Pre-shipment inspection | By supplier |
| Inspection upon delivery | By supplier |
| Installation Requirements | Pls referrer to point 1.12.4 of Section 5a above |
| Testing Requirements | Testing and Acceptance includes the following Acceptance Tests: • Mechanical Completion Test • Mini-Grid Connection Test • Practical Completion Test • Final Completion Test |
| Scope of Training on Operation and Maintenance | Pls refer to Point 1.12.6 & 1.24 under Section 5a above |
| Commissioning | Pls refer to point 1.21 under Section 5a above |
| Warranty Period | Pls refer to point 1.13 under Section 5a above |
| Local Service Support | The supplier must have presence in South Africa |
| Technical Support Requirements | 24hrs technical support is required |
| After-sale services Requirements | ☒ Warranty on Parts and Labor for minimum period of 3 ☒ Technical Support ☒ Provision of Service Unit when pulled out for maintenance /repair ☐ Others [pls. specify] |
| Payment Terms (max. advanced payment is 20% as per UNDP policy) | Other (pls. specify) as per milestone to be indicated in the schedule |
| Conditions for Release of Payment | ☐ Pre-shipment inspection ☒ Inspection upon arrival at destination ☒ Installation ☒ Testing ☒ Training on Operation and Maintenance ☒ Others Upon confirmation by the Engineer contracted for this project ☒ Written Acceptance of Goods based on full compliance with ITB requirements |
| All documentations, including catalogues, instructions and operating manuals, shall be in this language | English |

# Section 6: Returnable Bidding Forms / Checklist

This form serves as a checklist for preparation of your Bid. Please complete the Returnable Bidding Forms in accordance with the instructions in the forms and return them as part of your Bid submission. No alteration to format of forms shall be permitted and no substitution shall be accepted. All bidding forms indicated below MUST be submitted and fully completed as indicated in the forms. Failure to do so, the bid will not be considered for evaluations.

Before submitting your Bid, please ensure compliance with the Bid Submission instructions of the BDS 22.

Technical Bid:

| Have you duly completed all the Returnable Bidding Forms? |  |
| --- | --- |
| Form A: Bid Submission Form | ☒ |
| Form B: Bidder Information Form | ☒ |
| Form D: Qualification Form | ☒ |
| Form E: Format of Technical Bid/Bill of Quantities | ☒ |
| Form F : Price schedule form | ☒ |
| [Add other forms as necessary] | ☐ |
| Have you provided the required documents to establish compliance with the evaluation criteria in Section 4? | ☐ |

## Form A: Bid Submission Form

| Name of Bidder: | [Insert Name of Bidder] | Date: | Select date |
| --- | --- | --- | --- |
| ITB reference: | [Insert ITB Reference Number] |

We, the undersigned, offer to supply the goods and related services required for [Insert Title of goods and services] in accordance with your Invitation to Bid No. [Insert ITB Reference Number] and our Bid. We hereby submit our Bid, which includes this Technical Bid and Price Schedule.

Our attached Price Schedule is for the sum of [Insert amount in words and figures and indicate currency].

We hereby declare that our firm, its affiliates or subsidiaries or employees, including any JV/Consortium /Association members or subcontractors or suppliers for any part of the contract:

- is not under procurement prohibition by the United Nations, including but not limited to prohibitions derived from the Compendium of United Nations Security Council Sanctions Lists;

- have not been suspended, debarred, sanctioned or otherwise identified as ineligible by any UN Organization or the World Bank Group or any other international Organization;

- have no conflict of interest in accordance with Instruction to Bidders Clause 4;

- do not employ, or anticipate employing, any person(s) who is, or has been a UN staff member within the last year, if said UN staff member has or had prior professional dealings with our firm in his/her capacity as UN staff member within the last three years of service with the UN (in accordance with UN post-employment restrictions published in ST/SGB/2006/15);

- have not declared bankruptcy, are not involved in bankruptcy or receivership proceedings, and there is no judgment or pending legal action against them that could impair their operations in the foreseeable future;

- undertake not to engage in proscribed practices, including but not limited to corruption, fraud, coercion, collusion, obstruction, or any other unethical practice, with the UN or any other party, and to conduct business in a manner that averts any financial, operational, reputational or other undue risk to the UN and we embrace the principles of the United Nations Supplier Code of Conduct and adhere to the principles of the United Nations Global Compact.

We declare that all the information and statements made in this Bid are true and we accept that any misinterpretation or misrepresentation contained in this Bid may lead to our disqualification and/or sanctioning by the UNDP.

We offer to supply the goods and related services in conformity with the Bidding documents, including the UNDP General Conditions of Contract and in accordance with the Schedule of Requirements and Technical Specifications.

Our Bid shall be valid and remain binding upon us for the period specified in the Bid Data Sheet.

We understand and recognize that you are not bound to accept any Bid you receive.

I, the undersigned, certify that I am duly authorized by [Insert Name of Bidder] to sign this Bid and bind it should UNDP accept this Bid.

Name: 	_____________________________________________________________

Title: 	_____________________________________________________________

Date:	_____________________________________________________________

Signature: 	_____________________________________________________________

[Stamp with official stamp of the Bidder]

## Form B: Bidder Information Form

| Legal name of Bidder | [Complete] |
| --- | --- |
| Legal address | [Complete] |
| Year of registration | [Complete] |
| Bidder’s Authorized Representative Information | Name and Title: [Complete] Telephone numbers: [Complete] Email: [Complete] |
| Are you a UNGM registered vendor? | ☐ Yes ☐ No If yes, [insert UGNM vendor number] |
| Are you a UNDP vendor? | ☐ Yes ☐ No If yes, [insert UNDP vendor number] |
| Countries of operation | [Complete] |
| No. of full-time employees | [Complete] |
| Quality Assurance Certification (e.g. ISO 9000 or Equivalent) (If yes, provide a Copy of the valid Certificate): | [Complete] |
| Does your Company hold any accreditation such as ISO 14001 or ISO 14064 or equivalent related to the environment? (If yes, provide a Copy of the valid Certificate): | [Complete] |
| Does your Company have a written Statement of its Environmental Policy? (If yes, provide a Copy) | [Complete] |
| Does your organization demonstrates significant commitment to sustainability through some other means, for example internal company policy documents on women empowerment, renewable energies or membership of trade institutions promoting such issues | [Complete] |
| Is your company a member of the UN Global Compact | [Complete] |
| Contact person that UNDP may contact for requests for clarifications during Bid evaluation | Name and Title: [Complete] Telephone numbers: [Complete] Email: [Complete] |
| Please attach the following documents: | Company Profile, which should not exceed fifteen (15) pages, including printed brochures and product catalogues relevant to the goods and/or services being procured Certificate of Incorporation/ Business Registration Tax Registration/Payment Certificate issued by the Internal Revenue Authority evidencing that the Bidder is updated with its tax payment obligations, or Certificate of Tax exemption, if any such privilege is enjoyed by the Bidder Trade name registration papers, if applicable Quality Certificate (e.g., ISO, etc.) and/or other similar certificates, accreditations, awards and citations received by the Bidder, if any Environmental Compliance Certificates, Accreditations, Markings/Labels, and other evidences of the Bidder’s practices which contributes to the ecological sustainability and reduction of adverse environmental impact (e.g., use of non-toxic substances, recycled raw materials, energy-efficient equipment, reduced carbon emission, etc.), either in its business practices or in the goods it manufactures Patent Registration Certificates, if any of technologies submitted in the Bid is patented by the Bidder Certification or authorization to act as Agent on behalf of the Manufacturer, or Power of Attorney. Export Licenses, if applicable Local Government permit to locate and operate in assignment location, if applicable Official Letter of Appointment as local representative, if Bidder is submitting a Bid on behalf of an entity located outside the country |

## Form C: Joint Venture/Consortium/Association Information Form

| Name of Bidder: | [Insert Name of Bidder] | Date: | Select date |
| --- | --- | --- | --- |
| ITB reference: | [Insert ITB Reference Number] |

To be completed and returned with your Bid if the Bid is submitted as a Joint Venture/Consortium/Association.

| No | Name of Partner and contact information (address, telephone numbers, fax numbers, e-mail address) | Proposed proportion of responsibilities (in %) and type of goods and/or services to be performed |
| --- | --- | --- |
| 1 | [Complete] | [Complete] |
| 2 | [Complete] | [Complete] |
| 3 | [Complete] | [Complete] |

| Name of leading partner (with authority to bind the JV, Consortium, Association during the ITB process and, in the event a Contract is awarded, during contract execution) | [Complete] |
| --- | --- |

We have attached a copy of the below referenced document signed by every partner, which details the likely legal structure of and the confirmation of joint and severable liability of the members of the said joint venture:

☐ Letter of intent to form a joint venture	OR 	☐ JV/Consortium/Association agreement

We hereby confirm that if the contract is awarded, all parties of the Joint Venture/Consortium/Association shall be jointly and severally liable to UNDP for the fulfillment of the provisions of the Contract.

| Name of partner: ___________________________________ | Name of partner: ___________________________________ |
| --- | --- |
| Signature: ______________________________ | Signature: _______________________________ |
| Date: ___________________________________ | Date: ___________________________________ |
| Name of partner: ___________________________________ | Name of partner: ___________________________________ |
| Signature: ______________________________ | Signature: _______________________________ |
| Date: ___________________________________ | Date: ___________________________________ |

## Form D: Eligibility and Qualification Form

| Name of Bidder: | [Insert Name of Bidder] | Date: | Select date |
| --- | --- | --- | --- |
| ITB reference: | [Insert ITB Reference Number] |

If JV/Consortium/Association, to be completed by each partner.

History of Non- Performing Contracts

| ☐Non-performing contracts did not occur during the last 3 years |
| --- |
| ☐ Contract(s) not performed in the last 3 years |
| Year | Non- performed portion of contract | Contract Identification | Total Contract Amount (current value in US$) |
|  |  | Name of Client: Address of Client: Reason(s) for non-performance: |  |

Litigation History (including pending litigation)

| ☐ No litigation history for the last 3 years |
| --- |
| ☐ Litigation History as indicated below |
| Year of dispute | Amount in dispute (in US$) | Contract Identification | Total Contract Amount (current value in US$) |
|  |  | Name of Client: Address of Client: Matter in dispute: Party who initiated the dispute: Status of dispute: Party awarded if resolved: |  |

Previous Relevant Experience

Please list only previous similar assignments successfully completed in the last 3 years.

List only those assignments for which the Bidder was legally contracted or sub-contracted by the Client as a company or was one of the Consortium/JV partners. Assignments completed by the Bidder’s individual experts working privately or through other firms cannot be claimed as the relevant experience of the Bidder, or that of the Bidder’s partners or sub-consultants, but can be claimed by the Experts themselves in their CVs. The Bidder should be prepared to substantiate the claimed experience by presenting copies of relevant documents and references if so requested by UNDP.

| Project name & Country of Assignment | Client & Reference Contact Details | Contract Value | Period of activity and status | Types of activities undertaken |
| --- | --- | --- | --- | --- |

Bidders may also attach their own Project Data Sheets with more details for assignments above.

☐ Attached are the Statements of Satisfactory Performance from the Top 3 (three) Clients or more.

Financial Standing

| Annual Turnover for the last 3 years | Year USD Year USD Year USD |
| --- | --- |
| Latest Credit Rating (if any), indicate the source |  |

| Financial information (in US$ equivalent) | Historic information for the last 3 years |
| --- | --- |
|  | Year 1 | Year 2 | Year 3 |
|  | Information from Balance Sheet |
| Total Assets (TA) |  |  |  |
| Total Liabilities (TL) |  |  |  |
| Current Assets (CA) |  |  |  |
| Current Liabilities (CL) |  |  |  |
|  | Information from Income Statement |
| Total / Gross Revenue (TR) |  |  |  |
| Profits Before Taxes (PBT) |  |  |  |
| Net Profit |  |  |  |
| Current Ratio |  |  |  |

☐ Attached are copies of the audited financial statements (balance sheets, including all related notes, and income statements) for the years required above complying with the following condition:

  - Must reflect the financial situation of the Bidder or party to a JV, and not sister or parent companies;

  - Historic financial statements must be audited by a certified public accountant;

  - Historic financial statements must correspond to accounting periods already completed and audited. No statements for partial periods shall be accepted.

## Form E: Format of Technical Bid

| Name of Bidder: | [Insert Name of Bidder] | Date: | Select date |
| --- | --- | --- | --- |
| ITB reference: | [Insert ITB Reference Number] |

The Bidder’s Bid should be organized to follow this format of the Technical Bid. Where the bidder is presented with a requirement or asked to use a specific approach, the bidder must not only state its acceptance, but also describe how it intends to comply with the requirements. Where a descriptive response is requested, failure to provide the same will be viewed as non-responsive.

SECTION 1: Bidder’s qualification, capacity and expertise

  - General organizational capability which is likely to affect implementation: management structure, financial stability and project financing capacity, project management controls, extent to which any work would be subcontracted (if so, provide details).

  - Relevance of specialized knowledge and experience on similar engagements done in the region/country.

  - Quality assurance procedures and risk mitigation measures.

  - Organization’s commitment to sustainability.

SECTION 2: Scope of Supply, Technical Specifications, and Related Services

This section should demonstrate the Bidder’s responsiveness to the specification by identifying the specific components proposed, addressing the requirements, as specified, point by point; providing a detailed description of the essential performance characteristics proposed; and demonstrating how the proposed bid meets or exceeds the requirements/specifications. All important aspects should be addressed in sufficient detail.

  - A detailed description of how the Bidder will deliver the required goods and services, keeping in mind the appropriateness to local conditions and project environment. Details how the different service elements shall be organized, controlled and delivered.

  - Explain whether any work would be subcontracted, to whom, how much percentage of the requirements, the rationale for such, and the roles of the proposed sub-contractors and how everyone will function as a team.

  - The bid shall also include details of the Bidder’s internal technical and quality assurance review mechanisms.

  - Implementation plan including a Gantt Chart or Project Schedule indicating the detailed sequence of activities that will be undertaken and their corresponding timing.

  - Demonstrate how you plan to integrate sustainability measures in the execution of the contract.

| Goods and services to be Supplied and Technical Specifications | Your response |
| --- | --- |
|  | Compliance with technical specifications | Delivery Date (confirm that you comply or indicate your delivery date) | Quality Certificate/Export Licenses, etc. (indicate all that apply and attach) | Comments |
|  | Yes, we comply | No, we cannot comply (indicate discrepancies) |  |  |  |
| Wind Turbine Generator 5 Years Warranty |  |  |  |  |  |
| Tower 5 Years Warranty |  |  |  |  |  |
| Workmanship 1 Years Warranty |  |  |  |  |  |
| Insurance |  |  |  |  |  |
| Civils |  |  |  |  |  |
| Electrical Systems and Distribution Boards |  |  |  |  |  |
| General (please refer to detialed scope of work above) |  |  |  |  |  |
| Electrical Cabling |  |  |  |  |  |
| Metering |  |  |  |  |  |
| LV Distribution |  |  |  |  |  |
| Controls and Monitoring |  |  |  |  |  |
| Environmental |  |  |  |  |  |
| Commissioning |  |  |  |  |  |
| Testing and Acceptance -Mechanical Completion Test -Mini-Grid Connection Test -Practical Completion Test -Final Completion Test |  |  |  |  |  |
| Data acquisition system |  |  |  |  |  |
| Spare parts |  |  |  |  |  |

| Other Related services and requirements (based on the information provided in Section 5b) | Compliance with requirements | Details or comments on the related requirements |
| --- | --- | --- |
|  | Yes, we comply | No, we cannot comply (indicate discrepancies) |  |
| e.g. Delivery Term |  |  |  |
| Warranty |  |  |  |
| Local Service Support |  |  |  |

SECTION 3: Management Structure and Key Personnel

  - Describe the overall management approach toward planning and implementing the project. Include an organization chart for the management of the project describing the relationship of key positions and designations. Provide a spreadsheet to show the activities of each personnel and the time allocated for his/her involvement.

  - Provide CVs for key personnel that will be provided to support the implementation of this project using the format below. CVs should demonstrate qualifications in areas relevant to the scope of goods and/or services.

Format for CV of Proposed Key Personnel

| Name of Personnel | [Insert] |
| --- | --- |
| Position for this assignment | [Insert] |
| Nationality | [Insert] |
| Language proficiency | [Insert] |
| Education/ Qualifications | [Summarize college/university and other specialized education of personnel member, giving names of schools, dates attended, and degrees/qualifications obtained.] |
|  | [Insert] |
| Professional certifications | [Provide details of professional certifications relevant to the scope of goods and/or services] |
|  | Name of institution: [Insert] Date of certification: [Insert] |
| Employment Record/ Experience | [List all positions held by personnel (starting with present position, list in reverse order), giving dates, names of employing organization, title of position held and location of employment. For experience in last five years, detail the type of activities performed, degree of responsibilities, location of assignments and any other information or professional experience considered pertinent for this assignment.] |
|  | [Insert] |
| References | [Provide names, addresses, phone and email contact information for two (2) references] |
|  | Reference 1: [Insert] Reference 2: [Insert] |

I, the undersigned, certify that to the best of my knowledge and belief, the data provided above correctly describes my qualifications, my experiences, and other relevant information about myself.

________________________________________	___________________

Signature of Personnel						     Date (Day/Month/Year)

## FORM F: Price Schedule Form

| Name of Bidder: | [Insert Name of Bidder] | Date: | Select date |
| --- | --- | --- | --- |
| ITB reference: | [Insert ITB Reference Number] |

The Bidder is required to prepare the Price Schedule following the below format. The Price Schedule must include a detailed cost breakdown of all goods and related services to be provided. Separate figures must be provided for each functional grouping or category, if any. Any estimates for cost-reimbursable items, such as travel of experts and out-of-pocket expenses, should be listed separately.

Currency of the Bid: [Insert Currency]

Price Schedule

| Item # | Description | UOM | Quantity | Unit Price | Total Price |
| --- | --- | --- | --- | --- | --- |
| FCA charges, if any |  |
| Bid Subtotal FCA (Incoterms 2010) (please state FCA International Airport): |  |
| Transportation/Delivery Cost |  |
| Bid Total DDP / DAT / DAP, off-loaded/cleared, Place, Country (Incoterms 2010) |  |
| Installation |  |
| Training |  |
| Warranty |  |
| After Sales |  |
| GRAND TOTAL |  |

Name of Bidder: 		________________________________________________

Authorised signature: 		________________________________________________

Name of authorised signatory:	________________________________________________

Functional Title:			________________________________________________

Insert: address and email: ………………………………………………………………………………………………..

[insert: address and email address]

Non-performance, as decided by UNDP, shall include all contracts where (a) non-performance was not challenged by the contractor, including through referral to the dispute resolution mechanism under the respective contract, and (b) contracts that were so challenged but fully settled against the contractor. Non-performance shall not include contracts where Employers decision was overruled by the dispute resolution mechanism. Non-performance must be based on all information on fully settled disputes or litigation, i.e. dispute or litigation that has been resolved in accordance with the dispute resolution mechanism under the respective contract and where all appeal instances available to the Bidder have been exhausted.