Supplemental Information to the

Acquisition of diving equipment for Department of diving search and rescue works in the Azov Sea

Reference: 177-2020-UNDP-UKR-ITB-RPP, Lots 1-3

The following amendments have been made to the Section 3a: Schedule of Requirements and Technical Specifications ITB document:

- Lot 2. Ropes, booms etc, items 6 and 7 in Clause 3. Technical Specification to be amended and read as follows:

| No | Product name and specification requirements | Quantity of units (unit/pair) |
| --- | --- | --- |
| 6 | Booms: Continuous buoyancy booms with a flat float chamber, running meter Overall height, mm – 550 +/-10 % Freeboard, mm – 250 +/-10 % Section length, m- 10 +/-10 % Upper and lower cable / chain - yes, galvanized Fasteners - universal fasteners Fabric - PVC fabric with high resistance to corrosive media (petroleum products) and exposure to the environment Density of fabric, not less, g / m2- 900 | 600 |
| 7 | Coil for mobile movement and storage of booms Length – 2050 +/-10 % Width – 2250 +/-10 % Height – 2200 +/-10 % The diameter is 2475 Frequency of rotation, rpm –up to 7 Rotational torque, Newtons per meter – 700 Drum capacity, not less, m-250 (booms) The drive is electric Material - painted with anti-corrosion paint resistant to the marine environment Possibility of moving and reloading - is equipped with rubber wheels | 3 |