Annex 1

Technical Specifications

| Item Description |
| --- |
| Type | Special sanitation vehicle (Vacuum suction truck) |
| Condition | Brand new |
| Special equipment characteristics: |
| Tank capacity | Min. 5.0 m³ |
| Extraction depth | Min. 5.0 m |
| Pump productivity | Min. 310 m³/hour |
| Maximum vacuum in the tank | 0.08 MPa |
| Technical characteristics of the truck: |
| Engine type | diesel |
| Engine power | Min. 170 hp |
| Load capacity | Min. 5600 kg |
| Wheel formula | 4x2 or 6x4 |
| Gearbox | automatic/ mechanical |
| ABS braking system | yes |
| Fuel consumption per 100km | not more than 22l at a speed of 80km/ h |
| Warranty: |
| Warranty on vehicle | Minimum 2 years |
| Warranty on special equipment | Minimum 2 years |
| Other requirements: |
| Delivery to the Republic of Moldova |
| Training of relevant staff |
| Availability of authorized service in Moldova and comprehensiveness of after-sales services |
| Possibility to further conclude a maintenance contract with the end-user (Ministry of Defence of the Republic of Moldova) |