The tender was advertised on three of our online tendering platforms and you can download the tender document from the first link

https://procurement-notices.undp.org/view_notice.cfm?notice_id=71720

https://etendering.partneragencies.org  Event ID 0000007562

https://www.ungm.org/Public/Notice/Index/116290

Please note tender submission is strictly online so please also download the Etendering Guide to Bidders which provides all information on submission of bids from the link above.

Unfortunately, we missed the ZOOM meeting today as we were in a meeting ourselves, please could you advise if we could bid per lot item and yes, we will quote for all the items under each lot

The prebid meeting failed to take off and will be re-scheduled. All bidders who expressed interest on the online platform will be notified of the new prebid meeting date. We are also looking at extending deadline by one week. Confirmed date will be announced online.

|  |  | Comments |
| --- | --- | --- |
| Data logger and Controller | High Performance Data Recorder No baseline specifications or accuracy requirements have been specified? | Specifications for the data logger A/D conversion should be 24bit or better Standard Operating Temperature -40°C to +70 °C Extended Operating Temperature -55°C to +85 °C There should be Communication ports for configuring and downloading data from the data logger. The choice of communications depends on the supplier. There should also be communication port for the GSM/GPRS modem to be connected for data transmission Data Storage facility should be able to store data for at least 5 years. Again, the choice of technology used entirely depends on the supplier. Analogue Sensor Inputs for mentioned sensors and also for the future expansion. Accuracy Specifications for the analogue inputs. Accuracy specifications do not include sensor or measurement noise. ± (0.04% of measurement + offset) at 0° to 40°C ± (0.06% of measurement + offset) at -40° to +70°C ± (0.08% of measurement + offset) at -55° to +85°C (extended temperature range) Data logger should be housed in an environment with robust casing and the casing should withstand extreme weather conditions |
| Communications | Cellular Communication GPRS/GSM Where is the data to be transmitted? Are we expected to provide a central station database & visualization software at the client (local authority office) If the data is to be sent to an existing system, we will need details of the same for integration. Data SIM Cards: Please confirm data SIM cards with subscription paid would be provided by the client? | Normally when a supplier is supplying us new with Automatic Weather station, they should supply us with the central sever system/database. For those suppliers with their systems (AWS) already part of our networks do not need to supply us with a server station. There are two communication channels for the systems, one to the local office and the other that uses GSM/GPRS to sent to the central server at the Headquarters. So yes you are expected to provide with the central station database and visualization software at the client station. The central server system should have the at least archiving and data visualization capabilities. For the SIM normally it is not the responsibility of the supplier of equipment to take care of the subscription. Since this is a project where the Met Department is but a stakeholder, we are expecting the project to take care of the subscription, not the supplier of equipment. |
| Communications | Local Display of Data from weather stations Please confirm if the data logger can have a built-in display for viewing the data locally or should we supply a laptop? We assume each station will have a dedicated client display PC in a nearby office and the station can be hardwired to send data to this PC. Additionally, using the client provided data SIM card, the station will send the data to the central server at scheduled times. Please confirm this understanding is correct? What is the distance from the AWS station to the client Display PC in office? | It would be ideal if we can have both the laptop and a built-in display on the data logger. Yes, you are right on this approach. Depending on your system you can even have wireless connection instead of wired from the weather station to the local client display if you like. Within 150m |
| Sensors | No detailed Specifications are stated for the sensors Ø Air temperature Ø Relative humidity Ø Soil temperature Ø Wind speed & wind direction Ø Precipitation Tipping Bucket Rain gauges Ø Digital Barometric pressure Ø Global radiation first class Ø Potential Evapo-transpiration | For this one you can download CIMO guide for more guidance. https://www.wmo.int/pages/prog/www/IMOP/CIMO-Guide.html. |

Delivery location and incoterms:

Can you please confirm delivery locations and under which incoterms the delivery should be done for each lot ?

DAP Harare

Installation, training and commissioning:

Can you please confirm that installation, training, commissioning and assistance is not requested in that ITB and will be handled with another contract or locally for each lot ?

Installation, training and commissioning is not required in this instance. Bidder can however make use of Table 2 of the Price Schedule to provide any other costs. Evaluation of financial offer will be restricted to the supply of the requested goods.

Pre-bid meeting

We tried to connect to the pre-bid meeting online via zoom as specified in the Bid Data Sheet page 17, BDS n°4, but, the "zoom meeting" was closed. Can you please confirm that the zoom meeting has been cancelled or reported ?

Pre-bid has been rescheduled to Thursday 5 November 2020 and link is provided below

Topic: PRC/ZWE/ITB/0004/01/10/2020 Project:	Supply and delivery of weather stations, drones, solar freezers, generators, water tanks, motor bikes, dam scoop and tow grader

Time: Nov 5, 2020 10:00 AM Harare, Pretoria

Join Zoom Meeting

https://undp.zoom.us/j/82752984669?pwd=V09pQ3duRXVLTGRLSTFsSGpUVW1CZz09

Meeting ID: 827 5298 4669

Passcode: 122044

Submission deadline has been extended to 13 November 2020, 4pm (+2hour GMT harare Time)