Compliance sheet

Item 1.1 / 340 W Monocrystalline Solar Panel

| No. | Description | Required Specification | Bidder Offered | Remark/Comment on proposed deviations (clearly explain any proposed deviations from the equipment/items requested in the BOQ) |
| --- | --- | --- | --- | --- |
| 1 | Electrical specs |
|  | Electrical l parameters at STC* (irradiance 1000W/㎡, ambient temp. 25℃ @ morphemic quality) |
|  | Max. power output | 340W |  |  |
|  | Max. power output tolerances | 0~ +5W |  |  |
|  | Module efficiency | % 17 - 19 |  |  |
|  | Voltage at max power | 37 – 40 V |  |  |
|  | Current at max power | 9 - 11 A |  |  |
|  | Open circuit voltage | 45 – 48 V |  |  |
|  | Short circuit current | 9 – 11A |  |  |
|  | Certification and regulatory standards | ISO 9001/ISO 14001 |  |  |
|  | Electrical I parameters STC* (irradiance 800W/㎡, ambient temp. 25℃ and wind speed 1 m/s) |
|  | Power output | 258W |  |  |
|  | Voltage at max power | 34 – 36 V |  |  |
|  | Current at max power | 7 – 8 A |  |  |
|  | Open circuit voltage | 42 – 44 V |  |  |
|  | Short circuit current | 8 – 9 A |  |  |
| 2 | Mechanical specs |
|  | Module Dimension | 1950×990×40 mm |  |  |
|  | Cells | 156x156 mm (72cells = 6*10) |  |  |
|  | Weight (kg) | 20 – 25 kg |  |  |
|  | Class | High transmission glass 3.2mm |  |  |
|  | anti-reflective coating type | Anti-reflection glass |  |  |
|  | Junction box IP rating | IP67 1500VDC 3 bypass diode |  |  |
|  | Gable | 4mm² |  |  |
|  | Connector type | MC4 compatible |  |  |
|  | Fire performance | Class C |  |  |
|  | Working Conditions & Temperature |
|  | Temperature coefficient (Pmpp) | -0.39%/℃ |  |  |
|  | Temperature coefficient (Isc ) | +0.05%/℃ |  |  |
|  | Temperature coefficient (Voc ) | -0.29%/℃ |  |  |
|  | NOCT* | 45℃±2 ℃ |  |  |
|  | Maximum system voltage (IEC/UL) | 1500V DC |  |  |
|  | Max series fuse rating | 15A |  |  |
| 3 | Submit Manufacturer certification and test reports |  |  |
| 4 | Submit Detail drawing brochure catalogue. |  |  |

Item 1.2 / Solar Inverter:

| No. | Description | Required Specification | Bidder Offered | Remark/Comment on proposed deviations (clearly explain any proposed deviations from the equipment/items requested in the BOQ) |
| --- | --- | --- | --- | --- |
| 1 | Input data |
| a | PV source |
|  | Max Input Voltage | 800 V |  |  |
|  | Min Input Voltage at MPPT* | 350 V |  |  |
|  | Recommended voltage at MPPT | 500vdc-600vdc |  |  |
|  | Recommended Amps Input, at MPPT | 55 – 57A |  |  |
|  | Recommended Max Power | 44 – 45 kW |  |  |
| b | AC Input |
|  | Input Voltage | 380/400/415/440V AC – 3PH |  |  |
|  | Max current (RMS*) | 46 – 48A |  |  |
|  | Power and VA capability | 30 kVA |  |  |
| 2 | Output data |
|  | Output power | 24 -30kW |  |  |
|  | Output Voltage | 380/400/415/440VAC, 3PH |  |  |
|  | Max current (RMS) | 60 A |  |  |
|  | Output Frequency | 0-50HZ/60 HZ |  |  |
| a | Protection |
|  | Surge Protection | Integrated |  |  |
|  | overvoltage Protection |  |  |  |
|  | Under voltage Protection |  |  |  |
|  | Locked pump protection |  |  |  |
|  | Open circuit protection |  |  |  |
|  | Dry run protection |  |  |  |
| b | General data |
|  | Ambient Temperature Range | -10 to 55 °C |  |  |
|  | Cooling Method | Fan Colling |  |  |
|  | Ambient Humidity | 95% RH |  |  |
|  | Dimension (H*W*D) | 430*280*220 mm (min) |  |  |
|  | Gross Weight | 17 -21 kg |  |  |
|  | Efficiency | 97-98 % |  |  |
| 3 | Submit Manufacturer certification and test reports |  |  |
| 4 | Submit Detail drawing brochure catalogue. |  |  |

Item 1.3 / Fully Solar stand (KIT OF 6 PANELS EACH): (mechanical)

| No | Description | As per advertised BOQ | Offered by the bidder | Remark/Comment on proposed deviations (clearly explain any proposed deviations from the equipment/items requested in the BOQ) |
| --- | --- | --- | --- | --- |
|  | Number of solar panel | 6 solar panels each (1950×990mm) |  |  |
|  | Panels Platform dimensions | L 3 X W 4 m |  |  |
|  | Height | As per land elevation and sun ray direction. |  |  |
|  | Number of supports | 8 supports per each stand, each support fixed by 6 steel roll bolt M10x135 mm |  |  |
|  | Material of the panel | Aluminum |  |  |
|  | Structure | Hot dip galvanized steel with a standard of Zinc 80-120 (ASTM A526). |  |  |
|  | Module Rail | Aluminum EN AW-6063 T66 (W40xH40mm)and (W40xH70mm) and (W70xH70). |  |  |
|  | Material of the fixtures | Hot dip galvanized steel (grade 8.8). |  |  |
|  | Material of clamps | Z and U profiles are aluminum |  |  |
|  | Max. wind load | Up to 120km/hr |  |  |
|  | Type | Seasonal adjustable, fixed structure |  |  |
|  | Panel orientation | landscape or portrait |  |  |
|  | Submit Manufacturer certification and test reports | Submit Manufacturer certification and test reports. |  |  |
|  | Submit Detail drawing brochure catalogue. | Submit Detail drawings brochure catalogue. |  |  |

Item 1.7 / AC and DC protection:

| No. | Description | Required Specification | Bidder Offered | Remark/Comment on proposed deviations (clearly explain any proposed deviations from the equipment/items requested in the BOQ) |
| --- | --- | --- | --- | --- |
| 11 | AC & DC Surge Protection | 2P MDC 10kV and 3P MDC 30KV |  |  |
| 2 | Over-voltage Protection | Until 1000V |  |  |
| 3 | Under voltage protection | Until 200V |  |  |
| 4 | Locked pump protection | Integrated & Inbuilt type |  |  |
| 5 | Open circuit protection |  |  |  |
| 6 | Dry run protection |  |  |  |
| 7 | Submit Manufacturer certification and test reports |  |
| 8 | Submit Detail drawing brochure catalogue. |  |

Name of Bidder: ______________________________

Authorized signature: ______________________________

Functional Title: ______________________________

Company: ______________________________

Date: ______________________________