Annex 2

FORM FOR SUBMITTING SUPPLIER’S QUOTATION

(This Form must be submitted only using the Supplier’s Official Letterhead/Stationery)

We, the undersigned, hereby accept in full the UNDP General Terms and Conditions, and hereby offer to supply the items listed below in conformity with the specification and requirements of UNDP as per RFQ Reference No. 599-2020-UNDP-UKR-RFQ-RPP:

TABLE 1:  BRIEF COMPANY PROFILE

| BRIEF COMPANY PROFILE The Supplier must describe and explain how and why they are the best entity that can deliver the requirements of UNDP by indicating the following: |
| --- |
| Full registration name |  |
| Year of foundation |  |
| Legal status | If Consortium, please provide written confirmation from each member |
| Legal address |  |
| Actual address |  |
| Bank information |  |
| VAT payer status |  |
| Contact person name |  |
| Contact person email |  |
| Contact person phone |  |
| Company’s core activities |  |
| Profile – describing the nature of business, field of expertise, licenses, certifications, accreditations (If any); | Please indicate here |
| Business Licenses – Registration Papers, Tax Payment Certification, etc |  |
| Certificates and Accreditation | Please indicate here applicable including Quality Certificates, Patent Registrations, Environmental Sustainability Certificates, etc. |
| Please provide contact details of at least 2 previous partners for reference | Please attach minimum 2 recommendation letters from previous customers or copies of contract for provision of similar goods. |
| Company is not in the UN Security Council 1267/1989 List, UN Procurement Division List or Other UN Ineligibility List. | Please confirm (Answers: Yes, we are in the list/No, we are not in the list) |

TABLE 2:  Conformity to the specification

Lot 1. Computer and multimedia equipment

| # | Technical requirements (Features at least) | Conformity (Yes/No) | Offered Brand, Model and Exact characteristics |
| --- | --- | --- | --- |
| 1.1 | All-in-one computer (monoblock) Display diagonal: not less than 23.8 "; Matrix type: IPS; Maximum display resolution: at least 1920 x 1080; SSD capacity: not less than 256 GB; Processor: not less than Intel Core i3, 8th Generation or equivalent AMD Ryzen 3; RAM: at least 8 GB, DDR4 Ports: 4 x USB 3.1; 1 x HDMI input; 1 x HDMI output; 1 x LAN (RJ45); Additional features: Wi-Fi, Bluetooth modules; built-in speakers (2x3 W) Operating system: Windows 10 X64 Pro OEM Complete set must include: optical mouse (sensor resolution 1000 dpi), keyboard (Ukrainian/English layout), cables, documentation |  |  |
| 1.2 | Tablet Screen diagonal: not less than 10"; Screen resolution, not worse than: 2000x1200; Operating system: not lower than Android 9; Processor: not worse than Exynos 9611 Octa-core; Internal memory: at least 64 GB; RAM: not less than 4 GB; Stylus: Yes Complete set: compatible protective bumper, protective glass, stylus, documentation, charger |  |  |
| 1.3 | Laptop #1 Not less than Display: 15.6-inch FHD (1920 x 1080); Processor no worse than: Intel Core i3, 8th Generation or equivalent AMD processor; RAM: not less than 8 GB DDR4; Storage capacity and type: not less than 256 GB, SSD Additional: webcam, built-in microphone, built-in stereo speakers, Bluetooth, Wi-Fi, Ukrainian/Russian/English layout Interfaces: 1 x USB 2.0, 2 x USB 3.1, HDMI, LAN, combined audio jack Software: Windows 10 X64 Pro OEM Complete set: optical mouse (resolution 1000 dpi), documentation, power adapter |  |  |
| 1.4 | Laptop #2 Not less than Display: 17.3”, 1920x1080 Screen type: IPS CPU: Intel Core i5-9th Generation or equivalent AMD processor RAM: 8GB DDR4 SSD: 512GB Additional: webcam, built-in microphone, built-in stereo speakers, Bluetooth, Wi-Fi, Ukrainian/Russian/English layout Interfaces: 1 x USB 2.0, 2 x USB 3.1, HDMI, combined audio jack Software: Windows 10 X64 Pro OEM Complete set: laptop, optical mouse, documentation, power adapter |  |  |
| 1.5 | Microsoft Office 2019 with sticker 64-bit / Office version: for home and business / Language: Ukrainian / Program Package: Word, Exсel, PowerPoint, OneNote, Outlook / License: fixed for 1 PC |  |  |
| 1.6 | Smartphone Display: at least 6” Form factor: touch screen Battery capacity: at least 5000 mAh Resolution: at least 1080x1920 RAM: at least 6 GB Internal storage: at least 64 GB Rear camera: quad camera, at least 48+8+5+5 MP Front camera: 20 MP Operating system: Android 10 Number of SIMs: 2 Color: White Complete set: compatible protective bumper, protective glass, documentation, charger |  |  |
| 1.7 | Multifunctional device Printing technology: laser Print type: monochrome Maximum print format: A4 Maximum resolution, dpi: not less than 600 x 1200 Maximum speed of monochrome printing, not less than: 18 p/m Copy resolution, dpi: not less than 600 x 600 Maximum number of copies, not less than: 9 pcs Scanner type: tablet Optical scanner resolution: not less than 600 x 600 Number of print trays: 1 Supported paper sizes (main tray): A4, B5, LTR, LGL, EXE Interfaces: USB 2.0 Noise level: up to 60 dB |  |  |
| 1.8 | Multimedia projector Projection System: 3LCD Technology Color Light Output: 7,000-5,600 Lumen (economy mode) Resolution: WUXGA, 1920 x 1200, 16:10 High Definition: 4K enhancement Aspect Ratio: 16:10 Contrast Ratio: 50,000:1 Native Contrast: 2,000:1 Lamp (portrait mode):400 Watt, 2,000 hours Durability Interfaces: USB 2.0 Type A, USB 2.0 Type B (Service Only),RS -232C, Wired Network, Wireless LAN IEEE 802.11a/b/g/n (optional), VGA in, VGA out, DVI in,BNC in, HDBaseT, Stereo mini jack audio out, Stereo mini jack audio in (3x), HDMI (HDCP 2.2) |  |  |
| 1.9 | Ceiling mount for projector Distance from the ceiling: 55-1500 mm; Inclination: -15º +15º Compatibility with the projector Max load: 25 kg |  |  |
| 1.10 | Document scanner Scanner type: camera-scanner Maximum resolution: at least 1200x1200 Scanning speed: at least 20 pages per minute Maximum scanned area: A3 format Light source: built-in LED light |  |  |
| 1.11 | Desktop computer with LCD screen Main Unit Not less than CPU: Intel 6-Core i5 9th Generation RAM: 16 GB, DDR4 SSD capacity: 256 GB HDD capacity: 4 TB Graphics card: GeForce Radeon GT 1030 LCD screen: Size: 21.5" Type : IPS Resolution: 1920 x 1080 Complete set must include: main unit, monitor, optical mouse (sensor resolution 1000 dpi), keyboard (Ukrainian/English layout), cables, documentation |  |  |
| 1.12 | UPS Number of sockets: 8 Output power capacity: 405 W / 700 VA Input voltage range: 180-260V Surge protection and filtering |  |  |

Lot 2. STEM equipment

| # | Technical requirements (Features at least) | Conformity (Yes/No) | Offered Brand, Model and Exact characteristics |
| --- | --- | --- | --- |
| 2.1 | STEM-kit with programmable electronic module and set of sensors for practical classes in biology, physics, chemistry and geography Complete set must include: Mobile platform with integrated manipulator – 1 pc Weight of the transported cargo: not less than 1 kg; Continuous operation time: not less than 2 hours; Number of mobility steps: not less than 3; Built-in microcontroller with the following characteristics: - microcontroller: ATmega328; - USB-UART adapter (ATMega16u2); - additional drivers not required; The mobile platform with the integrated manipulator must include: - batteries - battery storage box Battery requirements: - type: Li-ion batteries with protection board - nominal capacity: not less than 3200 mAh Moving elements must be put in motion using servomotors Servomotors must be controlled by the I2C protocol. Interfaces for connecting additional devices: analog, digital, I2C, SPI. Microcontroller Arduino Uno – 2 pcs Type: ATmega328; Adapter type: USB-UART adapter (ATMega16u2), installation of additional drivers not required; Number of digital inputs / outputs: 14 (incl 6 PWM) Number of analog inputs: 6 Flash program memory: not less than 32Kb Operational memory: not less than 2Kb Body material: acrylic body Educational shield – 1 pc Adapted to the S4A learning environment by using the S4A-compatible ports. The educational shield must contain the following elements: Color LEDs: green – 2; red color - 2, yellow - 1, blue – 1; Photoresistive light sensor: 1 Clock buttons: 2 Piezzo buzzer: 1; RGB LED: 1; Number of servomotors connected simultaneously: 3 Accessible digital and analog ports of the controller. Battery – 2 pcs Type: Li-ion with protection board Nominal capacity: not less than 3200 mAh Maximum discharge current: not less than 4.8 A Nominal voltage: not less than 3.6 V Minimum voltage: not less than 2.75 V Maximum voltage: not less than 4.2 V Separate storage box: Yes Battery chargers: Yes Battery compartment – 1 pc Compartment for two batteries (type Li-ion with protection board) with series connection and available power connector 2.1x5.5 mm Breadboard power supply module 5V/3.3V – 1 pc Input voltage: DC 6 ~ 15V Output voltage to USB: 5V Output voltage on contacts: 3.3V / 5V Output current on USB: 500mA Output current on contacts: 1A-5V / 800mA-3.3V Overpadding protection Converter – 1 pc Converter type: step-down Input voltage: 5-48 V Output voltage: 0.5 - 40 V Maximum load current: not less than 3 A Voltage step-down converter with regulation of current and voltage – 1 pc Type: step-down voltage converter with output current and voltage limitation without galvanic isolation Conversion mode: asynchronous Input voltage: 8-36 V Output voltage: 1.25-32 V Minimum difference between input and output voltages: no more than 0.3 V Output current: adjustable, not less than 5 A Solar panel – 1 pc Operating voltage: not less than 5.5 V Operating current: not less than 170 mA Solderless breadboard – 2 pcs Number of points: 400 Number of power connection lines: 2 Self-adhesive surface on the reverse side Set of breadboard jumper wires, type M-M – 40 pcs Length: 200mm Set of breadboard jumper wires, type F-M – 40 pcs Length: 200mm Set of breadboard jumper wires, type F-F – 40 pcs Length: 200mm Set of jumper wires for Arduino – 1 pc 240mm – 5 pcs 200mm – 5 pcs 150mm – 8 pcs 110mm – 47pcs Infrared remote control and infrared receiver – 1 pc Maximum distance: not less than 8 m Effective angle: at least 60 degrees Number of control buttons: not less than 17 16-button membrane keyboard – 1 pc Flex length: not less than 86 mm Connector: 2.54mm pitch Maximum voltage: not more than 35 V, 100 mA Insulation resistance: not less than 100 MOhm, 100 V Sharpness of contacts: not more than 5 msec Lifetime: at least 1 million clicks Joystick – 1 pc Operating voltage: 5 V Availability of X-axis control Availability of Y-axis control Button: Yes Set of buttons with cap – 1 pc Contact resistance: not less than 100 mОhm Operating voltage: no more than 12V / 100 mA Mounting method: surface Lifetime: at least 100,000 times Size: 12 mm Number of buttons in the set: at least 5 Button caps of different colors Sensor module – 1 pc Number of channels: not less than 4 LED pressure indication is available Operating voltage: 2.4 V ~ 5.5 V RFID module – 1 pc Supply voltage: not more than 3.3 V Operating frequency: 13.56 MHz Reading range: 0 ~ 60 mm Interface: SPI, maximum transfer rate not less than 10Mbps Reading and writing RFID tags Includes: RFID module, access card, access keychain Real Time Clock module – 1 pc Thermal compensation and stride correction Counter of seconds, minutes, hours, days of the week, months and years with a calendar with a correction of the leap year until 2100 Stability of the generator: ± 2 ppm in the temperature range from 0 ° C - + 40 ° C Stability of the generator: ± 3,5 ppm in the temperature range from -40 ° C - + 85 ° C Accuracy of internal digital temperature sensor ± 3 ° C Clock accuracy correction register Programmable output of rectangular pulses 2 alarm clocks with the possibility of adjustment 2 I2C bus modes: Standard (100kHz) and Fast (400kHz) Operating supply voltage: from 3.0 V to 5.5 V Battery included Relay module 5 V 10 A with optocoupler – 1 pc Maximum switching current of the relay: not less than 10 A at 250 V Equipped with LED that indicates the current status of the relay contacts Encoder module – 1 pc Discreteness: at least 20 steps per rotation Slider variable resistor module – 1 pc Voltage: 3.3-5 V Signal: analog Resistance: not less than 10K Variable resistor – 2 pcs Nominal resistance: 10 kOhm Max. voltage: 150 V AC Nominal power: not less than 0.125 W Bluetooth module – 1 pc Communication protocol: Bluetooth Specification v2.0 + EDR Frequency: GFSK Sending power ≤4dBm, Class 2 Reception power ≤-84dBm at 0.1% BER Asynchronous speed: 2.1Mbps (Max) / 160 kbps, Synchronous speed: 1Mbps / 1Mbps Security authentication and encryption Bluetooth serial port profile Support for both slave and master mode Wi-fi module – 1 pc Protocol: WiFi 802.11 b / g / n Support for STA / AP / STA + AP modes Built-in TCP / IP protocol stack with support for multiple client connections (up to 5) D0 ~ D8, SD1 ~ SD3: can be used as GPIO, PWM, IIC, etc. Output current: 15 mA AD0: 1 ADC output Power supply: 4.5 - 9V (10V maximum) USB power supply with debugging interface Transmission speed: 110-460800 baud Support for UART / GPIO data interfaces Reflashing from the cloud or via USB Ethernet shield – 1 pc Operating voltage: 5 V Connection speed: 10/100 Mbps Compatible with 802.3 standard Support for TCP, UDP, IPv4, ICMP, ARP, IGMP and PPPoE protocols At least 16 Kbytes of internal data buffer Interaction with the controller via the SPI interface Integrated card reader: Yes MicroSD card 16GB Class 10 with adapter – 1 pc Fully complies with the standard SD 2.0 Compatible with card readers and devices that support MicroSDHC Compatible with Secure Digital Music Initiative (SDMI) Recording speed: at least 15 MB / sec Read speed: at least 80 MB / sec Multimeter – 1 pc Display: LCD 50x20 mm Power supply: Krona 9V battery, available in the set Constant voltage (DC), V: 200m / 2000m / 20/200/1000 Alternating voltage (AC), V: 200/750 DC, A: 2000μ / 20m / 200m / 10 Resistance, Ohm: 2000K / 200K / 20K / 2000/200 Possibility of testing diodes, transistors The multimeter has a built-in generator and a buzzer LED panel for visual indication of the output state of the microcontroller – 1 pc Supply voltage: 3.3-12 V Number of LEDs: not less than 6 pcs Type of indicators: common cathode Number of PIN connectors: at least 7 Schmitt Inverter Trigger 74HC14 – 1 pc Supply voltage: from 2V to 6V Output load capacity: 10 LSTTL inputs Static current consumption: 20 μA Signal delay time: 11 μs Output current: 4 mA at 5V Input current: less than 1 μA Housing type: DIP-14 Shear register 74HC595N – 4 pcs Housing type: PDIP-16 RoHS: Yes Technology: CMOS Operating voltage (typical): 2.5 / 3.3 / 5V Operating voltage (min.): 2V Operating voltage (max.): 6V Operating temperature range: -40 ... +85C Number of pins: 16 Set of resistors 0.25W – 1 pc 10 Ω – 20pcs 22 Ω – 20pcs 47 Ω – 20pcs 100 Ω – 20pcs 150 Ω – 20pcs 200 Ω – 20pcs 220 Ω – 20pcs 270 Ω – 20pcs 330 Ω – 20pcs 470 Ω – 20pcs 510 Ω – 20pcs 680 Ω – 20pcs 1 kΩ – 20pcs 2 kΩ – 20pcs 2.2 kΩ – 20pcs 3.3 kΩ – 20pcs 4.7 kΩ – 20pcs 5.1 kΩ – 20pcs 6.8 kΩ – 20pcs 10 kΩ – 20pcs 20 kΩ – 20pcs 47 kΩ – 20pcs 51 kΩ – 20pcs 68 kΩ – 20pcs 100 kΩ – 20pcs 220 kΩ – 20pcs 300 kΩ – 20pcs 470 kΩ – 20pcs 680 kΩ – 20pcs 1 MΩ – 20pcs LCD display – 1 pc I2C interface 16 x 2 format Power supply: not less than 5V OLED display – 1 pc Screen size: at least 0.96 " Screen type: OLED 4-pin supply voltage: 3.3-6 V Display resolution: at least 128 x 64 Availability of OLED module driver Viewing angle: not less than 160 degrees Availability of storage box Passive buzzer – 1 pc Power supply 3.3 - 5 V Buzzer – 1 pc Power supply 3.3 - 5 V LED matrix – 1 pc Supply voltage: 1.8-2.3 V Array size: at least 8 x 8 points The size of the matrix: 37 x 37 mm Nominal pixel current: 20 mA Output: anode Module of 4-point LED matrices – 1 pc Power supply: 5 V Complete set: 8x8 LED matrix Number of matrices: not less than 4 Soldered printed circuit board MAX7219 chip 10-segment 4-color progress bar – 1 pc 10 LEDs in one housing, each with its own anode and cathode. 4 colors: 2 red, 3 yellow, 4 green and 1 blue 7-segment 1-digit red LED indicator – 4 pcs RoHS: Yes Digit height: not less than 0.56 inches Output: cathode 7-segment 4-digit LED indicator – 1 pc Separators: vertical colon and decimal points Display type: 7-segment Number of digits: not less than 4 Digit height: not less than 0.56 inches Output: cathode Set of colored LEDs – 1 pc Red: 3 mm – not less than 10 pieces 5 mm – not less than 10 pieces Yellow: 3 mm – not less than 10 pieces 5 mm – not less than 10 pieces Green: 3 mm – not less than 10 pieces 5 mm – not less than 10 pieces Blue: 3 mm – not less than 10 pieces 5 mm – not less than 10 pieces White: 3 mm – not less than 10 pieces 5 mm – not less than 10 pieces Rated current: 20 mA LED-light - 4 pcs RGB type General cathode Diameter - not less than 5 mm The lens is matte Circle with LEDs – 1 pc Number of LEDs: not less than 12 Supply voltage: 4-7 V DC LED type: RGB WS2812 Interface: Single-wire consecutive Servomotor – 1 pc Speed without load: 0.12 sec / 60 degrees when powered by 4.8V Torque: 2 kg / cm Temperature range: 0 to + 50'C Dead zone width: 4 microseconds Operating supply voltage: 3.5-5 V Current consumption in motion: 50-80 mA Current consumption in stand-by: 5-10 mA Angle of rotation: 180 degrees Dimensions: 3.3 cm x 3 cm x 1.3 cm Stepper motor – 1 pc Nominal supply voltage: 5 V (direct current) Number of phases: 4 Number of strides: 64 Number of microstrides: 4096 Stride angle: 5.625 degrees Nominal frequency: 100 Hz Nominal resistance of coil (at 25 degrees): 50 Ohms Peak current of one coil: 320 mA Idling frequency (clockwise): 600 Hz Idling frequency (counterclockwise): 1000 Hz Torque (clockwise, at a frequency of 120 Hz): 34.3 N/m Pull in torque: 343 g/cm Electrical safety class: A Noise level <40dB Stepper motor driver – 1 pc Compatibility with 5V and 12V unipolar motors. Compatibility with standard Arduino Stepper library Number of light diodes: 4 (1 per channel) Micro electric motor – 2 pcs Supply voltage: 3-6 V Speed without load: at least 9000 ± 10% RPM Two-channel motor driver – 1 pc Power supply of motors: not less than 2.5 V - 15 V Operating voltage: from 2.7 V to 5.5 V Maximum motor current: 1.2 A (average) / 3.2 A (peak) Fan – 1 pc Engine type: brushless Dimensions: not less than 30 x 30 x 10 mm Nominal voltage: 5 V Resource: at least 35,000 hours Universal sound sensor – 1 pc Analog voltage output from the microphone Digital output of the threshold comparator Comparator: Yes Power indicator: Yes Digital output status indicator: Yes Operating voltage: 4 - 6 V Ultrasonic distance sensor – 1 pc Operating voltage 3.8 - 5.5 V The maximum distance: not less than 1500 mm The minimum distance: 0 cm Resolution: not less than 3 mm Pulse width: 10 μs Angle: 15 degrees Sensor mount: Yes Light sensor – 1 pc Sensitive element: photoresistor Adjustment of a threshold of operation by the variable resistor Operating voltage: from 3.3 V to 5 V Comparator: Yes Digital and analog outputs: Yes Infrared motion sensor – 1 pc Detection range: within at least 0-7 m Angle of operation: not less than 110 ° at a distance of up to 7 m Supply voltage: 4.5 - 12 V Delay time is not worse than 0.3 - 300 seconds with the possibility of adjustment Method of operation: repetitive and non-repetitive switching Infrared distance sensor – 1 pc Operating voltage: 4.5-5.5 V Output signal type: analog Average time for updating information for output: no more than 16.5 ms Measuring distance: not less than 10 to 80 cm Interference sensor – 1 pc Obstacle detection distance: not worse than 2-30 cm Operating voltage: 3.3 to 5 V Comparator: Yes Line sensor – 2 pcs Supply voltage: 3.3-5 V Fire sensor module – 1 pc Definition wavelength: 760nm ~ 1100 m. Operating voltage: 3.3 - 5 V Comparator: Yes Trigger angle: up to 60 degrees Detection distance: not less than 80 cm Infrared thermo module – 1 pc Operating voltage: from 3V to 5V Comparator: Yes Range of the measured temperature: at least 20 to 80 ° C Built-in digital output and supply voltage status indicator Digital and analog outputs Color sensor – 1 pc Color determination distance: not less than 10 mm Availability of high-quality conversion of light intensity into frequency Availability of connection directly to the microcontroller Operating voltage: 3 - 5 V RGB sensor and gesture sensor module – 1 pc RGBC light sensor, proximity and gesture detector with IR indicator in the optical module Detection distance: not less than 100 mm Sensitivity to different directions of movement Measurement of the direction and speed of approach and gestures Factory calibration Humidity and temperature sensor module – 1 pc Supply voltage: 3-5 V Measuring humidity range: not worse than within 20-90% RH ± 5% (max.) Measuring temperature range: not less than 0-50 ºC ± 2% (max.) Comparator: Yes Soil moisture sensor (hygrometer) – 1 pc Measuring element: metallized probe Comparator: Yes Sensor outputs: digital and analog Sensor supply voltage: 3.3 - 5 V Soil moisture sensor – 1 pc Humidity measurement method: capacitive Output type: analog Supply voltage: from 3.3 to 5.5 V Output voltage: from 0 V to 3.0 V Temperature sensor – 1 pc Operating voltage: from 3 V to 5.5 V Accuracy: ± 0.5 ° C in the range -10 ° C to + 85 ° C Operating temperature range: from -55 to 125 ° C Waterproof Interface: 1-wire Length of connecting wires: not less than 50 cm Thermistor – 1 pc Rated resistance: 100 Ohms (0 ° C) Measured temperature range: -20 ° C to +500 ° C (+/- 2.5 ° C) Accuracy: +/- 0.3 - 0.8 ° C (in the range 0-450 ° C) Length of connecting wires: not less than 50 cm Waterproof Barometer – 1 pc Supply voltage: 1.7-3.6 V Calibration: factory calibration Noise level: up to 0.2 Pa (1.7 cm) and 0.01 temperature Measured pressure range: from 300 hPa to 1100 hPa (9000 m to - 500 m) Accelerometer and gyroscope module – 1 pc Power supply: 3 - 5 V Gyroscope range: + 250 500 1000 2000 ° / s Accelerometer range: ± 2 ± 4 ± 8 ± 16 g I2C protocol Current sensor with analog output – 1 pc Supply voltage: from 3 to 36 V Measured current: from 0 A to 3 A Direction of current measurement: bidirectional CO2 sensor module – 1 pc Module supply voltage: 5 V Availability of digital and analog outputs Rain, moisture, snow sensor – 1 pc Power supply 3.3 - 5 V. Sensitive module dimensions: not less than 60 mm x 39 mm Comparator: Yes Liquid level sensor – 1 pc Operating voltage: 3 - 5 V Operating current: less than 20 mA Sensor type: analog Detection area: not less than 40 mm x 16 mm Hall sensor module – 1 pc Sensor type: unipolar Supply voltage: 4.5 - 24 V Heart rate sensor – 1 pc Supply voltage: 3 - 5 V Wire length: not less than 180 mm Wavelength (sensitivity peak): 565 nm Microwave motion sensor – 1 pc Supply voltage: 4 - 28 V Detection range: not less than 5 m Detection angle: not less than 120 degrees Transmitter power: up to 30 mW (nominal up to 20 mW) Delay time before trigger reset: 2 sec ± 30% Bend sensor – 1 pc Length: at least 2.2 inches (5.6 cm) Weight sensor (strain gauge) with control module – 1 pc Impedance: 1000 ± 50Ω Recommended voltage: within 5-10 V Maximum weight: not less than 2 kg Complex error margin: no more than 0.2% FS Pressure sensor – 1 pc Sensitive diameter: not less than 1.2 cm Resistance without pressure: more than 1 MО Weight detection range: not less than 100 g to 10 kg Width: 1.9 cm Impact sensor module – 1 pc Output type: contact tightened to the "+" power supply Number of outputs: 3 ("+", "-", sensor output) Vibration sensor – 1 pc Supply voltage: from 3.3 to 5 V Output: digital Comparator: Yes Tilt and vibration sensor module – 1 pc Comparator: Yes Operating voltage from 3.3 V to 5 V Availability of digital output Sensor module of allotropic modification of oxygen (O3) – 1 pc Sensor type: semiconductor Main registered gas: allotropic modification of oxygen (O3 - Ozone) Gas concentration measurement range: 10-1000 ppm Heater supply voltage: 5V DC or AC Heater resistance: 31 Ohm Heater power consumption: 900mW Sensor resistance: 50-500 kOhm (at 50ppm O3) PH sensor – 1 pc Supply voltage: 3.3 ~ 5.5 V Output voltage: 0 ~ 3.0 V Signal connector: PH2.0-3P Measurement accuracy: ± 0.1@25 Probe type: laboratory Detection range: 0 ~ 14 Temperature range: 5 ~ 60°C Zero point: 7 ± 0.5 Response time: <2 min Internal Resistance: <250 MО GPRS/GSM + GPS module – 1 pc Operating bands: 850/900/1800/1900 MHz GPRS mobile stations class: B Operation: AT command (3GPP TS 27.007, 27.005 and SIMCOM improved AT commands) Navigation: built-in GPS / CNSS with A-GPS support Logic levels: from 3.0 V to 5.0 V Consumption in sleep mode: less than 1 mA Supported protocols: GPS NMEA SIM card port: Micro SIM Data transfer: GPRS multi-slot class 12, max. SPEED 85.6kbps Supply voltage: from 5 V to 12 V GSM antenna included GPS antenna included Organizer for small details – 1 pc Material: plastic or wood Number of compartments: at least 10 Study guide on Scratch for Arduino programming fundamentals – 1 pc Language: Ukrainian Each topic of the manual should contain theoretical and practical material. Practical and / or laboratory works (not less than 2) are developed for each topic in accordance with one of the curricula for labor training, computer science, physics, chemistry, biology, mathematics, geography. Practical and / or laboratory work should include: goal setting, problem statement, information and computer model, description of a computer experiment. Contains description of the integrated educational project. |  |  |

Lot 3. Video studio equipment

| # | Technical requirements (Features at least) | Conformity (Yes/No) | Offered Brand, Model and Exact characteristics |
| --- | --- | --- | --- |
| 3.1 | Holographic screen with rack and mounts Screen diagonal: not less than 27" Rack and mounting material: metal The rack should provide simultaneous fastening for holographic screen, multimedia short-focus projector, laptop The rack must be equipped with wheels |  |  |
| 3.2 | Multimedia projector Resolution: at least XGA (1024x768) Brightness: not less than 3700 ANSI lm Contrast: not less than 24000:1 Minimum projection distance: 0.54 meters Lamp life: at least 7,000 hours in standard mode and at least 15,000 hours in economy mode. Interface cable: not less than 10 meters Speaker: not less than 10 Wt |  |  |
| 3.3 | Contactless control system Type: Motion controller Features: Recognition of fingers of two hands Provides full control of the computer functions USB 2.0 interface OS: Windows 7/8, Mac OS X 10.7, Linux |  |  |
| 3.4 | Camera with 2 interchangeable lenses Camera type: SLR camera, with interchangeable lens Matrix type: CMOS (CMOS) Matrix: not worse than APS-C (20.7x13.8 - 28.1x18.7 mm) Number of megapixels: at least 24 Mpix Continuous shooting, frames / sec: not less than 10 File format: JPEG, RAW Focus distance: 15-45 mm Lens aperture: f/3.5-6.3 Display (diagonal): not less than 3.0” Maximum video resolution: 3840x2160 (4K) Video quality: not worse than HDR Frame rate: FullHD, 120 fps Exposure: 30-1/4000 s, manual prolonged exposure Memory card support: SD/SDHC/SDXC Additional interfaces: Bluetooth, NFC, Wi-Fi Lenses in the set: EF-M 15-45mm f/3.5-6.3; EF-M 55-200mm f/4.5-6.3 |  |  |
| 3.5 | SD memory card Memory capacity: at least 64 GB Speed ​​class (SD): not worse than UHS-I |  |  |
| 3.6 | Camera tripod Head type: 3D Removable head: None Maximum shooting height: 161 cm Number of sections: 3 Minimum shooting height: 64.5 cm Maximum load: 3.5 kg |  |  |
| 3.7 | Wall/ceiling mount system for 3 backgrounds Width: 2.72m Mounting type: metal anchors |  |  |
| 3.8 | Set of 3 paper backgrounds Color: White, Grey, Green Material: Paper Width: 2.72 m Length: 11 m |  |  |
| 3.9 | Set of constant diode light Number of softboxes: 2 Number of stands: 2 Number of 12W lamps: 8 Light power: 1200 W Electric power: 96 W Color temperature of lamps: 5500 K Lamp life: 30,000 hours Light type: diode Power adjustment: yes Minimum stand height: 0.8 m Maximum stand height: 2.0 m Tilt adjustment: yes |  |  |
| 3.10 | Studio crane with rack for studio lamps Type: stand Crossbar type: 2-section Length of crossbeam: 121 - 211 cm Diameter of the coupling: 1/4 "and 3/8" Counterweight weight: 0.3 kg |  |  |
| 3.11 | Light source (LED illuminator) Power: 60 W Color rendering index (CRI): 93 Color temperature: 3200K Power adjustment: Yes Remote control: Yes Bayonet standard: Bowens Luminous power: 4100 Lm |  |  |
| 3.12 | Deep reflector with Bowens bayonet The reflector creates a directed light flux with high contrast and clear boundaries. Reflector material: temperature-proof metal Diameter: at least 28 cm Depth: at least 34.5 Bayonet: Bowens |  |  |
| 3.13 | Wireless microphone system with 2 receivers and 2 lavalier microphones Wireless transmission: digital 2.4 GHz Number of transmitters: 2 x bodypack with microphone Max operating range: not less than 50 m RF output power: 3 mW Included cable connector: 1/8” / 3.5 mm TRS Microphone form factor: lavalier Polar pattern: omnidirectional SNR: 84 dB |  |  |
| 3.14 | Study materials on using multimedia and holographic technology in STEM Language: Ukrainian Accredited for using in educational institutions |  |  |

TABLE 3:  Financial offer for the supply of goods in accordance with the technical specification and

Requirements

Lot No. 1. Computer and multimedia equipment

| No. | Product name and specification requirements | Quantity of units (pcs / pair) | Unit price, without VAT, currency | Total price, without VAT, currency |
| --- | --- | --- | --- | --- |
| 1.1 | All-in-one computer (monoblock) | 14 |  |  |
| 1.2 | Tablet | 18 |  |  |
| 1.3 | Laptop #1 | 32 |  |  |
| 1.4 | Laptop #2 | 18 |  |  |
| 1.5 | Microsoft Office 2019 with sticker | 18 |  |  |
| 1.6 | Smartphone | 20 |  |  |
| 1.7 | Multifunctional device | 28 |  |  |
| 1.8 | Multimedia projector | 1 |  |  |
| 1.9 | Ceiling mount for projector | 1 |  |  |
| 1.10 | Document scanner | 4 |  |  |
| 1.11 | Personal computer with LCD screen | 4 |  |  |
| 1.12 | UPS block | 4 |  |  |
|  | Cost of delivery | 1 |  |  |
| Total, without VAT, currency |  |

Lot No. 2. STEM equipment

| No. | Product name and specification requirements | Quantity of units (pcs / pair) | Unit price, without VAT, currency | Total price, without VAT, currency |
| --- | --- | --- | --- | --- |
| 2.1 | STEM-kit with programmable electronic module and set of sensors for practical classes in biology, physics, chemistry and geography | 20 |  |  |
|  | Cost of delivery | 1 |  |  |
| Total, without VAT, currency |  |

Lot No. 3. Video studio equipment

| No. | Product name and specification requirements | Quantity of units ( pcs / pair) | Unit price, without VAT, currency | Total price, without VAT, currency |
| --- | --- | --- | --- | --- |
| 3.1 | Holographic screen with rack and mounts | 2 |  |  |
| 3.2 | Multimedia projector | 2 |  |  |
| 3.3 | Contactless control system | 2 |  |  |
| 3.4 | Camera with 2 interchangeable lenses | 2 |  |  |
| 3.5 | SD memory card | 4 |  |  |
| 3.6 | Camera tripod | 4 |  |  |
| 3.7 | Wall/ceiling mount system for 3 backgrounds | 2 |  |  |
| 3.8 | Set of 3 paper backgrounds | 2 |  |  |
| 3.9 | Set of constant diode light | 2 |  |  |
| 3.10 | Studio crane with rack for studio lamps | 2 |  |  |
| 3.11 | Light source (LED illuminator) | 2 |  |  |
| 3.12 | Deep reflector with Bowens bayonet | 2 |  |  |
| 3.13 | Wireless microphone system with 2 receivers and 2 lavalier microphones | 2 |  |  |
| 3.14 | Study materials on using multimedia and holographic technology in STEM | 2 |  |  |
|  | Cost of delivery | 1 |  |  |
| Total, without VAT, currency |  |

TABLE 4: Offer to Comply with Other Conditions and Related Requirements

| Other Information pertaining to our Quotation are as follows: | Your Responses |
| --- | --- |
|  | Yes, we will comply | No, we cannot comply | If you cannot comply, pls. indicate counter proposal |
| Delivery time (Delivery of equipment must be carried out within 60 (sixty) calendar days from PO/Contact signature date) |  |  |  |
| Compliance with technical requirements |  |  |  |
| Delivery terms: DDP – 15, Stusa street, Kramatorsk, Donetsk oblast, 84300, Ukraine DDP – 1, Miendielieieva street, Rubizhne, Luhansk oblast, 93000, Ukraine DDP – 8, Yehorova street, Sievierodonetsk, Luhansk oblast, 93400, Ukraine DDP – 52 Starovokzalna str., office 12, Dnipro, Territorial department of the Ministry of veterans in Dnipropetrovsk oblast DDP – 3/14 Maidan Koroliova, 10014 Zhytomyr, Territorial department of the Ministry of veterans in Zhytomyr oblast |  |  |  |
| Products meet the required quality standards. |  |  |  |
| Warranty and After-Sales Requirements: Not less than 12 months warranty service in Ukraine |  |  |  |
| Availability of warranty service in Ukraine |  |  |  |
| Validity of Quotation (min. 60 days) |  |  |  |
| All Provisions of the UNDP General Terms and Conditions. https://www.undp.org/content/undp/en/home/procurement/business/how-we-buy.html |  |  |  |

All other information that we have not provided automatically implies our full compliance with the requirements, terms and conditions of the RFQ.

[Name and Signature of the Supplier’s Authorized Person]

[Designation]

[Date]

This serves as a guide to the Supplier in preparing the quotation and price schedule.

Official Letterhead/Stationery must indicate contact details – addresses, email, phone and fax numbers – for verification purposes