AMENDMENT TO THE RFQ 689 - Design adaptation of the room and equipment installation/replacing in the building of the Institute of Public Health „Dr Milan Jovanović – Batut“ in Belgrade

30 March 2021

# Please note that two more position codes (01-40 as well as 01-41) has been added to the RFQ SCHEDULE OF REQUIREMENTS, under the TEKUCE ODRZAVANJE/CURRENT MAINTENANCE section. Therefore, RFQ document has been amended on the page 18 as follows:

| 01-40 | Čajna kuhinja: instalacije vodovoda i kanalizacije i oprema | Kitchenette: sanitary network installations and equipment |  |  |
| --- | --- | --- | --- | --- |
| 01-41 | Instalacije vodovoda i kanalizacije izvesti prema sledećoj specifikaciji: | Water supply and sewerage installations: |  |  |
|  | - Nabavka, transport i montaža, transport i montaža vodovodnih polipropilenskih cevi Ø 15 (d20mm), (kao tip proizvođača AQUATHERM ili ekvivalent) i fitinga zajedno sa materijalom potrebnim za spajanje. Cevi treba fiksirati original obujmicama sa unutrašnjim delom obloženim gumom, na propisanom rastojanju u zavisnosti od temperature i dimenzije, po uputstvu proizvođača. Iste termički izolovati izolacijom debljine 9mm (kao tip ARMAFLEX ili sličan), a cevi montarine u zidu izolacijom debljine 4mm. | - Procurement, transport and installation, transport and installation of polypropylene water pipes Ø 15 (d20mm), (as the type of manufacturer AQUATHERM or equivalent) and fittings together with the material required for connection. The pipes should be fixed to the original with clamps with an inner part coated with rubber, at the prescribed distance depending on the temperature and dimensions, according to the manufacturer's instructions. Thermally insulate them with 9mm thick insulation (like ARMAFLEX or equivalent), and mount the pipes in the wall with 4mm thick insulation. |  |  |
|  | - Nabavka, transport i montaža, transport i montaža ravnih ppr ventila Ø 15 (d20mm), sa hromiranom kapom i rozetom za radni pritisak do 10 bara. | - Procurement, transport and installation, transport and installation of flat prpr valves Ø 15 (d20mm), with chrome cap and rosette for working pressure up to 10 bar. |  |  |
|  | - Nabavka, transport i montaža, transport i montaža troslojnih kompozitnih cevi i fazonskih komada Ø 75 i Ø 50, (kao tip MASTER 3 poizvođača PIPELIFE ili sličan proizvod. | - Procurement, transport and installation, transport and installation of three - layer composite pipes and fittings Ø 75 and Ø 50, (as type MASTER 3 manufacturer PIPELIFE or equivalent product. |  |  |
|  | - Nabavka, transport i montaža, transport i montaža komplet niskomontažnog električnog bojlera 10l, sa sigurnosnim ventilom (kao tip proizvođača Ariston ili ekvivalent). Bojler montirati na zid. Spoj sa instalacijom vodovoda izvršiti hromiranim cevima. | - Procurement, transport and installation, transport and installation of a set of low-installation electric water heater 10l, with safety valve (as the type of manufacturer Ariston or equivalent). Mount the boiler on the wall structure. Make the connection with the plumbing installation with chrome pipes. |  |  |
|  | Cenom je obuhvaćeno probijanje otvora u zidovima i plafonima, štemanje šliceva, kao i krpljenje istih. Uračunat je kompletan materijal potreban za pričvršćenje i povezivanje sanitarne mreže na postojeću. Demontiran materijal i šut prikupiti, upakovati u džakove, izneti, utovariti na kamion i odvesti na gradsku deponiju udaljenu do 30km. | The price includes drilling openings in the walls and ceilings, trimming the slots, as well as patching them. The complete material needed for fastening and connecting the sanitary network to the existing one is included. Collect the dismantled material and rubble, pack it in bags, take it out, load it on a truck and take it to the city dump up to 30 km away. |  |  |
|  | Obračun po komadu komplet izvedene pozicije | Calculation per piece set of derived position | kom/pcs | 1.00 |

# Accordingly, the Annex 3.A. FORM OF THE FINANCIAL PROPOSAL is hereby amended and attached as separate excel file, named “AMENDED Annex 3.A. FORM OF THE FINANCIAL PROPOSAL”.