Equipment for Environmental Quality Monitoring (AIR, SOIL, WATER)

| S/N | Description | Specification | Environmental Media | Quantity |
| --- | --- | --- | --- | --- |
| 1 | Mercury Analyzer with accessories | Automated with decomposition furnace; detection limit as low as 0.005ng of Hg; Precision < 1.5% @ 10 ng Hg | Soil, Water, Sediments, Sludge, minerals, ores, fertilizers, foodstuffs, urine, hair, fly ash, coal | 1 Set |
| 2 | Water Quality Meter | Multi-meter with electrodes (probes); capable of measuring at least four of TDS, ORP, Salinity, pH, EC | Water | 3 pcs |
| 3 | Cuvette | 25 ml round glass vials with lids used for spectrometry analysis | Water | 10 pcs |
| 4 | Cool box | Onsite sample storage | Water | 3 pcs |
| 5 | Soil Quality Tester | Multi-meter with probes capable of measuring soil pH, moisture and temperature | Soil | 3 pcs |
| 6 | Soil EC Meter | Capable of measuring electric conductivity in soil | Soil | 3 pcs |
| 7 | Soil Auger | Stainless steel for soil sampling at minimum 50 cm depth | Soil | 3 pcs |
| 8 | Air Particulate Meter | Outdoor monitoring of PM2.5, PM10 | Air | 3 pcs |
| 9 | Air Quality Meter | Multi-meter with sensors for CH4, VOC, H2S, NO2, SO2, CO, O3 | Air | 3 Sets |
| 10 | Soxlets apparatus | Glass for sample separation | Water, Soil | 2 pcs |
| 11 | Magnetic stirrer | Electronic set for sample preparation | Water, Soil | 1 pc |
| 13 | Analytical balance | Electronic with minimum readings as low as 0.001 g | Soil | 1pc |