ANNEX 1: SCHEDULE OF REQUIREMENTS

# The equipment is being procured within project "Support to Economic Development at the Local Level in the Republic of Belarus", funded by the European Union and implemented by the United Nations Development Programme in partnership with the Ministry of Economy of the Republic of Belarus.

# Lot 1 – multi-needle embroidery machines with accessories (2 machines with accessories)

# Procurement is realized within implementation of the following entrepreneurial initiatives supported by the project: № 20-726 “Ya ne poteryayus’ ili dizajnerskie utyazhelyonnye zhilety dlya detej s autizmom” [I WILL NOT LOSE or designer weighted vests for children with autism], № 20-878 “Novyj rubezh”[ New frontier].

# General requirements and purpose of procurement: procurement of the embroidery machine within implementation of the initiative № 20-726 “Ya ne poteryayus’ ili dizajnerskie utyazhelyonnye zhilety dlya detej s autizmom” [I WILL NOT LOSE or designer weighted vests for children with autism] is required for manufacture of designer weighted vests and sensory bags made of special tough fabric for children with autism and children with psychophysical disabilities at the manufacturing facility located in Orsha district of Vitebsk region.

# Procurement of the embroidery machine within implementation of the initiative № 20-878 “Novyj rubezh” [New frontier] is required to expand the range of products manufactured by the enterprise producing souvenir and promo goods (T-shirts, baseball caps, promotional bags, etc.) from natural fabrics (linen, cotton, textiles, mixed fabrics) with elements of national features, located in Baran, Vitebsk region.

| Item to be Supplied and Quantity | Description / Specifications of Goods (according to the RFQ) and General Requirements | Statement of Compliance with Specifications (according to the RFQ) and General Requirements Comply / Does not comply | Description / Specifications of Goods (according to the purchase order) and Related Services Please indicate parameters of the offered goods as below |
| --- | --- | --- | --- |
| I. Technical Specifications: |
| 1. Embroidery machine – 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type: computerized, industrial one-head machine for embroidery on end-product, including caps, baseball caps, T-shirts and other tough fabric |  | Please indicate the offered parameters: |
|  | 2. Number of needles: at least 10 |  | Please indicate the offered parameters: |
|  | 3. Sewing speed: at least 400 stitches / min | - | Please indicate the offered parameters: |
|  | 4. System of automatic thread cutting: availability |  | Please indicate the offered parameters: |
|  | 5. Thread break sensor: availability |  | Please indicate the offered parameters: |
|  | 6. Display: color, touch screen |  | Please indicate the offered parameters: |
|  | 7. PC connection interface: USB; function of downloading embroidery programs from a USB-carrier; reading information from SD memory card |  | Please indicate the offered parameters: |
|  | 8. Software that allows to develop custom embroidery designs for the machine |  | Please indicate the offered parameters: |
| 2. Embroidery machine – 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type: computerized, one-head, 10-needle embroidery machine |  | Please indicate the offered parameters: |
|  | 2. Sewing area: at least 310 x 200 mm. |  | Please indicate the offered parameters: |
|  | 3. Number of needles: 10 pcs. |  | Please indicate the offered parameters: |
|  | 4. Number of built-in embroidery designs: at least 110 |  | Please indicate the offered parameters: |
|  | 5. Maximum sewing speed: 1000 stitches / min. |  | Please indicate the offered parameters: |
|  | 6. Cylindrical platform for embroidery on end products (at least on baseball caps): availability |  | Please indicate the offered parameters: |
|  | 7. Display: color, touch screen |  | Please indicate the offered parameters: |
|  | 8.Function of automatic upper and lower thread cutting: availability |  | Please indicate the offered parameters: |
|  | 9. PC connection interface: USB |  | Please indicate the offered parameters: |
|  | 10. Weight: no more than 50 kg. |  | Please indicate the offered parameters: |
| II. General Requirements: |
| 1. Operation and maintenance manual, technical passport, warranty booklet: in Russian (to be supplied with the goods) |  | Please enumerate the documents as part of a package deal and their language: |
| 2. Year of manufacture: brand new, not being used or repaired, refurbished or rehabilitated |  | Please indicate year of manufacture and confirm that the equipment is brand new: |
| 3. Delivery: delivery of all necessary equipment and components is carried out by the Contractor on the following terms: - embroidery machine (as per item 1 of Technical Specification) - DAP Orsha, Vitebsk region, Republic of Belarus (INCOTERMS 2010), or Delivery Terms (Delivery to the Purchaser’s warehouse): Delivery by the Contractor’s transport and at the Contractor’s cost to Vitebsk region, Orsha district, v. Dachnaya, Parkovaya str. 6б (for the delivery from the territory of the Republic of Belarus); - embroidery machine (as per item 2 of Technical Specification) - DAP Orsha, Vitebsk region, Republic of Belarus (INCOTERMS 2010), or Delivery Terms (Delivery to the Purchaser’s warehouse): Delivery by the Contractor’s transport and at the Contractor’s cost to Zarechnaya str. 4; 211011 Baran’, Vitebsk region (for the delivery from the territory of the Republic of Belarus). The supplied equipment will be checked at the place of delivery by the Customer's specialists and technical specialists of the end user for compliance with the declared quality and technical specification. |  | Please сonfirm the terms of delivery: |
| 4. Warranty: - Warranty for equipment for a period of at least 12 (twelve) months from the date of acceptance of the goods by UNDP in an authorized service center certified by the manufacturer; - After acceptance of the goods by UNDP, the right to use the warranty obligations for the goods passes from UNDP to the End User of the goods: - 1st embroidery machine as per item 1 of the Technical Specification - LLC «СЕА», - 2nd embroidery machine as per item 1 of the Technical Specification - Unitary enterprise "Baran'skie Arabeski”. |  | Please confirm the terms and indicate the warranty period: |
| 5. Warranty Service Requirements: - availability of a service center on the territory of the Republic of Belarus authorized and certified by the manufacturer; - the Contractor shall ensure warranty repairs, restoration of normal functioning of the Goods and replacement of faulty parts of the supplied Goods at the request of the Purchaser or the End-user within 30 calendar days upon receipt of such request. The Contractor guarantees that during the warranty period transportation of the Goods and parts and units of the Goods from the place of the Goods operation to the service center of the Contractor / authorized local representative of the Contractor and back to the place of operation in order to perform warranty repairs and servicing, if required, shall be done at the Contractor’s cost |  | Please indicate the name and address of the service center that provides warranty service of the sewing equipment: Please indicate the period of restoration of goods operation or its replacement: |

Signature:

Name: 	Click or tap here to enter text.

Title:	Click or tap here to enter text.

# Date:  	Click or tap to enter a date.

# Lot 2 – Sewing machines with accessories (7 machines with accessories), ironing systems (2 systems)

# Procurement is realized within implementation of the following entrepreneurial initiatives supported by the project: № 20-726 “Ya ne poteryayus’ ili dizajnerskie utyazhelyonnye zhilety dlya detej s autizmom” [I WILL NOT LOSE or designer weighted vests for children with autism], №20-832 “Rasshireniedeyatel’nostiatel’epoindividual’nomuposhivuodezhdynazakaz “TRIS”” [Expansion of activities of TRIS atelier for individual tailoring of clothes to order "TRIS”], № 20-878 “Novyj rubezh”[New frontier].

# General requirements and purpose of procurement: procurement of the equipment within implementation of the initiative № 20-726 “Ya ne poteryayus’ ili dizajnerskie utyazhelyonnye zhilety dlya detej s autizmom” [I WILL NOT LOSE or designer weighted vests for children with autism] is required for manufacture of designer weighted vests and sensory bags made of special tough fabric for children with autism and children with psychophysical disabilities at the manufacturing facility located in Orsha district of Vitebsk region.

# Procurement of the equipment within implementation of the initiative №20-832 Rasshireniedeyatel’nostiatel’epoindividual’nomuposhivuodezhdynazakaz “TRIS”” [Expansion of activities of TRIS atelier for individual tailoring of clothes to order "TRIS”] will expand the range of services, improve the quality of services, and reduce the lead time of the atelier located in Molodechno of Minsk region.

# Procurement of the equipment within implementation of the initiative № 20-878 “Novyj rubezh” [New frontier] is required to expand the range of products manufactured by the enterprise producing souvenir and promo goods (T-shirts, baseball caps, promotional bags, etc.) from natural fabrics (linen, cotton, textiles, mixed fabrics) with elements of national features, located in Baran, Vitebsk region.

| Item to be Supplied and Quantity | Description / Specifications of Goods (according to the RFQ) and General Requirements | Statement of Compliance with Specifications (according to the RFQ) and General Requirements Comply / Does not comply | Description / Specifications of Goods (according to the purchase order) and Related Services Please indicate parameters of the offered goods as below |
| --- | --- | --- | --- |
| I. Technical Specifications: |
| 1. Sewing machine for quilting – 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type: sewing computerized quilting machine |  | Please indicate the offered parameters: |
|  | 2. Number of operating modes: at least 350 |  | Please indicate the offered parameters: |
|  | 3. Stitch length adjustment: maximum stitch length at least 5 mm |  | Please indicate the offered parameters: |
|  | 4. Stitch width adjustment: maximum stitch width at least 7 mm |  | Please indicate the offered parameters: |
|  | 5. Twin needle sewing |  | Please indicate the offered parameters: |
|  | 6. The function of disabling of the bottom conveyor for sewing curly appliqués |  | Please indicate the offered parameters: |
|  | 7. The number of operating modes for making buttonholes (types of buttonholes): at least 12 |  | Please indicate the offered parameters: |
|  | 8. Function of sewing without pedal: availability |  | Please indicate the offered parameters: |
|  | 9. Screen: availability |  | Please indicate the offered parameters: |
| 2. Sewing machine – 1 pc. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type: computerized sewing machine for quilting (embroidery) |  | Please indicate the offered parameters: |
|  | 2. Number of operations performed: at least 350 |  | Please indicate the offered parameters: |
|  | 3. The function of deactivation of lower fabric feed for free motion stitching |  | Please indicate the offered parameters: |
|  | 4. Free-motion stitch foot: availability |  | Please indicate the offered parameters: |
|  | 5. Screen: availability |  | Please indicate the offered parameters: |
| 3. Сoverstitch sewing machine – 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type: flatbed electromechanical coverstitch sewing machine |  | Please indicate the offered parameters: |
|  | 2. Number of needles: 3 pcs |  | Please indicate the offered parameters: |
|  | 3. Number of threads: 5 pcs. |  | Please indicate the offered parameters: |
|  | 4. Stitch length adjustment |  | Please indicate the offered parameters: |
|  | 5. Table for the installation of the proposed machine model: to be supplied with a machine |  | Please indicate the offered parameters: |
|  | 6. Built-in servo motor: availability |  | Please indicate the offered parameters: |
| 4. Embroidery machine – 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type: computerized, embroidery |  | Please indicate the offered parameters: |
|  | 2. Types of fabric sewn by the machine: from thin and fine fabric (natural silk) to extra-dense (woolen cloth, genuine leather) |  | Please indicate the offered parameters: |
|  | 3. Built-in top fabric conveyor (with a dual feed system): availability |  | Please indicate the offered parameters: |
|  | 3. Number of operations performed: at least 690 types |  | Please indicate the offered parameters: |
|  | 4. Buttonhole: at least 15 types (automatic) |  | Please indicate the offered parameters: |
|  | 5. Maximum size of embroidery: at least 200 × 400 mm |  | Please indicate the offered parameters: |
|  | 6. Size of free arm platform (distance to the right of the needle): at least 250 mm |  | Please indicate the offered parameters: |
|  | 7. PC connections for downloading embroidery programs: availability of USB port |  | Please indicate the offered parameters: |
|  | 8. Power: at least 100 W |  | Please indicate the offered parameters: |
|  | 9. Software that allows to develop custom embroidery designs on a PC in a format read by an embroidery machine |  | Please indicate the offered parameters: |
|  | 10. Table for installation of the proposed machine model: to be supplied with a machine |  | Please indicate the offered parameters: |
| 5. Sewing machine – 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1.Type: computerized |  | Please indicate the offered parameters: |
|  | 2. Types of fabric sewn by the machine: from thin and fine fabric (natural silk) to extra-dense (woolen cloth, genuine leather) |  | Please indicate the offered parameters: |
|  | 3. Built-in top fabric conveyor (with a dual feed system): availability |  | Please indicate the offered parameters: |
|  | 4. Loop-taker (shuttle): horizontal, rotary |  | Please indicate the offered parameters: |
|  | 5. Number of operations performed: at least 350 types |  | Please indicate the offered parameters: |
|  | 6. Buttonhole: automatic, at least 20 types |  | Please indicate the offered parameters: |
|  | 7. Size of free arm platform: (distance to the right of the needle): at least 300 mm |  | Please indicate the offered parameters: |
|  | 8. Power: at least 85 W |  | Please indicate the offered parameters: |
|  | 9. Table for installation of the proposed machine model: to be supplied with a machine |  | Please indicate the offered parameters: |
| 6. Sewing machine – 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type: lockstitch, computerized |  | Please indicate the offered parameters: |
|  | 2. Types of fabric sewn by the machine: lightweight, mediumweight, heavyweight, knitted fabric |  | Please indicate the offered parameters: |
|  | 3. Stitch width adjustment: maximum stitch width at least 7 mm. |  | Please indicate the offered parameters: |
|  | 4. Stitch length adjustment: maximum stitch length at least 5 mm. |  | Please indicate the offered parameters: |
|  | 5. Number of stitch types: at least 340 |  | Please indicate the offered parameters: |
|  | 6. Buttonhole mode: at least 9 types of buttonholes |  | Please indicate the offered parameters: |
|  | 7. Built-in alphabet for letter embroidery on fabric: at least Latin, Russian |  | Please indicate the offered parameters: |
|  | 8. Adjustment of height of the sewing foot lift: maximum height lift of sewing foot is at least 10 mm |  | Please indicate the offered parameters: |
|  | 9. Screen: availability |  | Please indicate the offered parameters: |
|  | 10. Working surface: at least 25 cm to the right of the needle |  | Please indicate the offered parameters: |
|  | 11. Work surface lighting: LED |  | Please indicate the offered parameters: |
|  | 12. Automatic thread cutting function: availability |  | Please indicate the offered parameters: |
| 7. Overlock machine - 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type of fabric sewn by the machine: at least mediumweight, heavyweight fabric |  | Please indicate the offered parameters: |
|  | 2. Number of needles: 2 pcs. |  | Please indicate the offered parameters: |
|  | 3. Distance between needles: at least 2 mm. |  | Please indicate the offered parameters: |
|  | 4. Number of threads: 4 pcs. |  | Please indicate the offered parameters: |
|  | 5. Stitch width adjustment: maximum stitch width is at least 4 mm |  | Please indicate the offered parameters: |
|  | 6. Stitch length adjustment: maximum stitch length is at least 4 mm |  | Please indicate the offered parameters: |
|  | 7. Maximum sewing speed: at least 6500 stiches / min. |  | Please indicate the offered parameters: |
|  | 8. Height of the sewing foot lift: at least 6 mm |  | Please indicate the offered parameters: |
|  | 9. Servomotor: availability |  | Please indicate the offered parameters: |
|  | 10. Recessed overlock table: to be supplied with overlock |  | Please indicate the offered parameters: |
| 8. Ironing system - 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type: ironing system, consisting of an ironing board with a steam blowing and suction function, a steam generator, an iron, an ironing arm |  | Please indicate the offered parameters: |
|  | 2. Working surface of board: at least 120 x 44 сm. |  | Please indicate the offered parameters: |
|  | 3. Availability of steam supply regulator, maximum steam pressure: at least 5.0 bar |  | Please indicate the offered parameters: |
|  | 4. Volume of water tank of steam generator: at least 1 litre |  | Please indicate the offered parameters: |
|  | 5. Operational readiness: no more than 4 min |  | Please indicate the offered parameters: |
|  | 6. Ironing arm: availability |  | Please indicate the offered parameters: |
|  | 7. System weight: no more than 30 kg. |  | Please indicate the offered parameters: |
| 9. Ironing board with a steam generator - 1 pcs. | Model, manufacturer, country of origin | - | Please indicate for the offered Goods: Model:____________________ Manufacturer:______________ Country of origin:____________ |
|  | 1. Type: ironing system, consisting of an ironing board with a steam blowing and suction function, a steam generator, an iron, an ironing arm |  | Please indicate the offered parameters: |
|  | 2. Voltage: 220-230V |  | Please indicate the offered parameters: |
|  | 3. Volume of steam generator (steam boiler): no more than 2,5 litre |  | Please indicate the offered parameters: |
| II. General Requirements: |
| 1. Operation and maintenance manual, technical passport, warranty booklet: in Russian (to be supplied with goods) |  | Please enumerate the documents as part of a package deal and their language: |
| 2. Year of manufacture: brand new, not being used or repaired, refurbished or rehabilitated |  | Please indicate year of manufacture and confirm that the equipment is brand new: |
| 3. Delivery: delivery of all necessary equipment and components is carried out by the Contractor on the following terms: - sewing machines (as per items 4, 5 of Technical Specification) - DAP Molodechno, Minsk region, Republic of Belarus (INCOTERMS 2010), or Delivery Terms (Delivery to the Purchaser’s warehouse): Delivery by the Contractor’s transport and at the Contractor’s cost to Budavnikov str. (Stroitelej), 1; 222307 Molodechno, Minsk region (for the delivery from the territory of the Republic of Belarus); - sewing machines (as per items 6, 7 of the Technical specification), ironing system (as per item 8 of the Technical Specification) - DAP Orsha, Vitebsk region, Republic of Belarus (INCOTERMS 2010), or Delivery Terms (Delivery to the Purchaser’s warehouse): Delivery by the Contractor’s transport and at the Contractor’s cost to Zarechnaya str. 4; 211011 Baran’, Vitebsk region (for the delivery from the territory of the Republic of Belarus); - sewing machines (as per items п. 1-3 of Technical Specification), ironing board with a steam generator (as per item 9 of Technical Specification) - DAP Orsha, Vitebsk region, Republic of Belarus (INCOTERMS 2010), or Delivery Terms (Delivery to the Purchaser’s warehouse): Delivery by the Contractor’s transport and at the Contractor’s cost to Vitebsk region, Orsha district, v. Dachnaya, Parkovaya str. 6б (for the delivery from the territory of the Republic of Belarus). The supplied equipment will be checked at the place of delivery by the Customer's specialists and technical specialists of the end user for compliance with the declared quality and technical specification. |  | Please сonfirm the terms of delivery: |
| 4. Warranty: - Warranty for equipment for a period of at least 12 (twelve) months from the date of acceptance of the goods by UNDP in an authorized service center certified by the manufacturer; - After acceptance of the goods by UNDP, the right to use the warranty obligations for the goods passes from UNDP to the End User of the goods: - sewing machines as per items 4, 5 of Technical Specification - Individual entrepreneur Sadovskaya S.S., - sewing machines as per items 6, 7 of the Technical specification, ironing system as per item 8 of the Technical Specification - Unitary enterprise "Baran'skie Arabeski”, - sewing machines (as per items п. 1-3 of Technical Specification), ironing board with a steam generator (as per item 9 of Technical Specification) – LLC “СЕА” |  | Please confirm the terms and indicate the warranty period: |
| 5. Warranty Service Requirements: - availability of a service center on the territory of the Republic of Belarus authorized and certified by the manufacturer; - the Contractor shall ensure warranty repairs, restoration of normal functioning of the Goods and replacement of faulty parts of the supplied Goods at the request of the Purchaser or the End-user within 30 calendar days upon receipt of such request. The Contractor guarantees that during the warranty period transportation of the Goods and parts and units of the Goods from the place of the Goods operation to the service center of the Contractor / authorized local representative of the Contractor and back to the place of operation in order to perform warranty repairs and servicing, if required, shall be done at the Contractor’s cost |  | Please indicate the name and address of the service center that provides warranty service of the sewing equipment: Please indicate the period of restoration of goods operation or its replacement: |

Signature:

Name: 	Click or tap here to enter text.

Title:	Click or tap here to enter text.

# Date:  	Click or tap to enter a date.

ANNEX 2: QUOTATION SUBMISSION FORM

Bidders are requested to complete this form, including the Company Profile and Bidder’s Declaration, sign it and return it as part of their quotation along with Annex 1, 3: Technical and Financial Offer. The Bidder shall fill in this form in accordance with the instructions indicated. No alterations to its format shall be permitted and no substitutions shall be accepted.

| Name of Bidder: | Click or tap here to enter text. |
| --- | --- |
| RFQ reference: | UNDP/LED/349/2021 | Date: Click or tap to enter a date. |

Company Profile

| Item Description | Detail |
| --- | --- |
| Legal name of bidder or Lead entity for JVs | Click or tap here to enter text. |
| Legal Address, City, Country | Click or tap here to enter text. |
| Website | Click or tap here to enter text. |
| Year of Registration | Click or tap here to enter text. |
| Legal structure | Choose an item. |
| Are you a UNGM registered vendor? | ☐ Yes ☐ No If yes, insert UNGM Vendor Number |
| Quality Assurance Certification (e.g. ISO 9000 or Equivalent) (If yes, provide a Copy of the valid Certificate) | ☐ Yes ☐ No |
| Does your Company hold any accreditation such as ISO 14001 or ISO 14064 or equivalent related to the environment? (If yes, provide a Copy of the valid Certificate) | ☐ Yes ☐ No |
| Does your Company have a written Statement of its Environmental Policy? (If yes, provide a Copy) | ☐ Yes ☐ No |
| Does your organization demonstrate significant commitment to sustainability through some other means, for example internal company policy documents on women empowerment, renewable energies or membership of trade institutions promoting such issues (If yes, provide a Copy) | ☐ Yes ☐ No |
| Is your company a member of the UN Global Compact | ☐ Yes ☐ No |
| Bank Information | Bank Name: Click or tap here to enter text. Bank Address: Click or tap here to enter text. IBAN: Click or tap here to enter text. SWIFT/BIC: Click or tap here to enter text. Account Currency: Click or tap here to enter text. Bank Account Number: Click or tap here to enter text. |
| Previous relevant experience: at least three contracts performed for supply of analogous equipment within last 3 years |
| Name of previous contracts | Client & Reference Contact Details including e-mail | Contract Value | Period of activity (dates of equipment supply) | Types of activities undertaken |

| List and value of ongoing Projects with UNDP and other national/multi-national organization with contact details of clients and current completion ratio of each ongoing project (if any) |
| --- |
| Name of current contracts with UNDP and other national/multi-national organization | Client & Reference Contact Details including e-mail | Contract Value (indicate currency) | Period of activity from/to (month/year) | Current completion rate of each project, % |

Bidder’s Declaration

| Yes | No |  |
| --- | --- | --- |
| ☐ | ☐ | Requirements and Terms and Conditions: I/We have read and fully understand the RFQ, including the RFQ Information and Data, Schedule of Requirements, the General Conditions of Contract, and any Special Conditions of Contract. I/we confirm that the Bidder agrees to be bound by them. |
| ☐ | ☐ | I/We confirm that the Bidder has the necessary capacity, capability, and necessary licenses to fully meet or exceed the Requirements and will be available to deliver throughout the relevant Contract period. |
| ☐ | ☐ | Ethics: In submitting this Quote I/we warrant that the bidder: has not entered into any improper, illegal, collusive or anti-competitive arrangements with any Competitor; has not directly or indirectly approached any representative of the Buyer (other than the Point of Contact) to lobby or solicit information in relation to the RFQ ;has not attempted to influence, or provide any form of personal inducement, reward or benefit to any representative of the Buyer. |
| ☐ | ☐ | I/We confirm to undertake not to engage in proscribed practices, , or any other unethical practice, with the UN or any other party, and to conduct business in a manner that averts any financial, operational, reputational or other undue risk to the UN and we have read the United Nations Supplier Code of Conduct :https://www.un.org/Depts/ptd/about-us/un-supplier-code-conduct and acknowledge that it provides the minimum standards expected of suppliers to the UN. |
| ☐ | ☐ | Conflict of interest: I/We warrant that the bidder has no actual, potential, or perceived Conflict of Interest in submitting this Quote or entering a Contract to deliver the Requirements. Where a Conflict of Interest arises during the RFQ process the bidder will report it immediately to the Procuring Organisation’s Point of Contact. |
| ☐ | ☐ | Prohibitions, Sanctions: l/We hereby declare that our firm, its affiliates or subsidiaries or employees, including any JV/Consortium members or subcontractors or suppliers for any part of the contract is not under procurement prohibition by the United Nations, including but not limited to prohibitions derived from the Compendium of United Nations Security Council Sanctions Lists and have not been suspended, debarred, sanctioned or otherwise identified as ineligible by any UN Organization or the World Bank Group or any other international Organization. |
| ☐ | ☐ | Bankruptcy: l/We have not declared bankruptcy, are not involved in bankruptcy or receivership proceedings, and there is no judgment or pending legal action against them that could impair their operations in the foreseeable future. |
| ☐ | ☐ | Offer Validity Period: I/We confirm that this Quote, including the price, remains open for acceptance for the Offer Validity. |
| ☐ | ☐ | I/We understand and recognize that you are not bound to accept any Quotation you receive, and we certify that the goods offered in our Quotation are new and unused. |
| ☐ | ☐ | By signing this declaration, the signatory below represents, warrants and agrees that he/she has been authorised by the Organization/s to make this declaration on its/their behalf. |

Signature:

Name: 	Click or tap here to enter text.

Title:	Click or tap here to enter text.

Date:  	Click or tap to enter a date.

## ANNEX 3: TECHNICAL AND FINANCIAL OFFER - GOODS

Bidders are requested to complete this form, sign it and return it as part of their bid along with Annex 2: Quotation Submission Form. The Bidder shall fill in this form in accordance with the instructions indicated. No alterations to its format shall be permitted and no substitutions shall be accepted.

| Name of Bidder: | Click or tap here to enter text. |
| --- | --- |
| RFQ reference: | UNDP/LED/349/2021 | Date: Click or tap to enter a date. |

Lot 1 - multi-needle embroidery machines with accessories (2 machines with accessories)

| Currency of the Quotation: (indicate currency) INCOTERMS: Delivery by the Contractor’s transport and at the Contractor’s cost to the destinations listed in Annex 1 |
| --- |
| Item No | Description | UOM | Qty | Unit price | Total price without VAT |
| 1.1 | Embroidery machine (as per Technical Specification of Annex 1: Schedule of requirements – lot 1, item 1) Model:__________ | Pcs. | 1 |  |  |
| 1.2 | Software (as per Technical Specification of Annex 1: Schedule of requirements – lot 1, item 1) | Pcs. | 1 |  |  |
| 2. | Embroidery machine (as per Technical Specification of Annex 1: Schedule of requirements – lot 1, item 2) Model:__________ | Pcs. | 1 |  |  |
| Transportation / delivery cost |  |  |
| VAT* |  |
| Total Final and All-inclusive Price (with VAT)* |  |
| Delivery lead time (days) |  |

* The price quotations of the Offerors, non-residents of the Republic of Belarus shall not include VAT. In the price quotations of the Offerors, residents of the Republic of Belarus, VAT, if included, shall be clearly indicated in the price quotation. The price quotations of the Offerors will be compared without VAT.

Note:

1.		Transportation and delivery on to the destinations listed in Annex 1

2. Total Final and All-Inclusive Price Quotation must include supply and delivery of equipment on DAP terms (Incoterms 2010), warranty and all other charges as appropriate.

We hereby declare and confirm that the Goods offered hereinabove are brand new, not used (operated), shall not be a sample or experimental batch, and shall not be assembled from the restored or rehabilitated parts, units or items.

Signature:

Name: 	Click or tap here to enter text.

Title:	Click or tap here to enter text.

Date:  	Click or tap to enter a date.

Lot 2 – Sewing machines with accessories (7 machines with accessories), ironing systems (2 systems)

| Currency of the Quotation: (indicate currency) INCOTERMS: Delivery by the Contractor’s transport and at the Contractor’s cost to the destinations listed in Annex 1 |
| --- |
| Item No | Description | UOM | Qty | Unit price | Total price without VAT |
| 1. | Sewing machine for quilting (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 1) Model:__________ | Pcs. | 1 |  |  |
| 2. | Sewing machine (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 2) Model:__________ | Pcs. | 1 |  |  |
| 3.1. | Сoverstitch sewing machine (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 3) Model:__________ | Pcs. | 1 |  |  |
| 3.2. | Table for the installation of the proposed machine model (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 3) Model:__________ | Pcs. | 1 |  |  |
| 4.1. | Embroidery machine (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 4) Model:__________ | Pcs. | 1 |  |  |
| 4.2. | Table for the installation of the proposed machine model (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 4) Model:__________ | Pcs. | 1 |  |  |
| 4.3. | Software (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 4) | Pcs. | 1 |  |  |
| 5.1. | Sewing machine (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 5) Model:__________ | Pcs. | 1 |  |  |
| 5.2. | Table for installation of the proposed machine model (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 5) Model:__________ | Pcs. | 1 |  |  |
| 6. | Sewing machine (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 6) Model:__________ | Pcs. | 1 |  |  |
| 7.1. | Overlock machine (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 7) Model:__________ | Pcs. | 1 |  |  |
| 7.2. | Recessed overlock table (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 7) Model:__________ | Pcs. | 1 |  |  |
| 7.3 | Servomotor (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 7) Model:__________ | Pcs. | 1 |  |  |
| 8. | Ironing system (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 8) Model:__________ | Pcs. | 1 |  |  |
| 9. | Ironing board with a steam generator (as per Technical Specification of Annex 1: Schedule of requirements – lot 2, item 9) Model:__________ | Pcs. | 1 |  |  |
| Transportation / delivery cost |  |  |
| VAT* |  |
| Total Final and All-inclusive Price (with VAT)* |  |
| Delivery lead time (days) |  |

* The price quotations of the Offerors, non-residents of the Republic of Belarus shall not include VAT. In the price quotations of the Offerors, residents of the Republic of Belarus, VAT, if included, shall be clearly indicated in the price quotation. The price quotations of the Offerors will be compared without VAT.

Note:

1.		Transportation and delivery on to the destinations listed in Annex 1

2. Total Final and All-Inclusive Price Quotation must include supply and delivery of equipment on DAP terms (Incoterms 2010), warranty and all other charges as appropriate.

We hereby declare and confirm that the Goods offered hereinabove are brand new, not used (operated), shall not be a sample or experimental batch, and shall not be assembled from the restored or rehabilitated parts, units or items.

Signature:

Name: 	Click or tap here to enter text.

Title:	Click or tap here to enter text.

Date:  	Click or tap to enter a date.

Compliance with Requirements

|  | You Responses |
| --- | --- |
|  | Yes, we will comply | No, we cannot comply | If you cannot comply, pls. indicate counter - offer |
| Compliance with Minimum Technical Specifications listed in Annex 1 | ☐ | ☐ | Click or tap here to enter text. |
| Delivery Term (INCOTERMS) DAP or Delivery to the Purchaser’s warehouse for the delivery from the territory of the Republic of Belarus (delivery destinations are listed in the Annex 1) | ☐ | ☐ | Click or tap here to enter text. |
| Delivery Lead Time During maximum 120 calendar days from the date of the Contract signing | ☐ | ☐ | Click or tap here to enter text. |
| Warranty and After-Sales Requirements Requirements listed in Annex 1: Schedule of Requirements of this RFQ. | ☐ | ☐ | Click or tap here to enter text. |
| Validity of Quotation Quotation remains valid for 90 (ninety) calendar days from the deadline for the submission of Quotation. | ☐ | ☐ | Click or tap here to enter text. |
| Payment terms 100% during 30 calendar days after the acceptance of the equipment by UNDP | ☐ | ☐ | Click or tap here to enter text. |
| Supply of equipment in a complete set announced by the manufacturer, in accordance with Technical specification | ☐ | ☐ | Click or tap here to enter text. |
| Full acceptance of the General Conditions of Contract | ☐ | ☐ | Click or tap here to enter text. |
| Availability of completed proposal documents, listed in 'Documents to be submitted’ of the SECTION 2: RFQ INSTRUCTIONS AND DATA | ☐ | ☐ | Click or tap here to enter text. |

Other Information:

| Estimated weight/volume/dimension of the Consignment: | Click or tap here to enter text. |
| --- | --- |
| Country/ies of Origin: (if export licence required this must be submitted if awarded the contract) | Click or tap here to enter text. |
| I, the undersigned, certify that I am duly authorized to sign this quotation and bind the company below in event that the quotation is accepted. |
| Exact name and address of company Company NameClick or tap here to enter text. Address: Click or tap here to enter text. Click or tap here to enter text. Phone No.: Click or tap here to enter text. Email Address: Click or tap here to enter text. | Authorized Signature: Date: Click or tap here to enter text. Name: Click or tap here to enter text. Functional Title of Authorised Signatory: Click or tap here to enter text. Email Address: Click or tap here to enter text. |