Addendum dated 01-Dec-2021

- Irrigation sites and borehole location: The google coordinates have been added for all the boreholes, see annex BH A.

- Borehole reports: information on the borehole reports has been added see annex BH A

- Drip irrigation pipes: the polyethylene pipes for the drip irrigation lateral pipe and emitter should meet the ISO 9001, ISO 9261 or any related international standard.

- Perimeter fencing: For the fencing of the perimeter areas for the irrigation sites, the Y standard poles shall be spaced at 5m apart and NOT 10m as originally stated, the perimeter for Gwembe and Luangwa sites is 1600m, Chongwe, Namwala and Rufunsa = 1200m

- Correction of typo error on the Chirundu tank stand: the support structure shall be 70mm X 70mm X 8mm RSA Vertical as indicated in the design and NOT 70mm x 70mm x 6m

- Tank stand footing: the foundation pads shall be 1500mm x 1500mm and NOT 1000mm x 1000mm.

- Page 21 on evaluation criteria; The modification of the text on membership to an engineering society, and it shall now read as “member of Engineering Institute of Zambia (EIZ) Certificate or alternative appropriate international Engineering Regulatory Body “ AND NOT member of engineering institute of Zambia ONLY

- On section 12 of the ITB under heading Equipment; Delete wedge HDPE machine and replaced with welding machine, similarly spark test machine deleted and replaced with Crane

- On section 11 in the ITB under key personnel; the requirement for Aqua culture expert is deleted.

- Correction of typo error in the detailed bill of quantities for infield drip network, the minimum wall thickness of the PE drip lateral shall be 0.5mm and NOT 0.5m

- The ITB didn’t include a sample pricing template ANNEX F, therefore pricing shall be made on the bill of quantities

- Section 4 on evaluation criteria; the text shall now read proof of tax compliance and not latest Zambia Revenue authority certificate.